From:	Sullivan, John F - DNR

Sent:	Friday, April 15, 2011 1:30 PM

To:	Larson, Aaron M - DNR

Cc:	Masnado, Robert G - DNR; Jerow, Thomas S - DNR; Baumann, Dan G - DNR

Subject:	2012 Impaired Waters Listing Recommendation for the Mississippi River

Attachments:	2012 Impaired Waters Doc Sheet UMR Reach 1.doc; 2012 Impaired Waters Doc Sheet UMR Reach 2 to 4.doc; UMR 303d Nutrient Impairment 2011 jfs.doc; Algae metaphyton examples UMR.pdf; Duckweed examples UMR.pdf; Median TP Analysis 2011 Assessment jfs.xls

Aaron,

I am recommending that nutrient-related impairments for four reaches of the Mississippi River be added to the 2012 Impaired Waters List.  The first reach is UMRBA Assessment Reach 1 (St. Croix River to Chippewa River), which includes Lake Pepin. The other three reaches are for UMRBA Assessment Reaches 2 to 4 (Chippewa River to Wisconsin River).  You will see that Reach 1 has both recreational use and fish and aquatic life (FAL) use impairments.  Reaches 2 to 4 are centered on General use impairments (NR 102.04) due to nutrient-related impacts (excessive filamentous algae and duckweeds), which contribute to hypoxic conditions in backwater areas. Specific fish or macroinvetebrate biological criteria for determining use support have not been established for backwaters or impounded areas of the Mississippi River.  Fish and Macroinvetebrate biotic indices developed for the main channel (Lyons IBI and EMAP-GRE) do not suggest the main channel in Assessment Reaches 2 to 4 are below thresholds suggestive of biological impairment.  However, in order to protect backwaters and impounded areas on the river, the main channel nutrient levels will need to be reduced. The is analogous to protecting "downstream waters," but in this case, the waters are adjacent to the main and side channels of the Mississippi River.

Here are the Impaired Waters Documentation Sheets.

.

Here is additional documentation for the impaired waters listing recommendation.

Here is the assessment of median total phosphorus concentrations in the Mississippi River. It includes some tributary data.  Most of the information was obtained from agencies outside the DNR and the data do not reside in our SWIMS database.

If you have questions or need additional information, please let me know. Also, I would be happy to travel to Madison to discuss these documents should you find that would be desirable.

John

John F. Sullivan

Wisconsin Department of Natural Resources

Mississippi River Water Quality Specialist

3550 Mormon Coulee Road

La Crosse, WI 54601

John.Sullivan@dnr.state.wi.us

608-785-9995

fax: 785-9990

"Plain question and plain answer make the shortest road out of most perplexities"   M. Twain