Water Quality Monitoring

Special Project Workplan Proposal - FY 2007

GENERAL INFORMATION

Author Name:	Craig Helker			Telephone: 262-884-2357

Region: SER					Program: WT

Basin: Rock River

PROJECT INFORMATION

Project Category: Category 1			Activity Code:	 WTSK

Project Location(s): 	Bark River – River mile 35 - 41

Watershed: Bark River

County: Waukesha

WORKPLAN DETAILS

1. Project Description (including what, when, where, who of project):

The project portion of the Bark River includes that portion of the river listed on the

303(d) list for low dissolved oxygen due to excessive Phosphorus.  The monitoring

described below, developed in consultation with Department Staff, will assist in

developing a TMDL for this portion of the Bark River.

A surface water grab sample will be collected once monthly by WT Staff (July, August, September) at three locations (Hwy 18 and Utica Road, Hwy 67, and Genesee Lake Road) and analyzed for the following:

- Total P

- Total Dissolved Phosphorus (as P)

- Nitrogen Series

- Suspended Solids

- Chlorophyll a

- 120-Day Ultimate BOD

A flow-proportional 24-hour composite sample will be collected once monthly by the Staff at each contributing Wastewater Treatment Plant, and analyzed for the following:

- Total P

- Total Dissolved Phosphorus (as P)

- Nitrogen Series

- Suspended Solids

- 120-Day Ultimate BOD

In addition, a Hydrolab will be deployed at and connected to the USGS gaging station at Hwy 18 and Utica Road, and will take continuous DO, temperature, pH, and Chl. A. readings. At the Hwy 67 and Genesee Lake Road sites,  two hydrolabs will be deployed on a monthly basis for 4-7 days, to record diel DO, temperature, and pH.   In addition, 10 locations (TBD) between the Hwy 83 and Utica Road site and the upstream Genesee Lake Road site will be sampled for instantaneous DO concurrently with diel monitoring deployments.  Stream flow will be recorded at each site during surface water grab sampling events.

Finally, macroinvertebrate samples will be collected from each sample site in October.

2. Justification (why is this project necessary?):

SER has been directed to develop 5 TMDLs annually.  Conducting the monitoring 	described will allow for TMDL development for this 303(d) listed segment of the 	Bark River.

3. Performance Measure(s) (including sample collection, report completion date, etc.):

Monthly collection, deployment, and downloading of continuous DO recording 		data sondes in July, August, and September.

Monthly sampling in July, August, and September

Collection and mailings of samples

Development of TMDL by June 30, 2007

4. Data Storage System (work station computer, lab portal, SWIMS, FH database, etc.):

Work Station Computer

SWIMS

5. File Manager Responsible for Data Entry:

Fox/Illinois Biologist

| Water Quality Special Project Workplan Proposal |  |
| --- | --- |
| Cost Worksheet |
| FY 2007 |  |  |
| July 1, 2006 - June 30, 2007 |  |  |
|  | Hours | Cost ($) |
| FTE Resources | 120 |  |
| LTE Resources | 160 | $2240 + fringe |
| Line S (supplies, contracts, travel) |  | $50 meals $600 travel $345 macroinverts $150 sample shipping |
| SLOH Lab Services (attach lab spreadsheet) |  | $4680.27 |
| Equipment <$5,000 |  | Two Hydrolab 5’s ($4700 x 2 = $9400) |
| Capital Equipment =>$5,000 |  |  |
| Subtotal DNR contributions |  | $17465.27 + LTE Fringe |
| Partner Contributions |  |  |
| Total Contributions |  | $17465.27 + LTE Fringe |