| 2008 Impaired Waters Documentation Sheet | Date Prepared __7/25/2007____________________________________________ |
| --- | --- |
| Author Erin Hanson_________________________________________________ |
| Waterbody Name Dutchman Creek – Segment 1_________________________________________ | Watershed __Apple and Ashwaubenon Creeks_ |
| WADRS ID | __10832___________ | WBIC _____121600______________ | Lower Fox |
| Choose One: |
| _______ | Proposed 303d List Change (new water, delisting, new pollutants) |
| X _______ | General 303d Documentation |
| TMDL/303D Listing Proposal |
| 0________ | Start Mile | 7________ | End Mile | _7______ | Size (Miles/Acres) |
| Current Assessment: |
| _________ | Current Fish & Aquatic Life (Aquatic Community) Use ___________________________________________________________________ |
| _________ | Attainable Fish & Aquatic Life (Aquatic Community) Use_________________________________________________________________ |
| _________ | Designated Fish & Aquatic Life Use__________________________________________________________________________________ |
| _________ | Supporting Attainable Use = fully, partially, not meeting ________________________________________________________________ |
| _________ | Does a Specific Fish Advisory Exist? (Yes/No) |
|  | ________ | If so, what is the advice? |
| Pollutants & Impairments |
| X________ | Impairments (Circle One or More) |
|  | Degraded habitat | Acute Toxicity | Chronic Toxicity | Temperature (Water) |
|  | Contaminated Fish Tissue | Eutrophication | Excessive Aquatic Plant Growth |
|  | Aquatic Invasives (AIS) Infestation |  | Dissolved Oxygen, Low |
|  | Other ______________________________________________________________________ |
| X________ | Pollutants (Circle One or More) |  |
|  | Total Phosphorus | Sediment | PCBs | PAHs | Creosote |
|  | NH3 (Ammonia) | Runoff Water (elevated temperatures) | Other _____________________________ |
|  | Other ______________________________________________________________________ |
| X________ | Assessment Level (monitored site specific data less than 5 years old) versus evaluated (other) data > 5 years old |
| ________ | DNR Category (3, 4d (recommended), 5a, 5b, 5c) |
| Monitoring and Listing |
| X________ | Water Quality Exceedances (As applicable) Station 053634: Dissolved Oxygen 4.5 mg/L 06/19/1997 Station 053516: insufficient samples to determine exceedance of fecal coliform standard; 50% samples exceed 400 cfu/100ml listed in second table below (1992, 1997 & 1999) |
| X________ | Assessment Parameters (M-IBI, FISH IBI, HBI) Macroinvertebrate HBI max 10 range between 6.2 and 7.9 (1997, 1998, 2000), data in SWIMS Fish Warmwater IBI Integrity Rating = “Very Poor” at SWIMS Stations 10007894 & 10007895 (14/8/00), data in Fisheries database |
| Stations/Dates/Metric/Scores ____________________________________________________________________________________ |
| Stations/Dates/Metric/Scores ____________________________________________________________________________________ |
| Attach any additional reports, analyses, etc. (Use Designation Survey, etc.) |
| Data From SWIMS Majority of water quality data is for Station ID 053516, DUTCHMAN CREEK - COUNTY HIGHWAY H-BROADWAY STREET, 1992 & 1997-1999 Some water quality samples for Station ID 053634, DUTCHMAN CREEK - AT GROSS STREET, 4/21/1997 through 12/16/1997 Parameter Station ID Average Min Max n DISSOLVED OXYGEN FIELD, mg/l 053516 8.9 5.65 14.9 15 053634 9.6 4.5 14.7 9 TEMPERATURE FIELD, deg C 053516 11.9 0.09 24.1 16 053634 10.5 0.38 19.6 9 FECAL COLIFORM, MEMBRANE FILTER, MFC AGAR, #/100ml 053516 2114 0 6100 14 053634 25 10 40 2 NITROGEN KJELDAHL TOTAL, mg/l 053516 0.733 0.6 0.8 3 NITROGEN NH3-N DISS, mg/l 053516 0.098 0 0.509 12 053634 0.058 0 0.236 9 NITROGEN NO3+NO2 DISS (AS N), mg/l 053516 0.568 0.404 0.666 3 PHOSPHATE ORTHO DISS, mg/l 053516 0.100 0.002 0.3 15 053634 0.038 0 0.098 9 PHOSPHORUS TOTAL , mg/l 053516 0.225 0 0.65 16 053634 0.077 0 0.162 9 RESIDUE TOTAL NFLT (TOTAL SUSPENDED SOLIDS), mg/l 053516 43.333 0 180 15 053634 13.611 0 56 9 FECAL COLIFORM, MEMBRANE FILTER, MFC AGAR, Results > 400 cfu/100ml Station ID Date Result Result Units 053516 13/07/1992 5000 #/100 ml 053516 15/09/1992 2400 #/100 ml 053516 23/07/1997 4,500 #/100 ml 053516 29/09/1997 6100 #/100 ml 053516 02/06/1999 3,500 #/100 ml 053516 23/06/1999 1800 #/100 ml 053516 06/07/1999 5,700 #/100 ml Macroinvertebrate Data: Station ID 053634, DUTCHMAN CREEK - AT GROSS STREET, 5/22/97, 10/20/97 & 9/11/2000 Station ID 10015851, DUTCHMAN CREEK - ONEIDA STREET, 12/10/1998 Station ID 10007894, DUTCHMAN CREEK - WAUBE LN DOWNSTREAM, 9/11/2000 Parameter Station ID Count Average Min Max HBI Max 10 053634 3 7.277 6.571 7.857 10015851 1 6.188 6.188 6.188 10007894 1 7.349 7.349 7.349 INDEX OF BIOTIC INTEGRITY (IBI) 053634 3 2.523 1.859 3.826 10015851 1 4.567 4.567 4.567 10007894 1 2.793 2.793 2.793 Data from USGS Two USGS stations have data for Dutchman’s Creek – Segment 1: USGS 040850745 DUTCHMAN CREEK AT PIONEER ROAD AT ASHWAUBENON, WI has no equivalent DNR sample station & no nutrient results in the USGS database. It is not clear where the USGS 04085080 DUTCHMAN CREEK NEAR DEPERE, WI sample station is located; however the only results for this station are for 1960 and are not summarized here. Data Summary provided by James Reyburn, WDNR Water Quality Biologist – Lower Fox Basin: Suspended Solids Concentrations – event and non-event Average Total Phosphorous Concentrations - event and non-event Lower Fox River Tributary Daily total Phosphorous Loads & Daily total Suspended Solids Loads – NOTE: Dutchman’s Creek has the largest daily total suspended solid load (final graph) |