303(d) Listing Documentation

Waterbody Name: Yaeger Valley Creek

Waterbody ID Code (WBIC): 1810200

County(ies): Buffalo

Impaired Stream Reach (location and mileage): Entire stream from its confluence with Waumandee Creek at STH 88, upstream four miles crossing Yeager Road. (4 miles).

Type of impairment (water quality standards violations [ex. pH, DO, etc.], not meeting codified use [ex. WWFF should be Cold II], eutrophication, etc.):

Existing use is WWFF, codified use is WWSF (default). Potential use is Cold III.

Cause of impairment (ex. temperature, nutrients, sediment, BOD, toxics, etc.):

Habitat, sedimentation

Source of impairment (ex. point source, nonpoint source, internal load, unknown, etc.):

Streambank erosion, hydrological modifications (dam)  No dams were found on the stream using the WT Viewer.  Need to verify if a dam actually exists.

Description of monitoring conducted (including dates, results, quality of data and reports):

1998 Stream Survey Report (water temperature =12 degrees C.), clear water, and common aquatic life. Stations 1 and 2 had 15 brook trout ranging from 5-7 inches.

Fish Management surveyed the stream at two locations in 2002 and 2006.  The survey near the mouth at STH 88 (SWIMs ID 10009481) found nine trout in 2002 ranging in size from 1.5 to 8 inches.  No other species were reported in the database.  In 2006, only three fish were collected including a 3.5 inch brook trout.

A survey completed approximately one mile upstream from STH 88 (SWIMs ID = 10009482) in 2002 found 76 brook trout represented by multiple year classes including young of year. The survey completed in 2006 found 99 trout, mostly young of the year.  The largest trout measured was 4.5 inches.

A habitat survey completed in 2002 indicates the mean width of the stream is two meters.  The same data appears to be entered for both sites in the database; therefore it cannot be determined which site the habitat survey represents.

The watershed should be evaluated to determine if impacts to the stream are controlled and if the stream is meeting its designated use.

1996 Buffalo-Trempealeau Basin Plan

2002 Black- Buffalo-Trempealeau Basin Report

Location of supporting data (electronic and hard copy files): WDNR Black River Falls  Fish and habitat data can be found electronically in FH database and hard copy data is located in FH files in Black River Falls.

Reviewer’s Name: Chris Flicek; Revised by Mark Hazuga

Date Reviewed: 3-4-02, Revised 12/18/03 by Ken Schreiber; Revised 1/31/2008