| 2008 Impaired Waters Documentation Sheet |
| --- |
| Author: Erin Hanson | Date Prepared: 1/15/2008 |
| Waterbody Name: Lower Fox River Seg. 2 | Watershed Code and Name: LF01, LF02, LF03, LF04 |
| WADRS ID: 357301 | WBIC: 117900 | If you don’t know the ID numbers, go to i-SWDV (CRTL + Click) to find them. |
| Choose from the following to indicate what you are recommending: |
| _____ Proposed new listing |
| _____ Proposed for special project monitoring (need more data) |
| _____ Proposed changes for water already on 303(d) list (check type of change below) ( TMDL ID Number: _______ |
|  | _____ Proposed change to existing list (new pollutants, impairments, mileages, etc.) |
|  | _____ Proposed for de-listing ( a report may be needed depending on the reasons) |
|  | ___X__ General 303d documentation for water already on list |
| Description of waterbody segment |
| Start Mile: _7.39 ___________ End Mile: 32.18 ____________ Total miles: _24.79 ___________ Lake Acres: ____________ | Detail (describe segment using road crossings, convergence with other waterbodies, etc.): De Pere Dam to Middle Appleton Dam |
| Use Designation Categories | List use designation & data source for each category. |
| Current (Existing) Fish & Aquatic Life Use: (Aquatic Community) | WWSF (WATERS) |
| Attainable (Potential) Fish & Aquatic Life Use: (Aquatic Community) | WWSF (WATERS) |
| Designated (Codified) Fish & Aquatic Life Use: | DEFAULT (WATERS) |
| Is it supporting its Attainable Use? _____ Fully supporting _____ Partially supporting _X____ Not supporting Does a Specific Fish Advisory Exist? (This is different from the statewide mercury advisory.) _X__ Yes ____ No ___ Don’t know If so, what is the specific advisory: PCB |
| Pollutants & Impairments Pollutants (Place an X next to all pollutants that you are recommending for listing, de-listing or monitoring needs. If you are recommending adding a new pollutant to a waterbody that is already on the list, write ADD.) |
| ___X__ Phosphorus | _____ Sediment | _____ Bacteria | _____ PAHs | __X___ PCBs |
| _____ NH3 (Ammonia) | _____ Thermal (elevated temp.) | _____ Hg | _____ Creosote | _____ Metals |
| Other Pollutants: Remove Hg as a pollutant in WATERS. This is incorrect as confirmed by Candy Schrank. |
| Impairments (Place an X next to all impairments that you are recommending for listing, delisting, or monitoring needs. If you are recommending adding a new pollutant to a waterbody that is already on the list, write ADD. ) |
| _____ Degraded Habitat | _____ Eutrophication | _____ Temperature |
| __X___ Contaminated Fish Tissue | _____ Chronic Toxicity | _____ Aquatic Toxicity |
| __X__ Low Dissolved Oxygen | _____ Aquatic Invasives |  |
| Other Impairments: |
| Source of impairment (Place an X next to the source category.) if you need an explanation of source categories., see http://dnr.wi.gov/org/water/wm/wqs/303d/categories.html . |
| _____ NPS Dominated | _X____ NPS/Pt. Source Blend | _____ Point Source |
| _X____ Contaminated Sediment | _____ Atmospheric Deposition | _____ Physical Habitat |
| _____ Unknown | Other: _____________________________ |
| Specific causes of impairment (Describe to the best of your ability what you think is contributing to the impairment.) NOTE: “WATERS incorrectly lists Hg as a pollutant for FCA and this is not correct. It does not appear on the 303(d) list for Hg. Since it did not appear on the 2006 list, this is a DNR internal correction only.” Email from Carolyn Betz, 1/13/2008 |
| Information is based on: ____ Monitoring data (specific data) less than 5 years old ____ Evaluated data (data more than 5 years old) |
| Map |
| Monitoring & Listing Data 1. Monitoring Study, Date, Results. List water quality exceedences indicating magnitude, duration and frequency. Stations: for specific station descriptions see additional comments below. Parameters: Dissolved Oxygen < 5 mg/l: Station 453059: 4.0 mg/l on 8/31/1976 Station 453064: 4.5 mg/l on 8/31/1976 Station 453068: 0.7 mg/l on 8/31/1976 Station 453226: 7 readings 7/16/1981 through 9/1/1996, above data in SWIMS USGS Station 4085000: 4.8 mg/l on 1/10/1979 Database where data is stored (Fish Database, SWIMS, FishSED, Personal PC): SWIMS & USGS |
| 2. Monitoring Study, Date, Results. List water quality exceedences indicating magnitude, duration and frequency. Stations: SWIMS ID 10009536, FOX RIVER LCR#4GET (05/02/1980 – 10/17/1980) Parameters: Assessment Parameters (M-IBI, FISH IBI, HBI) HBI max 10, Station 10009536, “FOX RIVER LCR#4GET” = 7.91 (5/2/1980 & 10/17/1980), “poor” water quality & “very significant” degree of organic pollution (Lillie et al, 2003), data in SWIMS No Warmwater IBI or habitat rating in fisheries database Database where data is stored (Fish Database, SWIMS, FishSED, Personal PC): SWIMS |
| 3. Monitoring Study, Date, Results. List water quality exceedences indicating magnitude, duration and frequency. Stations: Station 10009536, “FOX RIVER LCR#4GET”, 5/2/1980 & 10/17/1980 Station 053692, FOX RIVER - AT STH 32 IN DE PERE, 10/12/1998 Parameters: Macroinvertebrate Data from SWIMS: Parameter Station ID Average Min Max Count HBI Max 10 10009536 7.910 7.526 8.293 2 INDEX OF BIOTIC INTEGRITY (IBI) 053692 3.356 3.35612 3.35612 2 10009536 2.198 1.86477 2.53202 2 SHANNON'S DIVERSITY INDEX 053692 1.781 1.781 1.781 2 SPECIES RICHNESS 053692 16 16 16 2 Database where data is stored (Fish Database, SWIMS, FishSED, Personal PC): SWIMS |
| Additional Comments: Data from SWIMS: Note: Stations with recent data identified by bold text. No map of sample stations created. Station ID Station Name Result Dates 053073 FOX RIVER - WRIGHTSTOWN STP 09/26/1977 - 03/23/1981 053451 FOX RIVER - AT STATE HWY 96 05/01/1980 - 08/14/1982 053692 FOX RIVER - AT STH 32 IN DE PERE 10/12/1998 - 10/12/1998 10008282 FOX RIVER (WRIGHTSTOWN - POOL 10) MILE 13.1 TO 19.2 08/21/2001 - 09/26/2006 10008284 FOX RIVER (KAUKAUNA - POOL 7) MILE 24.0 TO 25.4 05/22/2001 - 09/26/2006 10008323 FOX RIVER (KIMBERLY - POOL 4) 08/14/2003 10009536 FOX RIVER LCR#4GET 05/02/1980 - 10/17/1980 10009784 FOX RIVER - FOX RIVER (KAUKAUNA - POOL 9) MILE 19.2 TO 22.8 08/22/2002 - 08/22/2002 10012539 KIMBERLY AT SUNSET BEACH PARK 08/21/2001 - 11/14/2006 453031 FOX RIVER - APPLETON STP 07/21/1976 - 04/02/1985 453032 FOX RIVER - APPLETON STP PRIMARY DISCHRG 002 11/08/1976 - 05/08/1978 453053 FOX RIVER - BELOW LOWER DAM APPLETON 08/31/1976 - 09/25/1979 453055 FOX RIVER - AT BEND BL CONS PAP APPLTN 08/31/1976 453056 FOX RIVER - ABOVE APPLETON STP 08/30/1978 453057 FOX RIVER - BETW APPLTN STP AND BOAT LDG 08/31/1976 453059 FOX RIVER - ABOVE K-C CORP KIMBERLY DAM 07/27/1975 - 08/29/1988 453062 FOX RIVER - AT LITTLE CHUTE SANITORIUM 08/31/1976 453063 FOX RIVER - AT KAUKAUNA BOAT LANDING 08/21/2001 453064 FOX RIVER - ABOVE UPPER KAUKAUNA DAM 07/27/1975 - 08/30/1988 453065 FOX RIVER - ADJ TO THILMANY ABV LAGOON 08/31/1976 - 09/25/1979 453067 FOX RIVER - AT BEND, NEAR BUOY 27 08/31/1976 - 08/30/1978 453068 FOX RIVER - ABOVE RAPIDS CROCHE DAM 07/06/1975 - 08/30/1988 453069 FOX RIVER - BELOW RAPIDS CROCHE DAM 09/24/1979 - 09/25/1979 453071 FOX RIVER - CONSOLIDATED PAPERS APPLETON 001 08/14/1978 - 12/16/1981 453074 FOX RIVER - CONSOLIDATED PAPERS APPLETON 004 05/05/1976 453075 FOX RIVER - CONSOLIDATED PAPERS APPLETON 005 05/05/1976 453077 FOX RIVER - CONSOLIDATED PAPERS APPLETON 007 05/05/1976 453226 FOX RIVER - AT APPLETON 01/20/1977 - 12/17/1996 453236 FOX RIVER, TOXICS STUDY - ABOVE RAPIDS CROCHE DAM 05/20/2003 - 06/17/2003 453239 FOX RIVER - AT STH 55, AT KAUAKAUNA, WI 05/03/1989 - 11/17/1992 453240 FOX RIVER - AT STH 96, AT WRIGHTSTOWN, WI 07/08/2004 453251 FOX RIVER - KIMBERLY MIDDLE SEAWALL 10/05/1992 453269 LOWER FOX RIVER - DEEP HOLE-POOL 5 06/22/2000 - 09/05/2000 453271 FOX RIVER - UPSTREAM SITE, AT KIMBERLY, WI 10/22/1998 - 12/20/2000 453272 FOX RIVER - DOWNSTREAM SITE, AT KIMBERLY, WI 10/22/1998 - 12/20/2000 453278 FOX RIVER - AT RAPIDS CROCHE DAM, NEAR WRIGHTSTOWN, WI 07/15/2003 - 10/16/2003 Selected water quality parameters: Parameter, units Station ID Average Min Max Count DISSOLVED OXYGEN FIELD, mg/l 10008282 10.8 8.9 14.2 3 10008284 8.5 8.3 8.7 2 10012539 9.7 6 14.5 16 453053 8.9 8.4 9.5 3 453055 7.8 1 453056 9.5 1 453057 7.3 1 453059 18.4 4 92 8 453062 6.0 1 453063 10.3 1 453064 45.9 4.5 200 5 453065 7.9 5.2 9.7 4 453067 7.7 7.3 8 2 453068 71.9 0.7 210 3 453069 8.9 8.8 8.9 2 453226 10.4 0.3 19 188 453269 9.2 1 PHOSPHATE ORTHO DISS, mg/l 053451 0.03 0.004 0.113 30 10008282 0.07 0.062 0.073 3 10008284 0.03 1 10008323 0.05 1 10012539 0.08 0.06 0.1 4 453031 1.31 0.03 4.4 8 453032 0.66 1 453053 0.03 1 453056 0.03 1 453059 0.03 0.016 0.04 4 453063 0.07 1 453064 0.07 0.04 0.116 3 453065 0.03 1 453067 0.14 1 453068 24.70 0.03 74 3 453069 0.05 1 453071 1.26 0.22 3.2 6 453226 0.03 0 0.71 156 453239 0.01 0.003 0.021 24 PHOSPHORUS TOTAL, mg/l 053073 13.60 1 053451 0.17 0.05 0.34 44 10008282 0.30 0.161 0.54 3 10008284 0.11 0.087 0.141 2 10008323 0.18 1 10012539 0.22 0.063 0.963 16 453031 6.24 0.62 16.8 30 453032 11.65 5.3 18 2 453053 0.19 1 453056 0.22 1 453059 0.62 0.21 1.7 4 453063 0.82 1 453064 0.94 0.27 2.2 3 453065 0.29 0.21 0.43 3 453067 0.34 1 453068 0.70 0.24 1.6 3 453069 0.20 1 453071 3.11 0.74 6.55 8 453226 0.11 0 2 153 453236 0.10 0.092 0.109 2 453239 0.11 0.04 0.16 15 453240 0.12 0.12 0.12 2 453269 0.13 0.089 0.184 3 453278 0.18 0.12 0.212 6 RESIDUE TOTAL NFLT (TOTAL SUSPENDED SOLIDS), mg/l 453073 41.5 39 44 2 053073 93.5 49 138 2 053451 58.4 3 408 44 10008282 56.0 29 99 3 10008284 28.0 1 10008323 23.0 1 10012539 34.3 2 159 16 453031 145.8 18 472 13 453032 760.0 1 453053 35.0 1 453056 40.0 1 453059 111.5 33 340 4 453063 72.0 1 453064 150.7 32 380 3 453065 45.0 35 56 3 453067 26.0 1 453068 39.0 39 39 2 453069 30.0 1 453071 384.7 92 1070 6 453074 2.0 1 453075 29.0 1 453077 29.0 1 453226 19.0 0 440 154 453239 25.4 4 45 17 453269 26.0 1 453271 13.3 0 57 392 453272 11.6 0 82 488 Data from USGS: Site ID Site Name Sample Dates 4084475 FOX RIVER AT STATE HIGHWAY 55 AT KAUKAUNA, WI 04/19/1989 - 11/17/1992 4084500 FOX R AT RAPIDE CROCHE DAM NEAR WRIGHTSTOWN, WI 08/25/1977 - 10/16/2003 4085000 FOX RIVER AT WRIGHTSTOWN, WI 06/03/1960 - 08/24/1994 4085054 FOX RIVER AT LITTLE RAPIDS, WI 03/15/1989 - 07/10/1993 Selected water quality parameters for USGS stations listed below: Parameter Site ID Average Min Max Count Dissolved oxygen, water, unfiltered, mg/l 4084475 11.0 6.7 15.6 28 4084500 9.7 8.3 13.5 6 4085000 10.1 4.8 16.1 128 4085054 11.3 8 15.3 28 Suspended sediment concentration, mg/l 4084475 26 0 219 375 4084500 25 16 38 6 4085000 27 1 150 158 4085054 34 2 418 539 Suspended sediment discharge, tons per day 4084475 271 0 4090 371 4084500 258 93 562 6 4085000 319 6 2640 152 4085054 502 14 14000 534 Data from other sources: Scheberle, D., H.J. Harris, M. Finney, J. Potter, S. Oldenburg, P. Dessart. no date. Toward a Total Maximum Daily Load (TMDL) for Phosphorus and Suspended Solids: The Lower Fox River Basin and Green Bay Area of Concern “According to the WDNR 303 (d) list, the water quality of Lower Green Bay and the Fox River is impaired due to phosphorus and PCBs (WDNR, 2005). Phosphorus and TSS are the pollutants of concern for this framework. Even though suspended solids are not listed as a pollutant that impairs designated uses for the lower Fox River and the bay, ample research demonstrates that both TSS and phosphorous affect water quality (Harris, 1993; Millard & Sager, 1994).” p. 18 “Suspended solids loading into the AOC and Green Bay have also been estimated through monitoring (SDATF, 2002) and modeling (Baumgart, 2005). The average monitoring SS load at the mouth of the Fox River for water years 1995-1999 was 119,400 mt/yr-1 (Table 2b). This amounts to 327 metric tons per day in an average year. With the addition of the point sources, the estimated contribution from Lake Winnebago, and the estimated autogenic solids contribution from the river (WDNR, 2001), the simulated 1989-2000 suspended sediment load at the Fox River outlet to Green Bay is 119,000 mt/yr-1 (Baumgart, 2005). p. 31“ Contaminated Sediments: Excerpt from: “Draft Studies Completed on Cleanup of PCBs in Lower Fox River Sediments” WDNR Summary Fact Sheet 3/1999 Available at: http://dnr.wi.gov/org/water/wm/foxriver/documents/rifs/foxrivercleanup.pdf “As many as 360 different chemicals have been found in the water, sediments, fish and wildlife of the Lower Fox River. These chemicals include PCBs, dioxins, furans, mercury, ammonia, DDT and other pesticides (see table on page 6 for more information on these chemicals). The Lower Fox River, which flows northeast for about 39 miles from Lake Winnebago at Neenah-Menasha to the river’s mouth at Green Bay, contributes more PCBs to Green Bay and Lake Michigan than any other source…. An estimated 63,000 pounds of the PCBs previously discharged remain in the Lower Fox River. Most of them are downstream of the De Pere dam. An even larger quantity has passed through the Lower Fox River to Green Bay, Lake Michigan and beyond. Results of the intensive “Mass Balance” study conducted by the DNR and EPA in 1989 showed that about 160,000 pounds of PCBs have already found their way into Green Bay from the Lower Fox. It also showed that about 620 pounds of PCBs enter the bay from the river each year.” p. 2 & Figures below p. 4 & 5 Excerpts from “Remedial Investigation Report Lower Fox River and Green Bay Wisconsin” prepared for WDNR by The RETEC Group, Inc. 12/2002 “The results are summarized below and indicate that the De Pere to Green Bay Reach and Green Bay Zone 2, combined, contain almost 60 percent of the total PCB mass in the system in less than 10 percent of the total contaminated sediment volume. The PCB mass and volume of contaminated sediment for each river reach and bay zone are listed below.” P. 7-5 7.3.2.3 Appleton to Little Rapids Reach Sediment accumulation in the Appleton to Little Rapids Reach is more localized compared with the other three reaches. Deposits I through DD contain about 94 kg (207 pounds) of PCBs in about 184,790 m3 ( 241,700 yd3) of sediment with concentrations greater than 50 μg/kg PCB. RI findings for this reach include the following: Deposits I through DD cover approximately 153 hectares (378 acres) and these deposits generally occur in areas of slower stream flow velocities (e.g., where the river widens, in the vicinity of dams/locks, eddy pools along the banks, etc.). The highest total PCB concentration was 77,444 μg/kg. Only deposits W, X, and DD have a volume exceeding 30,000 m3 (39,240 yd3) of sediment and these are located where the river widens and/or upstream of a dam. The average sediment volume in each of the remaining 19 deposits in this reach is about 3,780 m3 (4,944 yd3) and sediments range up to approximately 100 cm (3.28 ft) thick. Deposits T and DD contain a combined mass of about 45 kg (100 pounds) of PCBs, and these PCBs are located at depths less than 100 cm (3.28 ft). Approximately 32 kg (71 pounds) of PCBs remain in deposits N and O following completion of the SRD project and no future attempt to remove this mass is currently under consideration. The Thousand-Islands Nature Conservancy, located near the city of Kaukauna and just upstream of deposits W and X, is an important habitat area in this reach. The nature conservancy is protected island habitat in which eagles nest and other birds and terrestrial animals nest and feed. The wetland and SAV habitat associated with the shores of the conservancy are the largest in the reach. Additional wetlands and SAV areas are located near the Little Rapids dam, which is in the vicinity of Deposit DD. Mink habitat in this reach varies. Between Appleton and Kaukauna the mink habitat is generally characterized as either poor or unsuitable. However, between Kaukauna and Little Rapids, the shoreline habitat is characterized as moderate to good. 7.3.2.4 Little Rapids to De Pere Reach Sediment accumulation in this reach extends over a long distance and large area. Deposits EE through HH contain 980 kg (2,160 pounds) of PCBs in approximately 1.71 million m3 (2.24 million yd3) of sediment with concentrations greater than 50 μg/kg PCB. The four deposits in this reach are essentially a single sediment unit. RI findings for this reach include the following: These sediments cover about 266 hectares (657 acres) and are up to 2.3 m (7.5 ft) thick in select areas, especially near the De Pere dam. The highest total PCB concentration was 54,000 μg/kg. Further, PCB concentrations are lowest at the upstream end of Deposit EE and increase near the De Pere dam. Almost all of the PCB are contained in the upper 100 cm (3.28 ft) of sediments. No significant wetland or SAV areas are located in this reach. However, this reach is generally less developed than the other three reaches and large expanses of the shoreline are characterized as marginal to good for mink habitat. |
| List and Attach any additional reports, analyses etc. including use designation survey. 1. 2. 3. 4. 5. |