## Slide 1: Black Earth Creek Real-Time Monitoring
11-29-11

## Slide 2: Study Objectives
monitor the water-quality parameters of water temperature, specific conductance, pH, dissolved oxygen, and turbidity along BEC and use the data to identify the parameters of concern.
collect water-quality samples of suspended sediment, ammonia, and chloride to help describe water quality parameters of BEC and develop relationships between the real-time water-quality parameters and the water-quality sample results
establishing an alert system

## Slide 4: Basin Delineation

## Slide 5: Discharge
WY10
  Upstream = 19.24”
  Downstream = 17.46”
WY11
  Upstream = 17.10”
  Downstream = 16.32”
  The peak discharge in WY10 was ~370cfs (07/24/10) at the site near Black Earth and 193cfs in WY11 (03/20/11)

## Slide 6: Discharge
Chart: Black Earth Creek at Black Earth Comparison of Annual Mean Q and 3-year Moving Average
| 1955 | 1956 | 1957 | 1958 | 1959 | 1960 | 1961 | 1962 | 1963 | 1964 | 1965 | 1966 | 1967 | 1968 | 1969 | 1970 | 1971 | 1972 | 1973 | 1974 | 1975 | 1976 | 1977 | 1978 | 1979 | 1980 | 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007
Annual Mean Q | 32.1 | 26 | 24.7 | 20.6 | 28.5 | 49.1 | 37.9 | 35.7 | 27.3 | 19.8 | 28 | 23.7 | 23.2 | 24 | 30.5 | 23.6 | 29.4 | 31 | 46.1 | 48.4 | 44.7 | 37.3 | 25.8 | 31.3 | 34.7 | 36.4 | 32.8 | 36.4 | 36.2 | 40 | 48.1 | 53.4 | 39.4 | 37.4 | 29.5 | 27.3 | 29.1 | 33.5 | 61 | 45.1 | 38 | 44.3 | 40.4 | 43 | 48.4 | 47.2 | 49.4 | 43.9 | 31.1 | 44.9 | 36.8 | 29.8 | 42.6
3-year Moving Average | 27.6 | 23.7667 | 24.6 | 32.7333 | 38.5 | 40.9 | 33.6333 | 27.6 | 25.0333 | 23.8333 | 24.9667 | 23.6333 | 25.9 | 26.0333 | 27.8333 | 28 | 35.5 | 41.8333 | 46.4 | 43.4667 | 35.9333 | 31.4667 | 30.6 | 34.1333 | 34.6333 | 35.2 | 35.1333 | 37.5333 | 41.4333 | 47.1667 | 46.9667 | 43.4 | 35.4333 | 31.4 | 28.6333 | 29.9667 | 41.2 | 46.5333 | 48.0333 | 42.4667 | 40.9 | 42.5667 | 43.9333 | 46.2 | 48.3333 | 46.8333 | 41.4667 | 39.9667 | 37.6 | 37.1667 | 36.4 | 48.2

## Slide 7: Groundwater Recharge
According to a recent USGS publication (Gebert, 2011), base flow has been increasing in southwestern Wisconsin potentially due to improved agricultural practices.
With increasing recharge rates, it is suspect that daily mean water temperatures may be decreasing.
In a comparison of the average annual baseflow for the Black Earth gage for the full period of record (44years) to the data collected from 1970-99, there has been a 10.7 increase in the average annual baseflow.

## Slide 8
Chart: Daily Baseflow

## Slide 9
Chart: Black Earth Creek Baseflow Last 23 years

## Slide 10: Black Earth Creek Stormflow
Chart: 

## Slide 11: Discharge
Recharge Rates have been increasing
Stormflow in recent years has been minimal
There hasn’t been any “large” runoff events since monitoring started in 2009.
Improved recharge and decreased stormflow can impact fish communities and should be considered when evaluating the “condition” of Black Earth Creek

## Slide 12: Water Quality - samples
WY10 took 130 storm samples at the Brewery Rd and Black Earth locations
Took 6 storm samples at the remote sites
Monthly Baseflow samples

## Slide 13: Water Quality – Samples
Analyzed Water Quality Samples for:
Chloride
Total Kjeldahl Nitrogen
Ammonia
Nitrate
Suspended Sediment
Added the extra forms of Nitrogen to calculate Total Nitrogen and to see if a surrogate would be needed for Ammonium estimations.

## Slide 14: Ammonia
The highest ammonia concentrations occurred from snowmelt/rainfall event on 02/17-18/11. There were several discrete concentrations of ammonia over 2 mg/L at the downstream site that spanned over six hours.
The same event at the upstream site had concentrations at and just below 1 mg/L and just over on the grab sample from the Treatment Plant.
Using the conversion of the total ammonia nitrogen to un-ionized ammonia given the temp and pH at the time, the downstream max concentration of uni-ionized ammonia was 0.013mg/L. In this case the cold water temperature help keep the un-ionized ammonia concentrations low.

## Slide 15: Snowmelt Event
Ammonia concentrations were “high”
Conductivity didn’t show an increase due to the increased source of ammonia
Water temperature are low during this runoff event
Chart: Discharge, Turbidity, Water Temp * 10, and Ammonia Conc *100 in mg/L
Ammonia | 34.9 | 126 | 181 | 230 | 285 | 220

## Slide 16: Ammonia distribution between sites
Ammonia concentrations were highest at the downstream most site, despite lower concentrations at South Valley Rd.
Concentrations increased between the upstream site and the treatment plant but may be a result of the timing of the discrete sample collection.
Chart: Ammonia Concentration (mg/L)
| 40591.368055555555 | 40591.670138888891 | 40591.795138888891 | 40591.920138888891 | 40592.045138888891 | 40592.170138888891
BEC1 | 0.528 | 1 | 0.96 | 0.757 | 0.651 | 0.521
BEC2 | 1.38 | 0.581
BEC3 | 0.782 | 0.621
BEC4 | 0.349 | 1.26 | 1.81 | 2.3 | 2.85 | 2.2

## Slide 17: Real-Time Water Quality Trends WY10
Chart: BEC Water Temp
| 05406457 | 05406479 | 05406497 | 05406500
Min | 2.8 | 1.8 | 0 | 0
Mean | 10.5 | 10.6 | 10.6 | 10.5
Max | 20.4 | 22.3 | 22.6 | 22.5
Chart: BEC Conductance
| 05406457 | 05406479 | 05406497 | 05406500
Min | 378 | 245 | 235 | 320
Mean | 604 | 658 | 628 | 631
Max | 655 | 1210 | 856 | 782
Chart: BEC Turbidity
| 05406457 | 05406479 | 05406497 | 05406500
Min | 0 | 0 | 0 | 0
Mean | 11 | 21 | 10 | 10
Max | 150 | 600 | 210 | 180
Chart: BEC pH
| 05406457 | 05406479 | 05406497 | 05406500
Min | 7.1 | 7.4 | 7.2 | 7.4
Mean | 7.7 | 7.9 | 8 | 8
Max | 8.3 | 8.5 | 8.5 | 8.6

## Slide 18: Real-Time Water Quality Trends WY11
Chart: BEC Water Temp
| 05406457 | 05406479 | 05406497 | 05406500
Min | 0.8 | 0.1 | 0 | 0
Mean | 9.7 | 14 | 15.4 | 9.9
Max | 19.7 | 20.3 | 21.4 | 22.9
Chart: BEC Conductance
| 05406457 | 05406479 | 05406497 | 05406500
Min | 356 | 296 | 288 | 396
Mean | 614 | 671 | 647 | 634
Max | 700 | 958 | 991 | 818
Chart: BEC Turbidity
| 05406457 | 05406479 | 05406497 | 05406500
Min | 1.1 | 0.8 | 0 | 0.1
Mean | 12 | 14 | 6.6 | 5.5
Max | 150 | 370 | 200 | 77
Chart: BEC pH
| 05406457 | 05406479 | 05406497 | 05406500
Min | 7.3 | 7.4 | 7.4 | 7.4
Mean | 7.7 | 7.9 | 8 | 8.1
Max | 8.3 | 8.3 | 8.5 | 8.6

## Slide 19: Dissolved Oxygen
Chart: BEC DO WY10
| 05406457 | 05406479 | 05406497 | 05406500
Min | 4 | 5 | 4.3 | 4.7
Mean | 9.6 | 10.4 | 10.5 | 10.6
Max | 15.2 | 16 | 16.6 | 17.1
Chart: BEC DO WY11
| 05406457 | 05406479 | 05406497 | 05406500
Min | 6.2 | 6.5 | 6 | 5.2
Mean | 10 | 10.7 | 10.8 | 10.9
Max | 14.5 | 15.6 | 16.5 | 16.9

## Slide 20: Daily Minimum Dissolved Oxygen
All Sites were <5mg/L ~2% of the time
No Sites were <5mg/L
Chart: WY2010 Daily Minimum D.O.
Chart: WY2011 Daily Minimum D.O.

## Slide 21: Regressions
Ran stepwise linear regressions on the water quality data against the real-time water quality sondes outputs
Regressions looked at the both the sonde results and the log of the results (except pH)
Did this for every parameter measured
Current regressions represent relationships determined for ranges in flows and water quality conditions measured

## Slide 22: BEC @ Cross Plains Suspended Sediment
SS = 0.099-0.1394*w.temp-0.001*sp. Cond+2.4106*log w.temp+ 0.9155*turbidity

## Slide 23: BEC @ Cross Plains Ammonia
NH4 = 0.1785-0.0072*Q-0.0024*sp.cond-0.2503*D.O.-1.5341*log w.temp+3.7362*logD.O.+0.2734*logturbidity

## Slide 24: BEC @ Black Earth Suspended Sediment
SS = 0.8434-0.3732seasonal+0.0032*turbidity+0.6497*log turbidity

## Slide 25: BEC @ Black Earth Chloride
Cl = -1.6506-0.0068*w.temp+1.1302*log sp. Cond.+0.0431*log turbidity

## Slide 26: BEC @ Black Earth Ammonia
NH4= -6.0459-0.0085*Q-0.0272*w.temp+3.0521*log Q+0.2858*log turbidity

## Slide 27: Regression Status
As more data has been added the regression equations have been changing.
Need to get “bigger” storms or get through another year and see if the regression equations hold

## Slide 28: Alerts
No Conditions were met that required an alert to be sent
Though a couple of alerts were sent during calibration and probe malfunctions

## Slide 29: Publication
Review of historic and new water-quality data
Include real-time results
Initial regression review
Potential review of historic and current “bug” data
Identify times and water quality parameters of concern.