Date: 7/12/2016    Scenario: 1955 Diatom Inferred TP

Lake Id: Big Blake Lake

Watershed Id: 0

Hydrologic and Morphometric Data

Tributary Drainage Area: 2165.5 acre

Total Unit Runoff: 8.00 in.

Annual Runoff Volume: 1443.7 acre-ft

Lake Surface Area <As>: 208.0 acre

Lake Volume <V>: 1872.0 acre-ft

Lake Mean Depth <z>: 9.0 ft

Precipitation - Evaporation: 3.3 in.

Hydraulic Loading: 1500.9 acre-ft/year

Areal Water Load <qs>: 7.2 ft/year

Lake Flushing Rate <p>: 0.80 1/year

Water Residence Time: 1.25 year

Observed spring overturn total phosphorus (SPO): 54.9 mg/m^3

Observed growing season mean phosphorus (GSM): 54.9 mg/m^3

% NPS Change: 0%

% PS Change: 0%

NON-POINT SOURCE DATA

Land Use        Acre        Low    Most Likely    High    Loading %   Low    Most Likely    High

(ac)     |---- Loading (kg/ha-year) ----|            |-----  Loading (kg/year) ----|

Row Crop AG           488.5       0.50       1.00       3.00       63.1         99        198        593

Mixed AG                0.0       0.30       0.80       1.40        0.0          0          0          0

Pasture/Grass         318.5       0.10       0.30       0.50       12.3         13         39         64

HD Urban (1/8 Ac)       0.0       1.00       1.50       2.00        0.0          0          0          0

MD Urban (1/4 Ac)       0.0       0.30       0.50       0.80        0.0          0          0          0

Rural Res (>1 Ac)     131.7       0.05       0.10       0.25        1.7          3          5         13

Wetlands              474.1       0.10       0.10       0.10        6.1         19         19         19

Forest                752.7       0.05       0.09       0.18        8.7         15         27         55

Lake Surface          208.0       0.10       0.30       1.00        8.1          8         25         84

POINT SOURCE DATA

Point Sources     Water Load     Low    Most Likely    High    Loading %

(m^3/year)  (kg/year)  (kg/year)   (kg/year)          _

SEPTIC TANK DATA

Description                                        Low    Most Likely   High     Loading %

Septic Tank Output (kg/capita-year)                0.30        0.50     0.80

# capita-years                          0.0

% Phosphorus Retained by Soil                      98.0        90.0     80.0

Septic Tank Loading (kg/year)                      0.00        0.00     0.00         0.0

TOTALS DATA

Description                      Low    Most Likely   High     Loading %

Total Loading (lb)               346.6       691.3      1827.7   100.0

Total Loading (kg)               157.2       313.5       829.1   100.0

Areal Loading (lb/ac-year)        1.67        3.32        8.79

Areal Loading (mg/m^2-year)     186.80      372.50      984.92

Total PS Loading (lb)              0.0         0.0         0.0     0.0

Total PS Loading (kg)              0.0         0.0         0.0     0.0

Total NPS Loading (lb)           328.1       635.6      1642.2   100.0

Total NPS Loading (kg)           148.8       288.3       744.9   100.0

Wisconsin Internal Load Estimator

Date: 7/12/2016    Scenario: 22

Method 1 - A Complete Total Phosphorus Mass Budget

Method 1 - A Complete Total Phosphorus Mass Budget 54.87 mg/m^3

Phosphorus Inflow Concentration: 169.4 mg/m^3

Areal External Loading: 372.5 mg/m^2-year

Predicted Phosphorus Retention Coefficient: 0.74

Observed Phosphorus Retention Coefficient: 0.68

Internal Load:  46 Lb      21 kg

Method 2 - From Growing Season In Situ Phososphorus Increases

Start of Anoxia

Average Hypolimnetic Phosphorus Concentration: 0 mg/m^3

Hypolimnetic Volume: 0.0 acre-ft

Anoxia Sediment Area: 0.0 acres

Just Prior To The End of Stratification

Average Hypolimnetic Phosphorus Concentration: 0 mg/m^3

Hypolimnetic Volume: 0.0 acre-ft

Anoxia Sediment Area: 0.0 acres

Time Period of Stratification: 1 days

Sediment Phosphorus Release Rate: 0 mg/m^2-day     0 lb/acre-day

Internal Load: 0 Lb     0 kg

Method 3 - From In Situ Phososphorus Increases In The Fall

Start of Anoxia

Average Hypolimnetic Phosphorus Concentration: 0 mg/m^3

Hypolimnetic Volume: 0 acre-ft

Anoxia Sediment Area: 0 acres

Just Prior To The End of Stratification

Average Water Column Phosphorus Concentration: 0 mg/m^3

Lake Volume: 1872.0 acre-ft

Anoxia Sediment Area Just Before Turnover: 0 acres

Time Period Between Observations: 1 days

Sediment Phosphorus Release Rate: 0 mg/m^2-day     0 lb/acre-day

Internal Load:   0 Lb       0 kg

Method 4 - From Phososphorus Release Rate and Anoxic Area

Start of Anoxia Anoxic Sediment Area: 0 acre

End of Anoxia Anoxic Sediment Area: 0 acre

Phosphorus Release Rate As Calculated In Method 2: 0 mg/m^2-day

Phosphorus Release Rate As Calculated In Method 3: 0 mg/m^2-day

Average of Methods 2 and 3 Release Rates: 0.0 mg/m^2-day

Period of Anoxia: 0 days

Default Areal Sediment Phosphorus Release Rates:

Low   Most Likely   High

6        14         24

Internal Load: (Lb)            0         0          0

Internal Load: (kg)            0         0          0

Internal Load Comparison (Percentanges are of the Total Estimate Load)

Total External Load: 691 Lb      314 kg

Lb         kg         %

From A Complete Mass Budget:                               46        21       6.2

From Growing Season In Situ Phosphorus Increases:           0         0         0

From In Situ Phososphorus Increases In The Fall:            0         0       0.0

From Phososphorus Release Rate and Anoxic Area:             0         0         0

Predicted Water Column Total Phosphorus Concentration (ug/l)

Nurnberg+ 1984 Total Phosphorus Model:      Low    Most Likely   High

33          44       115

Osgood, 1988 Lake Mixing Index: 3.0

Phosphorus Loading Summary:

Low      Most Likely     High

Internal Load (Lb):        46            0.0          0

Internal Load (kg):        21            0.0          0

External Load (Lb):       347            691       1828

External Load (kg):       157            314        829

Total Load (Lb):          393            691       1828

Total Load (kg):          178            314        829

Phosphorus Prediction and Uncertainty Analysis Module

Date: 7/12/2016    Scenario: 16

Observed spring overturn total phosphorus (SPO): 54.9 mg/m^3

Observed growing season mean phosphorus (GSM): 54.9 mg/m^3

Back calculation for SPO total phosphorus: 0.47 mg/m^3

Back calculation GSM phosphorus: 0.47 mg/m^3

% Confidence Range: 70%

Nurenberg Model Input - Est. Gross Int. Loading: 44 kg

Lake Phosphorus Model              Low   Most Likely   High     Predicted  % Dif.

Total P   Total P    Total P   -Observed

(mg/m^3) (mg/m^3)   (mg/m^3)   (mg/m^3)

Walker, 1987 Reservoir                         30       60        159          5         9

Canfield-Bachmann, 1981 Natural Lake           35       58        112          3         5

Canfield-Bachmann, 1981 Artificial Lake        31       48         81         -7       -13

Rechow, 1979 General                           13       26         69        -29       -53

Rechow, 1977 Anoxic                            63      126        334         71       129

Rechow, 1977 water load<50m/year               30       60        158          5         9

Rechow, 1977 water load>50m/year              N/A      N/A        N/A        N/A       N/A

Walker, 1977 General                           44       89        234         34        62

Vollenweider, 1982 Combined OECD               32       56        125          1         2

Dillon-Rigler-Kirchner                         22       43        114        -12       -22

Vollenweider, 1982 Shallow Lake/Res.           26       48        113         -7       -13

Larsen-Mercier, 1976                           40       80        212         25        46

Nurnberg, 1984 Oxic                            46       67        139         12        22

Lake Phosphorus Model          Confidence Confidence  Parameter    Back       Model

Lower      Upper      Fit?    Calculation   Type

Bound      Bound               (kg/year)

Walker, 1987 Reservoir                       35        124         FIT         2       GSM

Canfield-Bachmann, 1981 Natural Lake         18        167         FIT         1       GSM

Canfield-Bachmann, 1981 Artificial Lake      15        138         FIT         1       GSM

Rechow, 1979 General                         15         54         FIT         6       GSM

Rechow, 1977 Anoxic                          75        259         FIT         1       GSM

Rechow, 1977 water load<50m/year             34        124         FIT         2       GSM

Rechow, 1977 water load>50m/year            N/A        N/A         N/A       N/A       N/A

Walker, 1977 General                         44        192         FIT         2       SPO

Vollenweider, 1982 Combined OECD             28        113         FIT         1       ANN

Dillon-Rigler-Kirchner                       26         89           P         3       SPO

Vollenweider, 1982 Shallow Lake/Res.         24         98         FIT         2       ANN

Larsen-Mercier, 1976                         49        164       P Pin         2       SPO

Nurnberg, 1984 Oxic                          39        123           P      -168       ANN