Date: 7/26/2016    Scenario: L-THIA combined 15% reduction

Lake Id: Big Blake Lake

Watershed Id: 1

Hydrologic and Morphometric Data

Tributary Drainage Area: 20066.1 acre

Total Unit Runoff: 8.00 in.

Annual Runoff Volume: 13377.4 acre-ft

Lake Surface Area <As>: 208.0 acre

Lake Volume <V>: 1872.0 acre-ft

Lake Mean Depth <z>: 9.0 ft

Precipitation - Evaporation: 3.3 in.

Hydraulic Loading: 13434.6 acre-ft/year

Areal Water Load <qs>: 64.6 ft/year

Lake Flushing Rate <p>: 7.18 1/year

Water Residence Time: 0.14 year

Observed spring overturn total phosphorus (SPO): 36.8 mg/m^3

Observed growing season mean phosphorus (GSM): 57.0 mg/m^3

% NPS Change: -15%

% PS Change: 0%

NON-POINT SOURCE DATA

Land Use        Acre        Low    Most Likely    High    Loading %   Low    Most Likely    High

(ac)     |---- Loading (kg/ha-year) ----|            |-----  Loading (kg/year) ----|

Row Crop AG          1023.8       0.50       1.00       3.00       24.7        176        352       1057

Mixed AG                0.0       0.30       0.80       1.40        0.0          0          0          0

Pasture/Grass        4790.6       0.10       0.30       0.50       34.7        165        494        824

HD Urban (1/8 Ac)       4.3       1.00       1.50       2.00        0.2          1          2          3

MD Urban (1/4 Ac)       0.0       0.30       0.50       0.80        0.0          0          0          0

Rural Res (>1 Ac)     691.9       0.05       0.10       0.25        1.7         12         24         60

Wetlands             1496.3       0.10       0.10       0.10        3.6         51         51         51

Forest              10759.2       0.05       0.09       0.18       23.4        185        333        666

Lake Surface          208.0       0.10       0.30       1.00        1.8          8         25         84

POINT SOURCE DATA

Point Sources     Water Load     Low    Most Likely    High    Loading %

(m^3/year)  (kg/year)  (kg/year)   (kg/year)          _

SEPTIC TANK DATA

Description                                        Low    Most Likely   High     Loading %

Septic Tank Output (kg/capita-year)                0.30        0.50     0.80

# capita-years                        164.4

% Phosphorus Retained by Soil                      98.0        90.0     80.0

Septic Tank Loading (kg/year)                      0.99        8.22    26.30         0.6

TOTALS DATA

Description                      Low    Most Likely   High     Loading %

Total Loading (lb)              1421.8      3141.1      7095.1   100.0

Total Loading (kg)               644.9      1424.8      3218.3   100.0

Areal Loading (lb/ac-year)        6.84       15.10       34.11

Areal Loading (mg/m^2-year)     766.16     1692.66     3823.39

Total PS Loading (lb)              0.0         0.0         0.0     0.0

Total PS Loading (kg)              0.0         0.0         0.0     0.0

Total NPS Loading (lb)          1401.0      3067.3      6851.6    99.4

Total NPS Loading (kg)           635.5      1391.3      3107.8    99.4

Phosphorus Prediction and Uncertainty Analysis Module

Date: 7/26/2016    Scenario: 21

Observed spring overturn total phosphorus (SPO): 36.8 mg/m^3

Observed growing season mean phosphorus (GSM): 57.0 mg/m^3

Back calculation for SPO total phosphorus: 37.14 mg/m^3

Back calculation GSM phosphorus: 57.24 mg/m^3

% Confidence Range: 70%

Nurenberg Model Input - Est. Gross Int. Loading: 65 kg

Lake Phosphorus Model              Low   Most Likely   High     Predicted  % Dif.

Total P   Total P    Total P   -Observed

(mg/m^3) (mg/m^3)   (mg/m^3)   (mg/m^3)

Walker, 1987 Reservoir                         23       50        114         -7       -12

Canfield-Bachmann, 1981 Natural Lake           30       60        120          3         5

Canfield-Bachmann, 1981 Artificial Lake        27       51         91         -6       -11

Rechow, 1979 General                           22       48        109         -9       -16

Rechow, 1977 Anoxic                            34       75        168         18        32

Rechow, 1977 water load<50m/year               25       56        127         -1        -2

Rechow, 1977 water load>50m/year              N/A      N/A        N/A        N/A       N/A

Walker, 1977 General                           29       64        145         27        73

Vollenweider, 1982 Combined OECD               24       46         90         -1        -2

Dillon-Rigler-Kirchner                         20       45        101          8        22

Vollenweider, 1982 Shallow Lake/Res.           19       39         80         -8       -17

Larsen-Mercier, 1976                           28       63        141         26        71

Nurnberg, 1984 Oxic                            27       56        121         -1        -2

Lake Phosphorus Model          Confidence Confidence  Parameter    Back       Model

Lower      Upper      Fit?    Calculation   Type

Bound      Bound               (kg/year)

Walker, 1987 Reservoir                       28         93         FIT      1623       GSM

Canfield-Bachmann, 1981 Natural Lake         19        173         FIT      1318       GSM

Canfield-Bachmann, 1981 Artificial Lake      16        147         FIT      1641       GSM

Rechow, 1979 General                         26         90         FIT      1697       GSM

Rechow, 1977 Anoxic                          43        137         FIT      1094       GSM

Rechow, 1977 water load<50m/year             31        105         FIT      1448       GSM

Rechow, 1977 water load>50m/year            N/A        N/A         N/A       N/A       N/A

Walker, 1977 General                         31        126         FIT       823       SPO

Vollenweider, 1982 Combined OECD             22         87         FIT      1469       ANN

Dillon-Rigler-Kirchner                       26         82           P      1180       SPO

Vollenweider, 1982 Shallow Lake/Res.         19         74         FIT      1801       ANN

Larsen-Mercier, 1976                         37        114       P Pin       845       SPO

Nurnberg, 1984 Oxic                          29        105         FIT      1468       ANN