| 2008 Impaired Waters Documentation Sheet | Date Prepared _9/24/07_____________________________________________ |
| --- | --- |
| Author _Erin Hanson___________________________________________________ |
| Waterbody Name _Lower Fox River Seg. 3 (1)_____________________________ | Watershed_ ____________________ |
| WADRS ID | _ 10678 ____________ | WBIC _117900__________________ |  |
| Choose One: |
| _X______ | Proposed 303d List Change (new water, delisting, new pollutants) NEW = Sediment |
| _______ | General 303d Documentation |
| TMDL/303D Listing Proposal |
| _0_______ | Start Mile | _7.39____ | End Mile | _7.39___ | Size (Miles/Acres) |
| Current Assessment: |
| _________ | Current Fish & Aquatic Life (Aquatic Community) Use _WWSF____________________________________________________________ |
| _________ | Attainable Fish & Aquatic Life (Aquatic Community) Use__WWSF__________________________________________________________ |
| _________ | Designated Fish & Aquatic Life Use_DEFAULT_________________________________________________________________________ |
| _________ | Supporting Attainable Use = fully, partially, not meeting _not supporting____________________________________________________ |
| _________ | Does a Specific Fish Advisory Exist? (Yes/No) |
|  | ________ | If so, what is the advice? PCB |
| Pollutants & Impairments |
| X________ | Impairments (Circle One or More) |
|  | Degraded habitat | Acute Toxicity | Chronic Toxicity | Temperature (Water) |
|  | Contaminated Fish Tissue | Eutrophication | Excessive Aquatic Plant Growth |
|  | Aquatic Invasives (AIS) Infestation |  | Dissolved Oxygen, Low |
|  | Other ______________________________________________________________________ |
| X________ | Pollutants (Circle One or More) |  |
|  | Total Phosphorus | Sediment - NEW | PCBs | PAHs | Creosote |
|  | NH3 (Ammonia) | Runoff Water (elevated temperatures) | Other _____________________________ |
|  | Other mercury_____________________________________________________________________ |
| X________ | Assessment Level (monitored site specific data less than 5 years old) versus evaluated (other) |
| ________ | DNR Category (3, 4d (recommended), 5a, 5b, 5c) |
| Monitoring and Listing |
| X________ | Water Quality Exceedances (As applicable) Dissolved Oxygen Station ID # Results < 5 mg/l Dates 053001 46 05/16/1961 - 07/29/1976 053002 2 08/12/1975 053210 7 07/06/1975 - 05/04/1995 053222 4 07/16/1980 - 08/31/1983 053223 3 07/06/1975 053311 4 09/17/1974 - 08/18/1975 053512 1 08/17/1992 |
| X________ | Assessment Parameters (M-IBI, FISH IBI, HBI) Macroinvertebrate IBI: Station 053219 = 4.01 (11/12/1975), Station 053692 = 3.36 (10/12/1998), data in SWIMS No data for fish Warmwater IBI or habitat rating in WDNR fisheries database |
| Stations/Dates/Metric/Scores ____________________________________________________________________________________ |
| Stations/Dates/Metric/Scores ____________________________________________________________________________________ |
| Attach any additional reports, analyses, etc. (Use Designation Survey, etc.) |
| Excerpts from “Toward a Total Maximum Daily Load (TMDL) for Phosphorus and Suspended Solids: The Lower Fox River Basin and Green Bay Area of Concern” by Scheberle, D., H.J. Harris, M. Finney, J. Potter, S. Oldenburg, P. Dessart., no date “According to the WDNR 303 (d) list, the water quality of Lower Green Bay and the Fox River is impaired due to phosphorus and PCBs (WDNR, 2005). Phosphorus and TSS are the pollutants of concern for this framework. Even though suspended solids are not listed as a pollutant that impairs designated uses for the lower Fox River and the bay, ample research demonstrates that both TSS and phosphorous affect water quality (Harris, 1993; Millard & Sager, 1994).” p. 18 “Figure 10 a: TSS for River Stations. Graph of mean TSS concentrations for the river stations 1. The blue dotted line represents the RAP target of 10 mg/l.” p. 24 (Data collected by GBMSD, River stations = data from Fox River (4 stations) & East River (2 stations) “Suspended solids loading into the AOC and Green Bay have also been estimated through monitoring (SDATF, 2002) and modeling (Baumgart, 2005). The average monitoring SS load at the mouth of the Fox River for water years 1995-1999 was 119,400 mt/yr-1 (Table 2b). This amounts to 327 metric tons per day in an average year. With the addition of the point sources, the estimated contribution from Lake Winnebago, and the estimated autogenic solids contribution from the river (WDNR, 2001), the simulated 1989-2000 suspended sediment load at the Fox River outlet to Green Bay is 119,000 mt/yr-1 (Baumgart, 2005). p. 31“ Data from SWIMS: Sample Station Locations. Note: Stations with recent data identified by bold text. No map of sample stations created. Station ID Station Name Start Date End Date 053001 FOX RIVER - AT MASON ST IN GREEN BAY 4/11/1961 12/14/1976 053002 GREEN BAY - STUDY DNR STA 1 9/17/1973 8/12/1975 053043 FOX RIVER - DE PERE STP 001 10/15/1975 1/8/1985 053079 FOX RIVER - CHARMIN PAPER CO GR BAY OTFL 001 9/26/1977 6/4/1985 053080 FOX RIVER - CHARMIN PAPER CO GREEN BAY 009 1/21/1981 12/1/1981 053104 FOX RIVER - NICOLET PAPER CO SETTLING POND 5/3/1977 3/21/1985 053210 FOX RIVER - ABOVE DEPERE DAM 7/6/1975 9/12/2007 053211 FOX RIVER - BELOW DEPERE DAM AT LOCKS 9/17/1974 8/18/1975 053220 FOX RIVER - ABOVE EAST RIVER 1969 (6 dates) 2002 (6 dates) 053222 FOX RIVER - AT GREEN BAY YACHT CLUB 6/27/1978 4/27/2007 053223 FOX RIVER - AT MOUTH GREEN BAY 7/6/1975 7/27/1977 053311 GREEN BAY - NR SHR STDY STA 76A01A 9/17/1974 8/18/1975 053362 GREEN BAY - NR SHR STDY STA 78C01M 6/14/1972 7/25/1973 053483 FOX RIVER - AT MOUTH, AT GREEN BAY, WI 7/6/1988 11/1/1995 053512 GREEN BAY - MOUTH OF FOX R A1 5/19/1992 10/13/1992 053552 FOX RIVER - DOWNSTREAM FROM DUTCHMAN'S CREEK 7/10/1993 3/30/2000 053583 FOX RIVER - GBMBS STN 2FRB22 11/8/1989 053681 FOX RIVER - DOWNSTREAM OF FORT JAMES, AT GREEN BAY, WI 8/4/1999 3/30/2000 Selected Water Quality Parameters from SWIMS: Parameter, units Station ID Average Min Max Count DISSOLVED OXYGEN FIELD, mg/l 053001 7.5 0 15.4 172 053002 6.5 2.5 9.4 14 053210 11.5 0 220 370 053211 8.8 6.8 12.5 35 053220 8.8 7.6 10 6 053222 8.3 1.9 14.1 32 053223 4.5 1.5 6.5 9 053311 8.5 2.1 13.6 12 053512 8.2 4.4 9.7 13 TEMPERATURE FIELD, deg C 053001 11.4 0 31 172 053002 20.1 15.5 25 64 053104 34.9 10 64 5 053210 11.4 -0.2 30.4 365 053211 21.7 10 29 35 053222 18.2 2.2 27 32 053223 23.8 21.5 26 9 053311 11.4 0 25.5 12 053362 23.8 21.5 27 24 053512 18.8 12.6 23.8 13 FECAL COLIFORM, MEMBRANE FILTER, MFC AGAR, #/100ml 053210 220 0 6300 165 NITROGEN KJELDAHL TOTAL, mg/l 053079 5.43 3.8 7.2 4 053104 14.68 3.2 26 6 053210 1.59 0 23 196 053211 1.81 1 2.5 28 053220 1.22 0.63 1.75 6 053222 1.85 0.89 3.2 30 053483 2.10 0 20 309 053512 1.47 1.4 1.6 3 NITROGEN NH3-N DISS, mg/l 053001 0.22 0.02 1.1 101 053002 1.20 0.101 3.57 14 053043 16.73 0.3 32 10 053079 0.95 0.1 4.6 10 053080 69.00 1 053104 100.02 0.8 360 18 053210 0.13 0 1.1 259 053211 0.05 0.02 0.27 38 053220 0.03 0.018 0.045 6 053222 0.24 0.04 0.97 28 053223 0.51 0.34 0.7 12 053483 0.31 0.02 3 297 NITROGEN NH3-N TOTAL, mg/l 053210 0.18 0 0.512 30 053311 0.71 0.09 2.3 12 053362 0.83 0.021 1.848 30 053483 0.12 0 0.36 93 053512 0.08 0.058 0.086 3 NITROGEN NO3+NO2 DISS (AS N), mg/l 053001 0.15 0.01 0.4 28 053002 0.42 0.42 0.42 2 053043 2.25 0.1 4.4 2 053079 0.41 0.36 0.5 6 053080 0.20 0.2 0.2 1 053104 0.63 0.5 0.9 3 053210 0.34 0 2.5 260 053211 0.08 0.02 0.41 37 053220 1.79 0.095 5.06 6 053222 0.11 0.02 0.64 28 053223 0.05 0.02 0.1 12 053483 0.18 0 1.51 390 053512 0.31 0.292 0.316 3 PHOSPHATE ORTHO DISS, mg/l 053001 0.04 0.004 0.17 46 053002 0.02 0.009 0.044 12 053043 1.70 0.154 3.9 3 053079 0.10 0.007 0.196 3 053210 0.03 0 0.154 284 053211 0.03 0.002 0.099 34 053222 0.04 0.003 0.14 36 053223 0.05 0.016 0.085 6 053311 0.03 0.001 0.115 12 053362 0.12 0.034 0.219 36 053483 0.02 0 0.14 405 053512 0.00 0 0.003 3 053583 0.00 0.004 0.005 2 PHOSPHORUS TOTAL , mg/l 053001 0.19 0.03 0.58 102 053002 0.16 0.076 0.247 14 053043 5.64 0.47 12.3 13 053079 0.32 0.1 0.76 10 053080 0.16 0.16 0.16 1 053104 1.17 0.15 3.6 9 053210 0.14 0 1.6 286 053211 0.18 0.08 0.3 34 053220 0.16 0.067 0.245 6 053222 0.18 0.068 0.404 36 053223 0.25 0.21 0.3 12 053311 0.19 0.062 0.68 12 053483 0.18 0 2.4 315 053512 0.13 0.113 0.14 3 RESIDUE TOTAL NFLT (TOTAL SUSPENDED SOLIDS), mg/l 053001 19.6 0 106 174 053002 17.8 8.8 24.8 12 053043 598.2 0 5360 11 053079 69.6 40 124 5 053080 125.0 96 154 2 053104 98.0 6 660 8 053210 24.0 0 340 274 053211 33.9 13 64 38 053222 30.1 6 104 38 053223 40.0 18 68 12 053311 23.1 1 64 12 053483 35.9 0 1370 2247 053512 32.0 25 37 3 053552 10.0 0 82 404 053681 11.0 0 139 506 TURBIDITY, LAB NEPHELOMETRIC NTU 053210 20.9 1.1 114 69 Macroinvertebrate data from SWIMS: Station 053219 - FOX RIVER - AT MAIN ST GREEN BAY, 11/12/1975 Station 053692 - FOX RIVER - AT STH 32 IN DE PERE, 10/12/1998 Parameter Station ID Average Min Max Count INDEX OF BIOTIC INTEGRITY (IBI) 053219 4.01 1 053692 3.36 3.36 3.36 2 Data from USGS: USGS 04085139 FOX RIVER AT MOUTH AT GREEN BAY, WI – 7/6/1988 through 12/5/1995 USGS 040851385 FOX RIVER AT OIL TANK DEPOT AT GREEN BAY, WI – 11/3/1993 through 8/9/2006 USGS 04085084 FOX RIVER DOWNSTREAM OF FORT JAMES AT GREEN BAY,WI – 8/4/1999 through 3/30/2000 USGS 040850825 FOX RIVER UPSTREAM OF FORT JAMES AT GREEN BAY, WI - 8/4/1999 through 3/30/2000 USGS 04085059 FOX RIVER AT DE PERE, WI – 6/14/1988 through 7/10/1993 Parameter, units Site ID Average Min Max Count Dissolved oxygen, water, unfiltered, milligrams per liter 4085059 11.4 5.9 17.5 78 4085139 10.1 3.3 16.7 168 40851385 10.1 5.2 15.3 40 Temperature, water, degrees Celsius 4085059 14.4 0 27.1 78 4085139 14.5 0 28 170 40851385 13.8 0.5 25.5 40 Total nitrogen, water, unfiltered, milligrams per liter 4085059 1.56 0.85 2.2 60 4085139 1.70 0.94 5 123 40851385 1.65 1.1 3.8 52 Organic nitrogen, water, unfiltered, milligrams per liter 4085059 1.24 0.7 2.2 51 4085139 1.39 0.66 2.9 158 40851385 1.10 0.68 1.8 49 Ammonia, water, filtered, milligrams per liter as nitrogen 4085059 0.09 0.019 0.3 75 4085139 0.24 0.01 2 166 40851385 0.13 0.015 0.36 53 Phosphorus, water, unfiltered, milligrams per liter 4085059 0.12 0.04 0.26 80 4085139 0.13 0.03 0.3 166 40851385 0.14 0.06 0.52 54 Orthophosphate, water, filtered, milligrams per liter 4085059 0.02 0.006 0.098 75 4085139 0.05 0.006 1.01 147 40851385 0.11 0.009 0.294 51 Residue, total nonfilterable, milligrams per liter 4085059 24 1 110 359 4085084 24 3 139 503 4085139 34 2 390 611 40850825 26 3 66 493 40851385 41 2 550 498 Residue on evap, dried at 105 C, water, unfilt, mg/l 4085059 312 306 320 6 4085139 329 280 374 3 40851385 318 278 358 10 Suspended sediment concentration, milligrams per liter 4085059 34 1 194 357 4085139 31 3 312 360 Suspended sediment discharge, tons per day 4085059 547 8.5 7800 295 4085139 1004 44 10200 16 |