| 2008 Impaired Waters Documentation Sheet | Date Prepared _10/9/2007____________________________________________ |
| --- | --- |
| Author _Erin Hanson___________________________________________________ |
| Waterbody Name _Duck Creek – Segment 2_______________________________________ | Watershed LF05 – Duck Creek______________ |
| WADRS ID | _10851 ____________ | WBIC _409700__________________ |  |
| Choose One: |
| _CHANGE | Proposed 303d List Change (new water, delisting, new pollutants) Mileage segments must change to reflect that some of this stream is in tribal territory. Miles 0-4.96 can stay on the list; miles 4.96-25.69 are on the reservation so cannot be on Wisconsin’s list. Miles 25.69 – 32.9 are impaired. Miles 32.9-39.82 are not impaired. |
| _X______ | General 303d Documentation |
| TMDL/303D Listing Proposal |
| _10.84___ | Start Mile | _32___ | End Mile | _21.16__ | Size (Miles/Acres) |
| Current Assessment: |
| _________ | Current Fish & Aquatic Life (Aquatic Community) Use _WWFF___________________________________________________________ |
| _________ | Attainable Fish & Aquatic Life (Aquatic Community) Use_ WWFF__________________________________________________________ |
| _________ | Designated Fish & Aquatic Life Use_DEFAULT_________________________________________________________________________ |
| _________ | Supporting Attainable Use = fully, partially, not meeting _NOT SUPPORTING_______________________________________________ |
| _________ | Does a Specific Fish Advisory Exist? (Yes/No) |
|  | ________ | If so, what is the advice? Statewide Mercury |
| Pollutants & Impairments |
| X________ | Impairments (Circle One or More) |
|  | Degraded habitat | Acute Toxicity | Chronic Toxicity | Temperature (Water) |
|  | Contaminated Fish Tissue | Eutrophication | Excessive Aquatic Plant Growth |
|  | Aquatic Invasives (AIS) Infestation |  | Dissolved Oxygen, Low |
|  | Other _Sediment_____________________________________________________________________ |
| _X_______ | Pollutants (Circle One or More) |  |
|  | Total Phosphorus | Sediment | PCBs | PAHs | Creosote |
|  | NH3 (Ammonia) | Runoff Water (elevated temperatures) | Other _____________________________ |
|  | Other _Mercury_____________________________________________________________________ |
| ________ | Assessment Level (monitored site specific data less than 5 years old) versus evaluated (other) |
| ________ | DNR Category (3, 4d (recommended), 5a, 5b, 5c) |
| Monitoring and Listing |
| _X_______ | Water Quality Exceedances (As applicable) Dissolved Oxygen < 5 mg/l USGS Station 4072050: 3/11/1993, 9/22/1994 (2 values), 8/2/1995 (2 values) & 8/17/2001 |
| ________ | Assessment Parameters (M-IBI, FISH IBI, HBI) HBI max 10 = 4.83 – 8.14 indicating “good” to “poor” water quality rating & “some” to “very significant” degree of organic pollution (Lillie et al 2003), table below, data in SWIMS |
| Stations/Dates/Metric/Scores ____________________________________________________________________________________ |
| Stations/Dates/Metric/Scores ____________________________________________________________________________________ |
| Attach any additional reports, analyses, etc. (Use Designation Survey, etc.) |
| Data in SWIMS: See map named 409700-2.pdf for sample station locations. Station ID Station Name Dates 453002 DUCK CREEK - FREEDOM SCHOOL DISTRICT NO 3 STP Macroinvert. 10/17/1980 283295 DUCK CREEK - AT CTH J Macroinvert. 05/12/1980 & 10/17/1980 10009507 DUCK CREEK (2) 20M UPSTREAM OF DISCHARGE Macroinvert 10/10/2002 & 10/26/2005 Water quality 5/10/2006 10009506 DUCK CREEK (1) 357M DOWNSTREAM OF DISCHARGE Macroinvert 10/10/2002 & Water quality 5/10/2006 453255 DUCK CREEK - AT SEMINARY RD Macroinvert 5/17/1995 & 5/4/1998 Water quality 7/26/07 453006 DUCK CREEK - AT CENTER VALLEY RD, NEAR FREEDOM, WI Macroinvert 1979 (2 dates), 9/29/1994 & 4/25/1995 Macroinvertebrate data: Parameter Station ID Average Min Max Count HBI Max 10 453006 6.40625 5.5 7.375 4 453255 5.4547778 4.894 6.048 9 10009506 8.138 1 10009507 6.9106667 5.807 7.648 3 10015820 5.057 1 10016382 4.827 1 INDEX OF BIOTIC INTEGRITY (IBI) 453006 1.7822825 0.36405 3.0301 4 453255 4.2869456 2.89474 5.9886 9 10009506 3.45388 1 10009507 3.766 2.2609 4.86672 3 10015820 4.13681 1 10016382 4.44135 1 Water Quality data: Parameter, units Station ID Average Min Max Count DISSOLVED OXYGEN FIELD, mg/l 453255 7.45 1 10009506 11.1 1 10009507 11.5 1 PHOSPHORUS TOTAL, mg/l 453255 0.583 0.583 0.583 1 PHOSPHORUS TOTAL DISS, mg/l 453255 0.46 1 10009506 0.139 1 10009507 0.087 1 RESIDUE TOTAL NFLT (TOTAL SUSPENDED SOLIDS), mg/l 453047 27.375 4 156 8 453255 3 3 3 1 10009506 0 1 10009507 0 1 Data from USGS: Table of stations below for both segments 1 & 2, not represented on sample station .pdf map. USGS 04072050 in Segment 2 downstream from SWIMS Station 453255, data summarized in table below. Agency Site ID Station Name Water Quality Begin Water Quality End Count USGS 04072013 DUCK CREEK AT STINGE ROAD NEAR BLACK CREEK, WI 05/11/1989 07/06/1994 5 USGS 04072014 DUCK CREEK AT CT HIGHWAY EE NEAR FIVE CORNERS, WI 04/06/1994 07/06/1994 3 USGS 04072015 DUCK CREEK AT FRITSCH ROAD NEAR FREEDOM, WI 05/17/1989 05/17/1989 1 USGS 04072016 DUCK CREEK AT MURPHY CORNER, WI 04/06/1994 08/27/2004 5 USGS 04072021 DUCK CREEK TRIBUTARY NEAR MACKVILLE, WI 04/06/1994 06/28/1994 2 USGS 04072024 DUCK CREEK AT VINE ROAD NEAR FREEDOM, WI 05/10/1989 08/09/1989 3 USGS 04072028 DUCK CREEK AT CNTY TRUNK HIGHWAY S NR FREEDOM, WI 07/11/1995 07/11/1995 1 USGS 04072029 DUCK CREEK AT FREEDOM, WI 10/08/1980 10/08/1980 1 USGS 040720305 DUCK CREEK 0.3 MI DS FREEDOM STP NEAR FREEDOM, WI 07/26/1988 08/09/1989 5 USGS 04072031 DUCK CREEK NEAR FREEDOM, WI 04/06/1994 08/27/1999 8 USGS 04072033 DUCK CREEK AT COUNTY HIGHWAY J NEAR FREEDOM, WI 05/17/1989 05/17/1989 1 USGS 04072036 DUCK CREEK AT HILLSIDE PARK NEAR ONEIDA, WI 07/26/1988 08/09/1989 5 USGS 04072042 DUCK CREEK AT COUNTY HIGHWAY EE NEAR ONEIDA, WI 05/17/1989 05/17/1989 1 USGS 04072043 DUCK CREEK ABOVE FISH CREEK ROAD NEAR ONEIDA, WI 01/16/1986 01/16/1986 1 USGS 040720432 DUCK CREEK AT FISH CREEK ROAD NEAR ONEIDA, WI 07/27/1988 08/09/1989 5 USGS 040720445 DUCK CREEK TRIBUTARY AT RANCH ROAD NEAR ONEIDA, WI 05/16/1989 06/28/1994 3 USGS 04072050 DUCK CREEK AT SEMINARY ROAD NEAR ONEIDA, WI 10/08/1980 10/20/2004 161 USGS 04072051 DUCK CREEK 0.7 MI DS 2ND RIDGE RD NEAR ONEIDA, WI 05/16/1989 05/16/1989 1 USGS 04072053 DUCK CREEK 0.5 MI US HWY 54 BRIDGE NEAR ONEIDA, WI 07/28/1988 08/08/1989 4 USGS 040720555 DUCK CREEK TRIBUTARY AT ONEIDA, WI 07/28/1988 07/28/1988 1 USGS 04072058 DUCK CREEK 0.25 MI DS HW 54 BRIDGE NEAR ONEIDA, WI 07/28/1988 08/10/1989 2 USGS 04072060 DUCK CREEK AT OVERLAND ROAD NEAR ONEIDA, WI 10/08/1980 08/08/1989 6 USGS 04072150 DUCK CREEK NEAR HOWARD, WI 08/12/1969 05/30/2007 768 USGS 04072217 DUCK CREEK SITE 1 NR PAMPERIN PARK AT GREEN BAY,WI 09/21/1988 08/27/1999 7 USGS 04072218 DUCK CREEK AT GREEN BAY, WI 10/08/1970 10/08/1970 1 USGS 5426300 DUCK CREEK NEAR SULLIVAN, WI 11/27/1967 11/27/1967 1 USGS 443042088101201 DUCK CREEK E 08/27/1982 08/27/1982 1 USGS 443124088084801 DUCK CREEK TC 08/27/1982 08/27/1982 1 USGS 443201088074501 DUCK CREEK B 08/27/1982 08/27/1982 1 USGS 443242088060901 DUCK CREEK A 08/27/1982 08/27/1982 1 USGS 04072050: Parameter, units Average Min Max Count Dissolved oxygen, water, unfiltered, milligrams per liter 9.50 1.2 16.7 125 Orthophosphate, water, filtered, milligrams per liter 0.44 0.092 1.44 113 Phosphorus, water, unfiltered, milligrams per liter 0.22 0.05 0.62 113 Phosphorus, water, filtered, milligrams per liter 0.16 0.03 0.49 63 Suspended sediment concentration, milligrams per liter 68.9 2 378 107 Suspended sediment discharge, tons per day 22.6 0.01 715 107 University of Wisconsin, Green Bay – Lower Fox River Watershed Monitoring Program summary of data: 2004 & 2005 annual summaries of discrete samples and daily USGS data (Mean daily discharge, Suspended Sediment Load, Total Phosphorous Load) available at: http://www.uwgb.edu/watershed/data/index.htm Stream Monitoring Sondes: UW-Milwaukee also installed YSI monitoring sondes at each of the 4 USGS monitoring stations to continuously record stage height, turbidity, conductivity, temperature, pH, and dissolved oxygen. The following links are Microsoft Excel files containing the 2003 and 2005 daily summary data for each sonde, which have been post-calibrated: http://www.uwgb.edu/watershed/data/UWM.htm |