| 2008 Impaired Waters Documentation Sheet | Date Prepared _10/2/2007_____________________________________________ |
| --- | --- |
| Author _Erin Hanson___________________________________________________ |
| Waterbody Name _Garners Creek__________________________________________ | Watershed_LF03 – Plum & Kankapot Creeks___ |
| WADRS ID | 10845 _____________ | WBIC _127700__________________ | Lower Fox |
| Choose One: |
| _X_____ | Proposed 303d List Change (new water, delisting, new pollutants) |
| _______ | General 303d Documentation |
| TMDL/303D Listing Proposal |
| 0________ | Start Mile | 5________ | End Mile | _5_____ | Size (Miles/Acres) |
| Current Assessment: |
| _________ | Current Fish & Aquatic Life (Aquatic Community) Use ___________________________________________________________________ |
| _________ | Attainable Fish & Aquatic Life (Aquatic Community) Use_WWSF___________________________________________________________ |
| _________ | Designated Fish & Aquatic Life Use__________________________________________________________________________________ |
| _________ | Supporting Attainable Use = fully, partially, not meeting _NOT ASSESSED___________________________________________________ |
| _________ | Does a Specific Fish Advisory Exist? (Yes/No) |
|  | ________ | If so, what is the advice? |
| Pollutants & Impairments |
| X________ | Impairments (Circle One or More) |
|  | Degraded habitat - NEW | Acute Toxicity | Chronic Toxicity | Temperature (Water) |
|  | Contaminated Fish Tissue | Eutrophication | Excessive Aquatic Plant Growth |
|  | Aquatic Invasives (AIS) Infestation |  | Dissolved Oxygen, Low |
|  | Other ______________________________________________________________________ |
| _X_______ | Pollutants (Circle One or More) |  |
|  | Total Phosphorus - NEW | Sediment - NEW | PCBs | PAHs | Creosote |
|  | NH3 (Ammonia) | Runoff Water (elevated temperatures) | Other _____________________________ |
|  | Other ______________________________________________________________________ |
| ________ | Assessment Level (monitored site specific data less than 5 years old) versus evaluated (other) |
| ________ | DNR Category (3, 4d (recommended), 5a, 5b, 5c) |
| Monitoring and Listing |
| ________ | Water Quality Exceedances (As applicable) Dissolved Oxygen below 5 mg/l “several times” fall 1998, see memo below by Scott Szymanski Dec. 1998 (WDNR) |
| _X_______ | Assessment Parameters (M-IBI, FISH IBI, HBI) HBI max 10, data in SWIMS: Station 10015871 average = 5.65 (1997) indicating “fair” water quality rating with “fairly significant” degree of organic pollution Station 10016542 average = 7.05 (1992) indicating “fairly poor” water quality rating with “significant” degree of organic pollution |
| Stations/Dates/Metric/Scores ____________________________________________________________________________________ |
| Stations/Dates/Metric/Scores ____________________________________________________________________________________ |
| Attach any additional reports, analyses, etc. (Use Designation Survey, etc.) |
| Data in SWIMS: See map named 0410000.pdf for sample station locations. Station 10016542 - GARNERS CREEK - BROOKHAVEN DR. - 500 FEET DOWN-STREAM JUST EAST OF CTH N AND NORTH OFCTH CE Station 10015871 - GARNERS CREEK - HARTJES RD. Station 453277 - GARNERS CREEK - @ PARK, 13 dates from 2004-2006 Macroinvertebrate Data: Parameter Station ID Average Min Max Count HBI Max 10 10015871 5.652 5.512 5.792 2 10016542 7.0515 6.532 7.571 2 INDEX OF BIOTIC INTEGRITY (IBI) 10015871 3.376085 3.09772 3.65445 2 10016542 3.85414 2.62753 5.08075 2 Selected water quality parameters for Station 453277: Parameter Average Min Max Count ALKALINITY TOTAL CACO3, MG/L 224.3 0 270 15 CONDUCTIVITY AT 25C, UMHOS/CM 1259.4 0 2140 15 TEMPERATURE FIELD, deg C 22.9 1 CHLORIDE, MG/L 207.1 0 516 15 NITROGEN NH3-N DISS, MG/L 0.041 1 PH LAB, SU 8.0 0 8.37 15 Data from Jim Reyburn, Wisconsin DNR Green Bay, Personal Files: 1992-1999 Flow Tot-P Tot-P Tot-P Susp. Solids Susp.Solids Susp. Solids Ammonia cfs mg/l lb/day lb/sq mi mg/l lb/day lb/sq mi mg/l Average for all 8.69 0.256 17 1.49 109 10268 909 0.110 n=23 Average low flow 0.76 0.109 0.4 0.04 22 126 11 0.086 n=11 Average event 17.42 0.391 35 3.10 188 21424 1896 0.118 n=12 Data from USGS: USGS 04084468: GARNERS CREEK AT PARK STREET AT KAUKAUNA, WI, 2004-02-10 through 2006-07-27, N=25 Parameter, units Average Min Max Count Temperature, water, degrees Celsius 17.025 14.7 21.7 4 Dissolved oxygen, water, unfiltered, milligrams per liter 8.6 7.8 10.1 3 Total nitrogen (nitrate + nitrite + ammonia + organic-N), water, unfiltered, analytically determined, mg/l 1.49 0.76 2.22 2 Ammonia, water, filtered, milligrams per liter as nitrogen 0.040 0.04 0.041 3 Nitrite plus nitrate, water, filtered, milligrams per liter as nitrogen 0.94 0.34 1.54 2 Orthophosphate, water, filtered, milligrams per liter 0.089 0.034 0.144 2 Phosphorus, water, unfiltered, milligrams per liter 0.0945 0.082 0.107 2 Suspended sediment concentration, milligrams per liter 143.5 80 207 2 Suspended sediment discharge, tons per day 1.22 0.24 2.2 2 Other Data: memo by Scott Szymanski Dec. 1998 (WDNR) in NER Central Files, Green Bay |