| 2008 Impaired Waters Documentation Sheet | Date Prepared :10/2/2007 |
| --- | --- |
| Author: Scott Provost |
| Waterbody Name: Peppermill Creek | Watershed Neenah Creek (UF-14) |
| WADRS ID | 10021850 | WBIC: 178400 | Upper Fox River Basin |
| Choose One: |
| __X_ | Proposed 303d List Change (new water, delisting, new pollutants) DE-LISTING |
| ______ | General 303d Documentation |
| TMDL/303D Listing Proposal |
| Start Mile | 0 | End Mile | 0.75 | Lake Acres: Detail: |
| Current Assessment: |
|  | Current Fish & Aquatic Life (Aquatic Community) Use: COLD (Currently listed use is WWFF) |
|  | Attainable Fish & Aquatic Life (Aquatic Community) Use: COLD |
|  | Designated Fish & Aquatic Life Use: DEF |
|  | Supporting Attainable Use = [fully, partially, not meeting]: Fully |
|  | Does a Specific Fish Advisory Exist? (Yes/No/I don’t know) No |
|  | If so, what is the advice? N/A |
| Pollutants & Impairments |
| Impairments (Circle One or highlight in RED one or more) |
| Degraded habitat | Acute OR Chronic Toxicity | Temperature (Water) |
| Contaminated Fish Tissue | Eutrophication | Excessive Aquatic Plant Growth |
| Aquatic Invasives (AIS) Infestation | Dissolved Oxygen, Low |
| Other ______________________________________________________________________ |
| Pollutants (Circle One or highlight in RED one or more) |
| Total Phosphorus | Sediment | PCBs | PAHs | Creosote |
| NH3 (Ammonia) | Runoff Water (elevated temperatures) | Other: |
| Is this information based on: ___X__Monitoring data (specific data) less than 5 years old OR _____Evaluated [Data more then 5 years old] |
| Cause of Impairment: |
| The Upper Fox River Basin Plan identifies the potential use of Peppermill Creek as COLD and existing use as WWFF. A fish survey in 2007 captured salmonid species, with other salmonids observed upstream. Hydraulic modification (HM) is listed as a source of a problem and Temperature and Migration as impacts. These factors are NOT controllable in this stream segment. There are two authorized dams on this two mile reach which are operational and function properly. There is one instance of a road culvert on 1st lane that is currently plugged via boulders. This can be easily removed, which will restore flow in the reach and remove the unauthorized HM. This stream is currently meeting its potential use and should not be included on the 303d list. A fish IBI survey was completed downstream of 1st Lane and macroinvertebrates will be sampled this fall. Due to the fact that salmonids were found and that the HM is authorized, the stream is currently meeting its potential use. The watershed table also lists NPS as a problem. Currently the watershed land use is comprised chiefly of forests and grassland. Agriculture has decreased over time to only to be 20% (478.4 acres out of the 2350.4 total land area) of the total current land use. There were no obvious NPS issues observed thus it is unlikely NPS is a significant problem. Habitat and sedimentation is listed as an impact associated with NPS. There has been trout habitat restoration completed downstream of 1st lane, and other habitat is affected by the presence of dams, which as described earlier, are uncontrollable. |

Sources of Impairment:

Source: NPS, HM * Impact: Hab, Sed, Temp, Mig* * as listed in the watershed table

Monitoring and Listing

List any Water Quality Excursions (explain):

1. Monitoring Study, Date, Results:09/19/2007 Stations: Confluence with Neenah Creek upstream to bridge Parameters: FISH IBI (results available in FH database) Database where Data is Stored (Fish DB, SWIMS, FishSED, Personal PC,: Not yet entered 2. Monitoring Study, Date, Results: Fall 2007 Stations: Same station Parameters: Macroinvertebrates HBI Database where Data is Stored (Fish DB, SWIMS, FishSED, Personal PC,: Will be entered in database via UWSP Data not available at this time 3. Monitoring Study, Date, Results: Stations: Parameters: Database where Data is Stored (Fish DB, SWIMS, FishSED, Personal PC,: Additional Comments:

List and Attach any additional reports, analyses, etc. (Use Designation Survey, etc.)