| 2008 Impaired Waters Documentation Sheet |
| --- |
| Author: Erin Hanson | Date Prepared: 1/15/2008 |
| Waterbody Name: Lower Fox River Seg 1 (1) | Watershed Code and Name: LF03, LF04, LF06, WATE |
| WADRS ID: 357364 | WBIC: 117900 | If you don’t know the ID numbers, go to i-SWDV (CRTL + Click) to find them. |
| Choose from the following to indicate what you are recommending: |
| _____ Proposed new listing |
| _____ Proposed for special project monitoring (need more data) |
| _____ Proposed changes for water already on 303(d) list (check type of change below) ( TMDL ID Number: _______ |
|  | _____ Proposed change to existing list (new pollutants, impairments, mileages, etc.) |
|  | _____ Proposed for de-listing ( a report may be needed depending on the reasons) |
|  | __X___ General 303d documentation for water already on list |
| Description of waterbody segment |
| Start Mile: _32.18 ___________ End Mile: _40.09 ___________ Total miles: 7.91 ____________ Lake Acres: ____________ | Detail (describe segment using road crossings, convergence with other waterbodies, etc.): Appleton Dam to Lake Winnebago outlet (Neenah Channel). |
| Use Designation Categories | List use designation & data source for each category. |
| Current (Existing) Fish & Aquatic Life Use: (Aquatic Community) | Unknown (WATERS) |
| Attainable (Potential) Fish & Aquatic Life Use: (Aquatic Community) | Unknown (WATERS) |
| Designated (Codified) Fish & Aquatic Life Use: | Default (WATERS) |
| Is it supporting its Attainable Use? _____ Fully supporting _____ Partially supporting __x___ Not supporting Does a Specific Fish Advisory Exist? (This is different from the statewide mercury advisory.) _x__ Yes ____ No ___ Don’t know If so, what is the specific advisory: PCB |
| Pollutants & Impairments Pollutants (Place an X next to all pollutants that you are recommending for listing, de-listing or monitoring needs. If you are recommending adding a new pollutant to a waterbody that is already on the list, write ADD.) |
| __X__ Phosphorus | _____ Sediment | _____ Bacteria | _____ PAHs | __X__ PCBs |
| _____ NH3 (Ammonia) | _____ Thermal (elevated temp.) | _____ Hg | _____ Creosote | _____ Metals |
| Other Pollutants: Drop Hg as a pollutant in WATERS. This is an error confirmed by Candy. Never on the 303(d) list for Hg. |
| Impairments (Place an X next to all impairments that you are recommending for listing, delisting, or monitoring needs. If you are recommending adding a new pollutant to a waterbody that is already on the list, write ADD. ) |
| _____ Degraded Habitat | _____ Eutrophication | _____ Temperature |
| __X__ Contaminated Fish Tissue | _____ Chronic Toxicity | _____ Aquatic Toxicity |
| ___X__ Low Dissolved Oxygen | _____ Aquatic Invasives |  |
| Other Impairments: |
| Source of impairment (Place an X next to the source category.) if you need an explanation of source categories., see http://dnr.wi.gov/org/water/wm/wqs/303d/categories.html . |
| _____ NPS Dominated | _____ NPS/Pt. Source Blend | _____ Point Source |
| _____ Contaminated Sediment | _____ Atmospheric Deposition | _____ Physical Habitat |
| _____ Unknown | Other: _____________________________ |
| Specific causes of impairment (Describe to the best of your ability what you think is contributing to the impairment.) NOTE: “WATERS incorrectly lists Hg as a pollutant for FCA and this is not correct. It does not appear on the 303(d) list for Hg. The version of these sheets in the W:\\watershed on 'central'\303(d)list\Central_Office_Docsheets has this noted Since it did not appear on the 2006 list, this is a DNR internal correction only.” Email from Carolyn Betz, 1/13/2008 |
| Information is based on: ____ Monitoring data (specific data) less than 5 years old ____ Evaluated data (data more than 5 years old) |
| Map |
| Monitoring & Listing Data 1. Monitoring Study, Date, Results. List water quality exceedences indicating magnitude, duration and frequency. Stations: Station 718248 - LITTLE LAKE BUTTE DES MORTS - SW CORNER, 10/13/1998 Parameters: Macroinvertebrate HBI max 10: Station 718248 = 5.64, 10/13/1998, data in SWIMS No data for fish Warmwater IBI or habitat rating in WDNR fisheries database Macroinvertebrate data from SWIMS: Parameter Result HBI Max 10 5.64 INDEX OF BIOTIC INTEGRITY (IBI) 4.06 SHANNON'S DIVERSITY INDEX 3.02 SPECIES RICHNESS 26 Database where data is stored (Fish Database, SWIMS, FishSED, Personal PC): SWIMS |
| 2. Monitoring Study, Date, Results. List water quality exceedences indicating magnitude, duration and frequency. Database where data is stored (Fish Database, SWIMS, FishSED, Personal PC): SWIMS SWIMS Sample Station Locations: No map of sample stations created. Station ID Station Name Sample Dates 714001 LITTLE BUTTE DES MORTS LAKE 08/01/1979 - 08/01/1979 718248 LITTLE LAKE BUTTE DES MORTS - SW CORNER 10/13/1998 - 10/13/1998 453049 FOX RIVER - NARROWS GRIGNON RAPIDS 09/24/1979 - 09/25/1979 453050 FOX RIVER - ABOVE VULCAN DAM APPLETON 07/06/1975 - 08/29/1988 453106 FOX RIVER – KIMBERLY-CLARK ATLAS MILL 001 04/01/1976 - 01/25/1979 453238 FOX RIVER - AT LUTZ PARK, AT APPLETON, WI 05/02/1989 - 11/17/1992 713057 FOX RIVER - NEENAH CHANNEL AT OAK ST 08/29/1988 - 08/29/1988 713062 FOX RIVER - LITTLE LAKE BUTTE D MRTS RR BRIDGE 08/31/1976 - 09/25/1979 713063 FOX RIVER - MIDDLE LIT LK BUTTE D MRTS 08/05/1998 - 09/20/1999 713064 FOX RIVER - STROBE ISLAND POWER LINES 08/31/1976 - 08/31/1976 713091 FOX RIVER – KIMBERLY-CLARK CORP LAKEVIEW 001 04/24/1978 - 07/30/1984 713092 FOX RIVER – KIMBERLY-CLARK CORP LAKEVIEW 003 03/24/1977 - 03/24/1977 713093 FOX RIVER – KIMBERLY-CLARK CORP LAKEVIEW 004 03/24/1977 - 03/24/1977 713106 LITTLE LAKE BUTTE DES MORTS - BERGSTROM PAPER NEENAH MILL 004 10/06/1975 - 05/09/1984 713107 LITTLE LAKE BUTTE DES MORTS - BERGSTROM PAPER NEENAH MILL 005 10/06/1975 - 10/06/1975 713108 LITTLE LAKE BUTTE DES MORTS - BERGSTROM PAPER NEENAH MILL 006 03/02/1977 - 06/13/1978 713109 LITTLE LAKE BUTTE DES MORTS - BERGSTROM PAPER NEENAH MILL 007 10/06/1975 - 06/13/1978 713241 FOX RIVER - AT STH 114, AT NEENAH, WI 05/02/1989 - 11/17/1992 Selected Water Quality Parameters from SWIMS: Parameter, units Station ID Average Min Max Count DISSOLVED OXYGEN FIELD, mg/l 714001 10.1 1 453049 8.8 7.8 9.8 2 453050 18.8375 5.8 92 8 713057 102 1 713062 9.325 7.1 10.6 4 713063 9.7125 8.8 11.7 8 713064 7.7 1 PHOSPHATE ORTHO DISS, mg/l 714001 0.06 1 453049 0.024 1 453050 0.0205 0.006 0.03 4 453238 0.0075556 0 0.023 27 713057 0.03 1 713062 0.024 0.005 0.043 2 713063 0.0088333 0 0.019 12 713091 0.0046 0.004 0.007 5 713106 0.2931429 0.007 0.78 7 713241 0.0081905 0.002 0.039 21 RESIDUE TOTAL NFLT (TOTAL SUSPENDED SOLIDS), mg/l 453049 30 1 453050 93.8 28 360 6 453106 3 3 3 3 453238 24.2 4 44 17 713057 190 1 713062 23 14 32 2 713063 3.2 0 33 12 713091 488.2 1 656 5 713092 10 1 713093 31 1 713106 595.1 10 3520 45 713107 12 1 713108 30.5 15 46 2 713109 6.7 2 12 3 713241 15.2 0 36 21 |
| 3. Monitoring Study, Date, Results. List water quality exceedences indicating magnitude, duration and frequency. Data from USGS: Sample Stations listed below, no map created. Site ID Site Name Sample Dates 4084413 FOX RIVER AT STATE HIGHWAY 114 AT NEENAH, WI 12/17/1987 - 03/15/1988 4084445 FOX RIVER AT APPLETON, WI 07/02/1986 - 11/17/1992 40844126 FOX RIVER MENASHA CHANNEL AT MENASHA, WI 04/18/1989 - 09/26/1990 40844128 FOX RIVER NEENAH CHANNEL AT NEENAH, WI 04/18/1989 - 11/17/1992 Selected water quality parameters for USGS stations listed below: Parameter Site ID Average Min Max Count Dissolved oxygen, water, unfiltered, mg/l 4084445 11.4 6.9 16.1 35 40844128 13.9 1 Orthophosphate, water, filtered, milligrams per liter 4084445 0.02 0.006 0.071 29 Suspended sediment concentration, milligrams per liter 4084445 21.2 0 262 2597 40844126 14.4 2 52 8 40844128 40.9 2 360 12 Suspended sediment discharge, tons per day 4084445 230.3 0 5800 1182 40844126 85.2 6.6 166 7 40844128 81.0 7.6 410 11 |
| Additional Comments: Data from other sources: Scheberle, D., H.J. Harris, M. Finney, J. Potter, S. Oldenburg, P. Dessart. no date. Toward a Total Maximum Daily Load (TMDL) for Phosphorus and Suspended Solids: The Lower Fox River Basin and Green Bay Area of Concern “According to the WDNR 303 (d) list, the water quality of Lower Green Bay and the Fox River is impaired due to phosphorus and PCBs (WDNR, 2005). Phosphorus and TSS are the pollutants of concern for this framework. Even though suspended solids are not listed as a pollutant that impairs designated uses for the lower Fox River and the bay, ample research demonstrates that both TSS and phosphorous affect water quality (Harris, 1993; Millard & Sager, 1994).” p. 18 “Suspended solids loading into the AOC and Green Bay have also been estimated through monitoring (SDATF, 2002) and modeling (Baumgart, 2005). The average monitoring SS load at the mouth of the Fox River for water years 1995-1999 was 119,400 mt/yr-1 (Table 2b). This amounts to 327 metric tons per day in an average year. With the addition of the point sources, the estimated contribution from Lake Winnebago, and the estimated autogenic solids contribution from the river (WDNR, 2001), the simulated 1989-2000 suspended sediment load at the Fox River outlet to Green Bay is 119,000 mt/yr-1 (Baumgart, 2005). p. 31“ Contaminated Sediments: Excerpt from: “Draft Studies Completed on Cleanup of PCBs in Lower Fox River Sediments” WDNR Summary Fact Sheet 3/1999 Available at: http://dnr.wi.gov/org/water/wm/foxriver/documents/rifs/foxrivercleanup.pdf “As many as 360 different chemicals have been found in the water, sediments, fish and wildlife of the Lower Fox River. These chemicals include PCBs, dioxins, furans, mercury, ammonia, DDT and other pesticides (see table on page 6 for more information on these chemicals). The Lower Fox River, which flows northeast for about 39 miles from Lake Winnebago at Neenah-Menasha to the river’s mouth at Green Bay, contributes more PCBs to Green Bay and Lake Michigan than any other source…. An estimated 63,000 pounds of the PCBs previously discharged remain in the Lower Fox River. Most of them are downstream of the De Pere dam. An even larger quantity has passed through the Lower Fox River to Green Bay, Lake Michigan and beyond. Results of the intensive “Mass Balance” study conducted by the DNR and EPA in 1989 showed that about 160,000 pounds of PCBs have already found their way into Green Bay from the Lower Fox. It also showed that about 620 pounds of PCBs enter the bay from the river each year.” p. 2 & Figures below p. 3 Excerpts from “Remedial Investigation Report Lower Fox River and Green Bay Wisconsin” prepared for WDNR by The RETEC Group, Inc. 12/2002 “The results are summarized below and indicate that the De Pere to Green Bay Reach and Green Bay Zone 2, combined, contain almost 60 percent of the total PCB mass in the system in less than 10 percent of the total contaminated sediment volume. The PCB mass and volume of contaminated sediment for each river reach and bay zone are listed below.” P. 7-5 “7.3.2.2 Little Lake Butte des Morts Reach Deposits A through H and POG contain about 1,540 kg (3,395 pounds) of PCBs in about 1.35 million m3 (1.77 million yd3) of sediment with concentrations greater than 50 μg/kg PCB. RI findings for this reach include the following: These deposits cover about 314 hectares (775 acres) and the deposits range up to approximately 1.9 m (6.2 ft) thick. The highest total PCB concentration was 222,722 μg/kg. Upstream deposits A, B, and POG have the highest PCB mass to volume ratios in this reach. These three deposits contain 952 kg (2,100 pounds) of the PCBs in about 252,000 m3 (329,600 yd3) of sediment. Also, about 910 kg (2,000 pounds) of the PCBs in these three deposits is present in the upper 100 cm (3.28 ft) of sediment. Deposit E contains about 454 kg (1,000 pounds) of PCBs. However, the mass to sediment volume ratios for this deposit is much lower than deposits A, B, and POG. Habitat associated with this reach include Stroebe Island, located on the northeast side of Deposit E. The wetlands located between Stroebe Island and the river bank are the largest in-river wetlands in this reach. Also, an eagle nest has been observed in this area. Smaller wetland areas are located in the vicinity of deposits A, C, and POG and SAV are present in the shallow waters nearby, including near Deposit B. Two large areas of cuts/coves are present on the west side of Deposit C and just south of Deposit POG. Most of the shoreline in the LLBdM Reach is characterized as either poor or unsuitable for mink.” p. 7-6 & 7-7 |
| List and Attach any additional reports, analyses etc. including use designation survey. 1. 2. 3. 4. 5. |