| 2008 Impaired Waters Documentation Sheet | Date Prepared 9/11/2007_________________________________________ |
| --- | --- |
| Author Erin Hanson________________________________________ |
| Waterbody Name Mud Creek – Segment 1___________________ | Watershed_Little Lake Butte des Morts______ |
| WADRS ID | _ 10846 ___________ | WBIC _129500____________ | Lower Fox |
| Choose One: |
| X______ | Proposed 303d List Change (new water, delisting, new pollutants) Total Phosphorous - NEW |
| _______ | General 303d Documentation |
| TMDL/303D Listing Proposal |
| 0_ ___ | Start Mile | 3.71_____ | End Mile | 3.71___ | Size (Miles/Acres) |
| Current Assessment: |
| _________ | Current Fish & Aquatic Life (Aquatic Community) Use _unknown________________________________________________________ |
| _________ | Attainable Fish & Aquatic Life (Aquatic Community) Use_unknown_________________________________________________________ |
| _________ | Designated Fish & Aquatic Life Use_default________________________________________________________________________ |
| _________ | Supporting Attainable Use = fully, partially, not meeting _not supporting____________________________________________________ |
| _________ | Does a Specific Fish Advisory Exist? (Yes/No) |
|  | ________ | If so, what is the advice? |
| Pollutants & Impairments |
| _X_______ | Impairments (Circle One or More) |
|  | Degraded habitat | Acute Toxicity | Chronic Toxicity | Temperature (Water) |
|  | Contaminated Fish Tissue | Eutrophication | Excessive Aquatic Plant Growth |
|  | Aquatic Invasives (AIS) Infestation |  | Dissolved Oxygen, Low |
|  | Other ______________________________________________________________________ |
| X________ | Pollutants (Circle One or More) |  |
|  | Total Phosphorus - NEW | Sediment | PCBs | PAHs | Creosote |
|  | NH3 (Ammonia) | Runoff Water (elevated temperatures) | Other _____________________________ |
|  | Other ______________________________________________________________________ |
| ________ | Assessment Level (monitored site specific data less than 5 years old) versus evaluated (other) |
| ________ | DNR Category (3, 4d (recommended), 5a, 5b, 5c) |
| Monitoring and Listing |
| X________ | Water Quality Exceedances (As applicable) Dissolved Oxygen < 5 mg/l: Station 453246 = 2.68 mg/l on 10/21/1999 |
| X________ | Assessment Parameters (M-IBI, FISH IBI, HBI) All for Station 10011423 Macroinvertebrate HBI max 10: 5.613 – 7.022 (n=5) “fair – fairly poor” water quality rating & “fairly significant – significant” degree of organic pollution (Lillie et al 2003), data in SWIMS summary table below Habitat score small streams = 55, Habitat rating “good” (7/29/2004), Warmwater IBI Integrity Rating “very poor” (8/19/2004), data in WDNR fisheries database |
| Stations/Dates/Metric/Scores ____________________________________________________________________________________ |
| Stations/Dates/Metric/Scores ____________________________________________________________________________________ |
| Attach any additional reports, analyses, etc. (Use Designation Survey, etc.) |
| Data from SWIMS: Station 10011423, MUD CREEK - SPENCER ST: macroinvertebrate data 1992 (2 dates), 1997 (2 dates) & 9/15/2004 DNR Parameter Description Average Min Max Count HBI Max 10 6.385 5.613 7.022 5 INDEX OF BIOTIC INTEGRITY (IBI) 2.900 1.339 4.006 5 Station 453048, MUD CREEK TO FOX R - BUTTE DES MORTS UTIL DIST STP – data from 1979 – 1981, not summarized here Station 453246, MUD CREEK - SPENCER ROAD – water quality data from 3 dates in 1997 Station 453258, MUD CREEK - COUNTY HIGHWAY BB – water quality data 1992 (2 dates), 1997 (8 dates), 6/10/1998 & 1994 (4 dates) Station 10021170, MUD CREEK - AT END OF TIMMER LANE, OUTAGAME COUNTY – water quality data from 08/16/2007 Parameter, units Station ID Average Min Max Count TEMPERATURE FIELD, deg C 10021170 22 1 453246 13.7 5.5 22.6 22 453258 0.6 0.04 1.56 3 DISSOLVED OXYGEN FIELD, mg/l 10021170 8.19 1 453246 9.9 2.68 17.2 21 453258 12.4 11.3 13.23 3 FECAL COLIFORM, MEMBRANE FILTER, MFC AGAR, #/100ml 453246 11470 0 150000 16 453258 30 10 50 2 NITROGEN KJELDAHL TOTAL, mg/l 453246 0.8 0.4 1.2 5 NITROGEN NH3-N DISS, mg/l 10021170 0.055 1 453246 0.152 0 2.19 17 453258 0.215 0.15 0.295 3 NITROGEN NO3+NO2 DISS (AS N), mg/l 10021170 0.11 1 453246 0.446 0.143 1 5 PHOSPHATE ORTHO DISS, mg/l 453246 0.064 0 0.378 22 453258 0.093 0.033 0.21 3 PHOSPHORUS TOTAL, mg/l 0.156 0 0.764 26 10021170 0.075 1 453246 0.164 0 0.764 22 453258 0.108 0 0.29 4 RESIDUE TOTAL NFLT (TOTAL SUSPENDED SOLIDS), mg/l 10021170 5 1 453246 23 0 137 22 453258 5 0 15 3 Data summary provided by James Reyburn, Water Quality Biologist - Lower Fox Basin: WDNR data 1992-1999 Flow Tot-P Tot-P Tot-P Susp. Solids Susp.Solids Susp. Solids Ammonia cfs mg/l lb/day lb/sq mi mg/l lb/day lb/sq mi mg/l Average for all 21.80 0.169 23 2.25 31 6489 624 0.163 n=23 Average low flow 2.62 0.145 1.8 0.17 11 126 12 0.253 n=12 Average event 47.38 0.214 52 5.03 53 14972 1440 0.079 n=11 Data from USGS: USGS 04084429 MUD CREEK AT SPENCER ROAD AT APPLETON, WI – water quality data for 11/12/2003, 2004 (6 dates) & 7/27/2006 Parameter, units Average Min Max Count Temperature, water, degrees Celsius 12.3 -0.2 21.7 7 Dissolved oxygen, water, unfiltered, mg/l 10.3 6.8 15.8 7 Ammonia, water, filtered, mg/l as NH4 0.115 0.05 0.27 4 Ammonia, water, filtered, mg/l as nitrogen 0.070 0.04 0.21 7 Nitrate, water, filtered, mg/l 2.419 0.403 3.64 6 Nitrate, water, filtered, mg/l as nitrogen 0.545 0.09 0.82 6 Nitrite plus nitrate, water, filtered, mg/l as nitrogen 0.563 0.11 0.84 6 Nitrite, water, filtered, mg/l 0.057 0.036 0.076 6 Nitrite, water, filtered, mg/l 0.017 0.011 0.023 6 Organic nitrogen, water, unfiltered, mg/l 0.493 0.26 0.62 3 Phosphorus, water, unfiltered, mg/l 0.098 0.052 0.188 6 Orthophosphate, water, filtered, mg/l 0.133 0.058 0.297 5 Orthophosphate, water, filtered, mg/l as phosphorus 0.037 0.006 0.097 6 Suspended sediment concentration, mg/l 130.833 89 170 6 Suspended sediment discharge, tons per day 2.593 0.46 6 6 Other sources: Baumgart, P. January, 2005. Lower Green Bay and Lower Fox Tributary Modeling Report: Source allocation of suspended sediment and phosphorus loads to Green Bay from the Lower Fox River Subbasin Using the Soil and Water Assessment Tool. “ Mean and median concentrations of TSS from samples collected by the WDNR (Northeast Region, unpublished watershed monitoring data 1997 to 2002) from LF03 watersheds such as Plum, Kankapot and Garners Creeks were all at least twice as high as those from Mud Creek, which is a subwatershed of LF04… In addition, phosphorus concentrations from LF03 watersheds Plum and Kankapot Creeks were all at least four times higher than those from Mud Creek (Mud Cr. phosphorus: mean = 0.17 mg/L, median = 0.11 mg/L, n=23). |