| 2008 Impaired Waters Documentation Sheet |
| --- |
| Author: Matt Aho and Marsha Burzynski | Date Prepared: November 7, 2009 |
| Waterbody Name: North Branch Pike River | Watershed Code and Name: Pike River (SE02) |
| WADRS ID: 10532 | WBIC: 1900 | If you don’t know the ID numbers, go to i-SWDV (CRTL + Click) to find them. |
| Choose from the following to indicate what you are recommending: |
| _____ Proposed new listing |
| _____ Proposed for special project monitoring (need more data) |
| _____ Proposed changes for water already on 303(d) list (check type of change below) ( TMDL ID Number: ___357____ |
|  | __X___ Proposed change to existing list (new pollutants, impairments, mileages, etc.) |
|  | ___ __ Proposed for de-listing ( a report may be needed depending on the reasons) |
|  | __X__ General 303d documentation for water already on list |
| Description of waterbody segment |
| Start Mile: _____0_______ End Mile: _____5.23____ Total miles: _____5.23____ Lake Acres: ____________ | Detail (describe segment using road crossings, convergence with other waterbodies, etc.): The listed segment is located in two counties. The mouth is located in Kenosha County and contains about 25% of the listed mileage. About 75% of the listed mileage is located in Racine County. |
| Use Designation Categories | List use designation & data source for each category. |
| Current (Existing) Fish & Aquatic Life Use: (Aquatic Community) | WWSF |
| Attainable (Potential) Fish & Aquatic Life Use: (Aquatic Community) | WWSF |
| Designated (Codified) Fish & Aquatic Life Use: | *Special variance for MFFCC and D.O., DEF for rest. See note under additional comments. |
| Is it supporting its Attainable Use? _____ Fully supporting __X___ Partially supporting _____ Not supporting Does a Specific Fish Advisory Exist? (This is different from the statewide mercury advisory.) ___ Yes __X__ No ___ Don’t know If so, what is the specific advisory: |
| Pollutants & Impairments Pollutants (Place an X next to all pollutants that you are recommending for listing, de-listing or monitoring needs. If you are recommending adding a new pollutant to a waterbody that is already on the list, write ADD.) |
| _____ Phosphorus | __ADD___ Sediment | _____ Bacteria | _____ PAHs | _____ PCBs |
| _____ NH3 (Ammonia) | _____ Thermal (elevated temp.) | _____ Hg | _____ Creosote | _____ Metals |
| Other Pollutants: historical acute toxicity (chlorine suspected) to N. Branch as a result of discharge from Waxdale Creek (tributary) |
| Impairments (Place an X next to all impairments that you are recommending for listing, delisting, or monitoring needs. If you are recommending adding a new pollutant to a waterbody that is already on the list, write ADD. ) |
| __ADD___ Degraded Habitat | _____ Eutrophication | _____ Temperature |
| _____ Contaminated Fish Tissue | _____ Chronic Toxicity | ___REMOVE__ Aquatic Toxicity |
| _____ Low Dissolved Oxygen | _____ Aquatic Invasives | Other Impairments: fish kills prior to 1990 (DELIST FOR FISH KILLS) |
| Source of impairment (Place an X next to the source category.) if you need an explanation of source categories., see http://dnr.wi.gov/org/water/wm/wqs/303d/categories.html . |
| _____ NPS Dominated | ___X__ NPS/Pt. Source Blend | _____ Point Source |
| _____ Contaminated Sediment | _____ Atmospheric Deposition | __X___ Physical Habitat |
| _____ Unknown | Other: _____________________________ |
| Specific causes of impairment (Describe to the best of your ability what you think is contributing to the impairment.) Degraded Habitat caused by stream channelization, debrushing of streambanks, draining of wetlands, sedimentation from runoff and increased stormwater drainage due to expanding development within the watershed. Fish kills attributed to potential chlorine discharges to Waxdale Creek, which affected the North Branch Pike River downstream from confluence with Waxdale Creek. No fish kills have been documented on the North Branch Pike River since 1990. |
| Information is based on: ____ Monitoring data (specific data) less than 5 years old __X__ Evaluated data (data more than 5 years old) |
| Map When possible, please create a map of your waterbody and submit it with this form. It is easy to create a 8.5 x 11 map of the area you are describing. Go to the go to the Intranet Surface Water Viewer i-SWDV (CRTL + Click). Choose “Find Location” to find the waterbody, then “Layers” to choose “Standards, Monitoring and Assessment”. If it is already on the 303(d) list, then click “Impaired Waters 303d". If you want to show the monitoring stations, also click on "SWIMS Station Points". Then choose “Print” (this will create a pdf map), add a title under "Map Title" and your name and date under “Map Notes", click "OK" and then "Open Map" at the next screen. Save the file and attach it when you send in this sheet. For additional help on how to make a map, check out page 12-14 on the website http://www.dnr.state.wi.us/org/water/SWDV/help/documents/SWDV_Basic_User_Guide_%209_07.pdf |
| Monitoring & Listing Data 1. Monitoring Study, Date, Results. List water quality exceedences indicating magnitude, duration and frequency. Water Quality Standards Review and Stream Classification for the North Branch of the Pike River, Pike River Watershed, Kenosha County, Wisconsin (T. Burzynski, 1993). Document attached. Stations: State Hwy 20 upstream to culvert at Knights Inn; 2. Upstream of culvert at Knights Inn to culvert at Mariner Road. Parameters: water temp, D.O., fish community, habitat, recreational use Database where data is stored (Fish Database, SWIMS, FishSED, Personal PC): Scanned stream classification document attached. Data located in North Branch Pike River File at Sturtevant Service Center. |
| 2. Monitoring Study, Date, Results. List water quality exceedences indicating magnitude, duration and frequency. Sampling of the North Branch of the Pike River, the Pike River, and the South Branch of the Pike River, Racine County and Kenosha County, by Fish Research Personnel During June, 1990. P. Kanehl and J. Lyons, October 1990. Stations: 1) mile 0.76; 2) mile 2.64; 3) mile 3.6 Parameters: Fish community and IBI, Habitat characteristics Database where data is stored (Fish Database, SWIMS, FishSED, Personal PC): Scanned report attached. Hard copy of report and raw data located in North Branch Pike River file at Sturtevant Service Center. |
| 3. Monitoring Study, Date, Results. List water quality exceedances indicating magnitude, duration and frequency. Basin Assessment Monitoring, 08/01/1996-10/30/1996 Stations: SWIMS Stations 523147, 303062 Parameters: water chemistry, fecal coliform Database where data is stored (Fish Database, SWIMS, FishSED, Personal PC): SWIMS |
| 4. Monitoring Study, Date, Results. List water quality exceedances indicating magnitude, duration and frequency. Macroinvertebrate Monitoring at four stations. Dates listed with stations below. Stations: SWIMS stations 523148 (10/18/1979); 523184 (10/17/1996); 10008155 (11/02/1999); 303062 (10/17/1996) Parameters: macroinvertebrate community and metrics Database where data is stored (Fish Database, SWIMS, FishSED, Personal PC): SWIMS |
| 5. Monitoring Study, Date, Results. List water quality exceedances indicating magnitude, duration and frequency. Nonpoint Source Nutrient Monitoring, 5/25/2001 Stations: 523147 Parameters: nutrient series Database where data is stored (Fish Database, SWIMS, FishSED, Personal PC): SWIMS |
| Additional Comments: *The portion of the North Branch Pike River in Racine County is listed in NR 104.06(2)(a)4 as a special variance stream. However, the mouth of the N. Branch Pike River is located in Kenosha County. Stream classification reports from 1992 (S. Mace) and 1993 (T. Burzynski) state that the North Branch of the Pike River is best classified as a warmwater sport fish community for its entire length. M. Burzynski contacted Jim Schmidt from the Water Evaluation Section, on October 16, 2007 to determine how to best interpret the information. Jim noted that the Pike River in Racine County must meet fish and aquatic life uses with the exception of the special variance for dissolved oxygen and MFFCC bacteria. Therefore, the designated use would reflect the information contained in the stream classifications on file (attached), while effluent limits for dissolved oxygen and MFFCC would be calculated for the special variance within the Racine County Portion. The North Branch of the Pike River (miles 0-5.23) was listed on the impaired waters list for chronic aquatic toxicity with unknown pollutants. Based on review of available data and stream classification documents on file, it is unclear why the North Branch of the Pike River as originally listed for this impairment. Based on review of available information, there is no indication that chronic toxicity was or is a problem on this waterbody. Fish kills were historically reported for Waxdale Creek that affected the North Branch downstream from the confluence. In most cases the agents causing the fish kills were not identified, but this did not lead to a lasting toxicity problem for the North Branch. The stream habitat had been severely degraded, and impaired. Extensive stream channel work has been completed on the Pike River that may have a positive influence on the habitat for the river. We recommend removing the listing for chronic aquatic toxicity for the North Branch of the Pike River, and recommend monitoring to determine if the river has improved in habitat to remove from the list. |
| List and Attach any additional reports, analyses etc. including use designation survey. 1. All reports mentioned in the monitoring and listing section are attached. 2. 3. 4. 5. |