Trega Foods, Ltd. - Luxemburg Facility

WPDES Permit No. WI-0050237

Trega Foods, Ltd. operates a cheese manufacturing and whey processing plant in Kewaunee County, approximately one mile south of State Highway 29 on County Highway AB (formerly State Highway 163), south of Luxemburg.  Process wastewater from cleaning and sanitizing production equipment is treated on-site with a wastewater treatment facility (WWTF), the effluent from which has been regulated as Outfall 003.  The WWTF includes an equalization basin, a pair of aeration basins and a pair of dissolved air flotation (DAF) units to separate solids.  Ferric Chloride is added to precipitate phosphorus, and a proprietary polymer is added to enhance solids removal, ahead of the DAF units.  A small volume of sanitary wastewater is collected and chlorinated before blending with the process wastewater prior to treatment.  NCCW, RO retentate, and “polished” COW water, regulated as Outfall 008, is blended with the treated WWTF effluent prior to discharge to a common outfall structure at approximately Latitude 44º 25' 45" North and Longitude 87º 41' 13" West.  The combined effluent is discharged to an unnamed tributary to the East Twin River, in the “East Twin River Watershed” (TK 02) in the Lakeshore Basin.

# Text boxes

# Approximate

Location of

# Combined Outfall

Plant Site

State Hwy 29