| 2010 Impaired Waters Documentation Sheet |
| --- |
| Author: Mary Gansberg | Date Prepared: 09/17/2009 |
| Waterbody Name: Silver Lake | Watershed Code and Name: MA01-Sevenmile-Silver Creek watershed |
| WADRS ID: | WBIC: 67400 | If you don’t know the ID numbers, go to i-SWDV (CRTL + Click) to find them. |
| Choose from the following to indicate what you are recommending: |
| _____ Proposed new listing |
| ___x__ Proposed changes for water already on 303(d) list (check type of change below) ( TMDL ID Number: _______ |
|  | _____ Proposed change to existing list (new pollutants, impairments, mileages, etc.) |
|  | __x___ Proposed for de-listing ( a report may be needed depending on the reasons) |
|  | _____ General 303d documentation for water already on list |
| Description of waterbody segment |
| Start Mile: ____________ End Mile: ____________ Total miles: ____________ Lake Acres: _____69_______ | Detail (describe segment using road crossings, convergence with other waterbodies, etc.): Entire lake – both east and west basins |
| Use Designation Categories | List use designation & data source for each category. |
| Current (Existing) Fish & Aquatic Life Use: (Aquatic Community) | Deep Seepage |
| Attainable (Potential) Fish & Aquatic Life Use: (Aquatic Community) | Deep Seepage |
| Designated (Codified) Fish & Aquatic Life Use: | Default |
| Is it supporting its Attainable Use? _____ Fully supporting __X__ Supporting _____ Not supporting Does a Specific Fish Advisory Exist? (This is different from the statewide mercury advisory.) ___ Yes __X__ No ___ Don’t know If so, what is the specific advisory: |
| Pollutants & Impairments Pollutants (Place an X next to all pollutants that you are recommending for listing, de-listing or monitoring needs. If you are recommending adding a new pollutant to a waterbody that is already on the list, write ADD.) |
| __REMOVE_ Phosphorus | _____ Sediment | _____ Bacteria | _____ PAHs | _____ PCBs |
| _____ NH3 (Ammonia) | _____ Thermal (elevated temp.) | _____ Hg | _____ Creosote | _____ Metals |
| Other Pollutants: |
| Impairments (Place an X next to all impairments that you are recommending for listing, delisting, or monitoring needs. If you are recommending adding a new pollutant to a waterbody that is already on the list, write ADD. ) |
| _____ Degraded Habitat | _____ Eutrophication | _____ Temperature |
| _____ Contaminated Fish Tissue | _____ Chronic Toxicity | _____ Aquatic Toxicity |
| REMOVE_ Low Dissolved Oxygen | _____ Aquatic Invasives | _REMOVE_ Fish Kill |
| Other Impairments: |
| Source of impairment (Place an X next to the source category.) if you need an explanation of source categories., see http://dnr.wi.gov/org/water/wm/wqs/303d/categories.html . |
| _____ NPS Dominated | REMOVE_____ NPS/Pt. Source Blend | _____ Point Source |
| _____ Contaminated Sediment | _____ Atmospheric Deposition | _____ Physical Habitat |
| _____ Unknown | Other: _____________________________ |
| Specific causes of impairment (Describe to the best of your ability what you think is contributing to the impairment.) |
| Information is based on: Monitoring data (specific data) less than 5 years old (Circle One) YES x NO |
| Map When possible, please create a map of your waterbody and submit it with this form. It is easy to create a 8.5 x 11 map of the area you are describing. Go to the go to the Intranet Surface Water Viewer i-SWDV (CRTL + Click). Choose “Find Location” to find the waterbody, then “Layers” to choose “Standards, Monitoring and Assessment”. If it is already on the 303(d) list, then click “Impaired Waters 303d". If you want to show the monitoring stations, also click on "SWIMS Station Points". Then choose “Print” (this will create a pdf map), add a title under "Map Title" and your name and date under “Map Notes", click "OK" and then "Open Map" at the next screen. Save the file and attach it when you send in this sheet. For additional help on how to make a map, check out page 12-14 on the website http://www.dnr.state.wi.us/org/water/SWDV/help/documents/SWDV_Basic_User_Guide_%209_07.pdf |
| Monitoring & Listing Data 1. Monitoring Study, Date, Results. List water quality exceedences indicating magnitude, duration and frequency. Stations: 363312, 363080 Parameters: Chlorophyll a, total phosphorus, secchi, profiles, fisheries, and aquatic plant surveys. Summer average secchi depth is 3.9 feet based on 32 samples collected between 7/15/2005 and 9/15/2009. The summer average total phosphorus value is 0.034 mg/l based on 25 samples collected between 7/15/2005 and 9/15/2009 (or .035 mg/l based on May-Oct, 2004-2008 standard TP calculation). Average chlorophyll TSI based on Carlson’s TSI calculations is 55, ‘Fair’. Using Wisconsin chlorophyll TSI calculation, TSI-chl is 52 (‘good’), and average TSI-secchi is 58 (‘fair’). These values are below the natural community impairment thresholds for deep seepage lakes. Database where data is stored (Fish Database, SWIMS, FishSED, Personal PC): SWIMS, WADRS |
| 2. Monitoring Study, Date, Results. List water quality exceedences indicating magnitude, duration and frequency. Stations: Parameters: Database where data is stored (Fish Database, SWIMS, FishSED, Personal PC): |
| 3. Monitoring Study, Date, Results. List water quality exceedences indicating magnitude, duration and frequency. Stations: Parameters: Database where data is stored (Fish Database, SWIMS, FishSED, Personal PC): |
| Narrative on why you are proposing this waterbody to be listed or delisted? Silver Lake has received considerable best management practices including diverting Silver Creek from the lake, eradication and restocking with desirable fish species, and an alum treatment to seal the deep water sediments from phosphorus release. These management activities have improved the lake to a point where it can now be removed from the impaired waters list. Water quality monitoring has confirmed that the lake has improved since the completion of the restoration efforts. For instance, summer average secchi depth is 3.9 feet based on 32 samples collected between 7/15/2005 and 9/15/2009. Average chlorophyll TSI based on Carlson’s TSI calculations is 55 (‘Fair’ for Deep Seepage Lakes). This is below the natural community impairment threshold for TSI of 63 for deep seepage lakes. (Note: Using the Wisconsin chlorophyll TSI calculation, TSI-chl is 52, and average TSI-secchi is 58.) The average total phosphorus value is .035 mg/l based on May-Oct, 2004-2008 (or 0.034 mg/l based on 25 summer samples collected between 7/15/2005 and 9/15/2009). Although these TP data still exceed the impairment threshold of .02 mg/l for deep seepage lakes, Silver Lake showed improving TP levels from the 2004 alum treatment through 2007 (the 2008 values spiked due to extreme flooding). This lake has undergone extensive treatment and is greatly improved; as evidenced by the TSI-chl. values of 'Fair', it should no longer be considered impaired. |
| List and Attach any additional reports, updated watershed tables, analyses etc. including use designation survey. 1. Reports are in the database. Monitoring has also been done during the summer 2009. All data are available, but have not been summarized in a report yet. 2. Personal reference per Paul Garrison (10/2009): Garrison’s best professional judgment is also to remove it from the list and no longer consider it impaired. Although macrophytes haven’t rebounded to the extent he would like, average TSI-chlorophyll for 2004-08 shows that it should no longer be considered impaired. 3. 4. 5. |

| Silver Lake WBIC |  |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Lake Water Quality Report - 1960 to 2009 |  |  |  |  |  |  |  |  |  |
| Lake Name | County Name | Station ID |  |  | Lake Name | County Name | Station ID |  |  |  |  |  |
| Silver Lake | Manitowoc | 363080 |  |  | Silver Lake | Manitowoc | 363312 |  |  |  |  |  |
|  |  | DeepHoleWest |  |  |  | DeepHoleEast |  |  |  |  |
| Group Seq No | Start Date | Total Phosphorus(ug/l) | Group Seq No | Start Date | Total Phosphorus(ug/l) | AVEs of both stations |  |
| 7000105 | 04/28/2004 | 75 |  |  | 7000105 | 04/28/2004 | 73 |  |  |  |  |  |
| 7000093 | 05/06/2004 | 69 |  |  | 7000093 | 05/06/2004 | 50 |  |  |  |  |  |
| 8188489 | 05/06/2004 |  |  |  | 7000093 | 06/16/2004 | 30 |  |  |  |  |  |
| 8188499 | 05/06/2004 |  |  |  | 7000093 | 07/19/2004 | 32 |  |  |  |  |  |
| 8188489 | 05/23/2004 |  |  |  | 7000093 | 08/24/2004 | 39 |  |  |  |  |  |
| 8188489 | 06/05/2004 |  |  |  | 7000105 | 09/13/2004 | 28 |  |  |  |  |  |
| 7000093 | 06/16/2004 | 32 |  |  |  |  |  |  |  |  |  |  |
| 8188489 | 06/20/2004 |  |  |  |  |  |  |  |  |  |  |  |
| 8188489 | 06/30/2004 |  |  |  |  |  |  |  |  |  |  |  |
| 7000093 | 07/19/2004 | 34 |  |  |  |  |  |  |  |  |  |  |
| 8188489 | 07/30/2004 |  |  |  |  |  |  |  |  |  |  |  |
| 7000093 | 08/24/2004 | 39 |  |  |  |  |  |  |  |  |  |  |
| 8188489 | 08/30/2004 |  |  |  |  |  |  |  |  |  |  |  |
| 7000066 | 09/13/2004 | 29 |  |  |  |  |  |  |  |  |  |  |
| 7000105 | 09/13/2004 | 31 |  |  |  |  |  |  |  |  |  |  |
| 2004 West Annual Average | 44.14286 |  |  | 2004 East Annual Average | 35.8 |  | 39.97143 |  |  |  |
| 8188489 | 05/21/2005 |  |  |  | 7000093 | 04/11/2005 | 49 |  |  |  |  |  |
| 7000093 | 06/04/2005 |  |  |  | 7000093 | 06/16/2005 | 24 |  |  |  |  |  |
| 8188489 | 06/18/2005 |  |  |  | 7000093 | 07/19/2005 | 29 |  |  |  |  |  |
| 8188489 | 07/06/2005 |  |  |  | 7000093 | 08/12/2005 | 27 |  |  |  |  |  |
| 8188489 | 07/27/2005 |  |  |  | 7000105 | 10/04/2005 | 28 |  |  |  |  |  |
| 8188489 | 08/17/2005 |  |  |  |  |  |  |  |  |  |  |  |
| 7000105 | 10/04/2005 | 24 |  |  |  |  |  |  |  |  |  |  |
| 2005 West Annual Average | NA |  |  | 2005 East Annual Average | 27 |  | 27 |  |  |  |
| 7000093 | 03/30/2006 | 55 |  |  | 7000093 | 03/30/2006 | 64 |  |  |  |  |  |
| 8188489 | 06/16/2006 |  |  |  | 8188489 | 06/16/2006 |  |  |  |  |  |  |
| 7000093 | 07/26/2006 | 32 |  |  | 7000093 | 07/26/2006 | 27 |  |  |  |  |  |
| 8188489 | 08/05/2006 |  |  |  | 8188489 | 08/05/2006 |  |  |  |  |  |  |
| 8188489 | 08/19/2006 |  |  |  | 8188489 | 08/18/2006 |  |  |  |  |  |  |
| 7000093 | 08/22/2006 | 27 |  |  | 8188489 | 08/19/2006 |  |  |  |  |  |  |
| 7000093 | 09/12/2006 | 33 |  |  | 7000093 | 08/22/2006 | 25 |  |  |  |  |  |
| 7000105 | 09/21/2006 | 74 |  |  | 7000093 | 09/12/2006 | 30 |  |  |  |  |  |
|  |  |  |  |  | 7000105 | 09/21/2006 | 27 |  |  |  |  |  |
| 2006 West Annual Average | 44.2 |  |  | 2005 East Annual Average | 27.25 |  | 35.725 |  |  |  |
| 7000093 | 04/09/2007 | 44 |  |  | 7000093 | 04/09/2007 | 42 |  |  |  |  |  |
| 7000093 | 05/21/2007 | 23 |  |  | 7000093 | 05/21/2007 | 21 |  |  |  |  |  |
| 7000093 | 06/11/2007 | 18 |  |  | 7000093 | 06/11/2007 | 27 |  |  |  |  |  |
| 7000093 | 07/18/2007 | 25 |  |  | 7000093 | 07/18/2007 | 27 |  |  |  |  |  |
| 7000093 | 08/28/2007 | 24 |  |  | 7000093 | 08/28/2007 | 22 |  |  |  |  |  |
| 7000093 | 09/20/2007 | 25 |  |  | 7000093 | 09/20/2007 | 36 |  |  |  |  |  |
| 2007 West Annual Average | 26.5 |  |  | 2007 East Annual Average | 26.6 |  | 26.55 |  |  |  |
| 7000093 | 04/15/2008 | 80 |  |  | 7000093 | 04/15/2008 | 78 |  |  |  |  |  |
| 7000093 | 05/27/2008 | 24 |  |  | 7000093 | 05/27/2008 | 28 |  |  |  |  |  |
| 25988479 | 05/27/2008 |  |  |  | 25988479 | 05/27/2008 |  |  |  |  |  |  |
| 7000093 | 07/09/2008 | 51 |  |  | 7000093 | 07/09/2008 | 56 |  |  |  |  |  |
| 7000093 | 07/30/2008 | 57 |  |  | 7000093 | 07/30/2008 | 60 |  |  |  |  |  |
| 7000093 | 08/21/2008 | 52 |  |  | 7000093 | 08/21/2008 | 43 |  |  |  |  |  |
| 7000093 | 09/03/2008 | 38 |  |  | 25988479 | 08/21/2008 |  |  |  |  |  |  |
| 7000105 | 09/17/2008 | 38 |  |  | 7000093 | 09/03/2008 | 40 |  |  |  |  |  |
|  |  |  |  |  | 7000105 | 09/17/2008 | 43 |  |  |  |  |  |
| 2008 West Annual Average | 48.57143 |  |  | 2008 East Annual Average | 45 |  | 46.78571 |  |  |  |
| 7000093 | 04/15/2009 | 80 |  |  | 7000093 | 04/15/2009 | 101 |  |  |  |  |  |
| 7000093 | 05/18/2009 | 55 |  |  | 7000093 | 05/18/2009 | 41 |  |  |  |  |  |
| 7000093 | 05/26/2009 | 33 |  |  | 7000093 | 05/26/2009 | 32 |  |  |  |  |  |
| 7000093 | 06/12/2009 | 33 |  |  | 7000093 | 06/12/2009 | 36 |  |  |  |  |  |
| 7000093 | 06/25/2009 | 27 |  |  | 7000093 | 06/25/2009 | 28 |  |  |  |  |  |
| 7000093 | 07/08/2009 | 46 |  |  | 7000093 | 07/08/2009 | 42 |  |  |  |  |  |
| 7000060 | 07/21/2009 | 42 |  |  | 7000060 | 07/21/2009 | 39 |  |  |  |  |  |
| 7000060 | 08/07/2009 | 28 |  |  | 7000060 | 08/07/2009 | 26 |  |  |  |  |  |
| 19205950 | 08/07/2009 |  |  |  | 7000105 | 08/07/2009 |  |  |  |  |  |  |
| 7000093 | 08/20/2009 | 25.7 |  |  | 7000093 | 08/20/2009 | 32.7 |  |  |  |  |  |
| (2009 data not used for calculations) |  |  | (2009 data not used for calculations) | Total AVES: | 35.20643 | ug/l | 32.31161 | (w/o 2008 data from high flood year) |
|  |  |  |  |  |  |  |  |  | 0.035206 | mg/l |  |  |
|  |  |  |  |  | Deep Seepage lake impairment threshold is greater than or equal to .02 mg/l |  |
|  |  |  |  |  | Silver lake does still exceed the impairment threshold for TP. |  |  |  |
|  |  |  |  |  | **NOTE: Per Mary Gansberg, the lake had improving TP levels from the 2004 alum treatment through 2007, but the 2008 values spiked due to extreme flooding. (If you take the 2008 data out & only use 2004-2007, then the average is .03, still exceeding the threshold of .02). This lake has undergone extensive treatment and is greatly improved, with TSI-chl. values of 'good'. Mary feels it should be delisted. |