WUERCHES CREEK STREAMCLASS STUDY, GREEN LAKE COUNTY,

WISCONSIN

By Michael Reif

WDNR, Oshkosh Service Center

November 5, 2010

INTRODUCTION

A stream classification/TMDL study was conducted in 2006-2007 to gather sufficient data to determine the stream classification and TMDLs of Wuerches Creek.  Wuerches Creek is a small spring-fed stream that enters Green Lake in the SW end.  It drains a surface area of 3035 acres (4.7 sq. miles).  There were no point sources on Wuerches Creek.  However, though work has been done improving non-point source, there was still at least one significant contributor observed.

STUDY AREA AND METHODS

Two sites (W1 and W2) were chosen to evaluate the water quality and obtain some hydraulic understanding of the Wuerches Creek Subwatershed (see Figure 1 and Table 1).  Figure 1 and the Stream Miles in Table 1 were done in Terrain Navigator Pro. The evaluation of Wuerches Cr. was done in a manner similar to the way I did the stream classification studies on several streams in Fond du Lac and Calumet Counties except fish and habitat surveys were not conducted.  The understanding is that this may be sufficient data to do a TMDL evaluation on Wuerches Cr. as well.

Table l.  Wuerches Cr. Site W1 and W2 descriptions.

| Site | Miles From Mouth | Swims Station ID | Site Description |
| --- | --- | --- | --- |
| W1 | 1.04 | 10020701 | 100 Feet Below Luedtke Rd. |
| W2 | 3.31 | 10012583 | 200 Feet Below CTY B |

Macroinvertebrate Community Assessment

Macroinvertebrates were collected in the spring (April 6) of 2007 from Site W2. Samples were delivered to the University of Wisconsin-Stevens Point Aquatic Entomology Lab for identification.

Water Quality Assessment

Onset temperature loggers were placed at Sites W1 and W2 in the spring, summer and fall of 2007.  Loggers were attached inside PVC canisters (see Photo 1) that had slits cut in 2 sides to allow water to freely pass through and create a continuous flow past the probe.  The canisters were attached to rebar pounded into the stream bottom.  The canisters were either allowed to lie on the hard gravel bottom in riffles to keep them in the flow and from sedimenting over.  Figures of the graphs from the temp. logger data are distributed in the main part of this report while the raw avg., min, and max.’s for each site are tabled in Appendix D.  Instantaneous temperature, conductivity and D.O. measurements were taken through the study with a YSI 85 meter.  Chemical samples for chloride, alkalinity,N-series, P, field conductivity and field Ph were conducted on sites W1 and W2 in the summer of 2007 (see Appendix A).

RESULTS AND DISCUSSION

I started the Wuerches Cr. sampling on April 2007 sampling the macroinvertebrates at Site W2.  A memo summarizing that sampling is in Reif, 2007.  While sampling the macroinvertebrates at W2 I caught 3 fat mottled sculpin in the D-frame net.  I expect they were females that were full of spawn.  This indicated to me that at least this part of Wuerches Cr. was at least a seasonal cold water sculpin stream.  Sculpin may migrate up from Green Lake to spawn in Wuerches Cr.  I did not do any fishery surveys so I cannot specify if the sculpin were resident or migratory or a combination.  Mottled sculpin were found in Mt. Vernon Cr. Wisconsin spawning between April 1 to May 3 in a temperature range of 8.9 Deg. C and 13.9 Deg. C (Becker, 1983).  Mottled sculpin were often found to be resident in waters that averaged 16-22 Deg. C (Becker, 1983).  The temperature monitor at Site W2 that measured hourly temperature from April 7 to Oct 7, 2007 found daily averages and maximums to be sufficiently cold (Figure 3) to qualify Wuerches Cr. as a Cold-Water Stream (WDNR 2004).  That would mean at least Coldwater B (CW-B) according to that guidance document.

The oxygen levels at Site W2 appeared sufficient for spring spawning of sculpin and spring spawning salmonids.  However, low D.O. concentrations were found at W2 in August and September (3.2 and 2.8 mg/l respectively).  These D.O. levels likely indicate oxygen conditions insufficient to sustain sculpin at those times of the year.  I was not able to determine if these low levels were due to human modifications of Wuerches Cr. above W2 or natural effects by wetlands above W2.  More evaluation of the entire stretch of Wuerches Cr. from W1 to W2 is necessary to help answer these questions.  I also don’t know if the hydraulics of the Creek were modifiable.  All flow values for W1 and W2 were found to be much higher at W2 than W1 except for the July 17, 2007 sampling where they were nearly the same (Table 4).  I can’t explain the July 17 occurrence other than it was possibly rainfall that reached W1 but not W2 or modifications of the flow between W1 and W2.

All T-P values for both sites were found to be well above the 0.075 mg/l proposed Phosphorus standard for small streams.  It appeared that most of the T-P at W1originated from above Luedtke Rd. (possibly the farm above Luedtke Rd).  T-P values were found to be much higher at W1 than W2 for all sample dates.  Averaging the T-P and flow for W2, converting to lbs/day and extrapolating over a year calculates a total yearly discharge of Phosphorus to Green Lake of 121 lbs (as P).

The macroinvertebrate species list for site W2 collected April 6, 2007 are in Table C1 of Appendix C.  The Hilsenhoff Biotic Index (HBI) determined from these data was 5.789 indicating Fair water quality (fairly significant organic pollution) (Hilsenhoff, 1987).  It is notable that the overwhelming dominant species found was Gammarus pseudolimnaeus (83 individuals picked out of a total of 285, or 29% of the population).  This indicates close proximity to a source of springs feeding the stream (Dimick, 2006).

CONCLUSIONS AND RECOMMENDATIONS

I have already submitted a 2008 Impaired Waters Documentation Sheet on November 8, 2007 for Wuerches Cr. to put the Creek on the 303d Impaired Waters List for low D.O. and the pollutants T-P and Sediment.  The data base for these recommendations are in the Discussion above.

The finding of sculpin in April 2007 and the documentation of cold water conditions as discussed above indicate that Wuerches Cr. is currently at least a spring seasonal CW-B stream.  Without the impairments mentioned above it has the potential to sustain resident sculpin throughout the spring, summer and fall.  Therefore, I am recommending Wuerches Cr. be also listed as a potential CW-B sculpin stream year around.  These conditions are similar to other feeder streams to Green Lake such as Dakin Cr.  If impairments were sufficiently corrected it also has the potential for CW-B MIG for spring spawning of salmonids.

Figure 2.  Wuerches Cr. Site W1 daily temperatures for summer 2007.

Figure 3.  Wuerches Cr. Site W2 daily temperatures for summer 2007.

Table 2.  Wuerches Cr. monthly D.O. field measurements (mg/l)

| Date | Site W1 | Site W2 |
| --- | --- | --- |
| April 18, 2007 | 8.2 | 11.1 |
| May 21, 2007 | 6.8 | 10.8 |
| June 4, 2007 | 5.6 | 7.5 |
| June 18, 2007 | 4.8 | 4.2 |
| July 17, 2007 | 5.8 | 6.1 |
| August 22, 2007 | 3.1 | 2.8 |
| September 26, 2007 | 4.3 | 4.4 |

Table 3.  Wuerches Cr. monthly T-P data (mg/l)

| Date | Site W1 | Site W2 |
| --- | --- | --- |
| April 18, 2007 | 0.34 | 0.089 |
| May 21, 2007 | 0.404 | 0.111 |
| June 4, 2007 | 1.64 | 0.172 |
| June 18, 2007 | 0.636 | 0.126 |
| July 17, 2007 | 0.586 | 0.137 |
| August 22, 2007 | 2.16 | 0.528 |
| September 26, 2007 | 1.55 | 0.155 |

Table 4.  Wuerches Cr. monthly flow data (cfs).

| Date | Site W1 | Site W2 |
| --- | --- | --- |
| April 18, 2007 | 0.431 | 1.728 |
| May 21, 2007 | 0.192 | 1.3 |
| June 4, 2007 | 0.315 | 1.905 |
| June 18, 2007 | - | 1.1 |
| July 17, 2007 | 0.772 | 0.825 |
| August 22, 2007 | 0.771 | 2.209 |
| September 26, 2007 | 0.068 | 1.309 |

LITERATURE CITED

Becker, G. C.  1983.  Fishes of Wisconsin.  University of Wisconsin Press.  1052 p.

Dimmick, J.  2006.  Personal Communication.  UW-SP.

Hilsenhoff, W. L.  1987.  An Improved Biotic Index of Organic Stream Pollution.  The Great Lakes Entomologist.  Vo. 20(1): 31-39.

Reif, M. D.  2007.  Roy and Wuerches Cr. Spring 2007 Macroinvertebrate Sampling.  WDNR File Memo.  2 p.

WDNR, 1980.  Wisconsin Trout Streams.   Publication 6-3600(80).  65 p.

WDNR, 2004.  Guidelines for Designating Fish & Aquatic Life Uses for Wisconsin Surface Waters.  Pub-WT-807-04.  60 pp.

APPENDIX A

CHEMICAL SAMPLING DATA

Table A1.  Wuerches Cr. Site W1 April 18, 2007 chemistry sampling data.

Table A2.  Wuerches Cr. Site W2 April 18, 2007 chemistry sampling data.

Table A3.  Wuerches Cr. Site W1 May 21, 2007 chemistry sampling data.

Table A4.  Wuerches Cr. Site W2 May 21, 2007 chemistry sampling data.

Table A5.  Wuerches Cr. Site W1 June 4, 2007 chemistry sampling data.

Table A6.  Wuerches Cr. Site W2 June 4, 2007 chemistry sampling data.

Table A7.  Wuerches Cr. Site W1 June 18, 2007 chemistry sampling data.

Table A8.  Wuerches Cr. Site W2 June 18, 2007 chemistry sampling data.

Table A9.  Wuerches Cr. Site W1 July 17, 2007 chemistry sampling data.

Table A10.  Wuerches Cr. Site W2 July 17, 2007 chemistry sampling data.

Table A11.  Wuerches Cr. Site W1 August 22, 2007 chemistry sampling data.

Table A12.  Wuerches Cr. Site W2 August 22, 2007 chemistry sampling data.

Table A13.  Wuerches Cr. Site W1 September 26, 2007 chemistry sampling data.

Table A14.  Wuerches Cr. Site W2 September 26, 2007 chemistry sampling data.

APPENDIX B

2007 FLOW DATA

Table B1.  Wuerches Cr. Site W1 April 18, 2007 flow data.

Table B2.  Wuerches Cr. Site W2 April 18, 2007 flow data.

Table B3.  Wuerches Cr. Site W1 May 21, 2007 flow data.

Table B4.  Wuerches Cr. Site W2 May 21, 2007 flow data.

Table B5.  Wuerches Cr. Site W1 June 4, 2007 flow data.

Table B6.  Wuerches Cr. Site W2 June 4, 2007 flow data.

Table B7.  Wuerches Cr. Site W1 June 18, 2007 flow data.

None, flow too low to measure.

Table B8.  Wuerches Cr. Site W2 June 18, 2007 flow data.

Table B9.  Wuerches Cr. Site W1 July 17, 2007 flow data.

Table B10.  Wuerches Cr. Site W2 July 17, 2007 flow data.

Table B11.  Wuerches Cr. Site W1 August 22, 2007 flow data.

Table B12.  Wuerches Cr. Site W2 August 22, 2007 flow data.

Table B13.  Wuerches Cr. Site W1 September 26, 2007 flow data.

Table B14.  Wuerches Cr. Site W2 September 26, 2007 flow data.

APPENDIX C

MACROINVERTEBRATE DATA

Table C1.  Wuerches Cr. Site W2 April 6, 2007 macroinvertebrate data.

APPENDIX D

TIDBIT TEMPERATURE DATA

# Text boxes

Wuerches Creek looking upstream from Luedtke Rd. (June 4, 2007).

Photo 1.  PVC canister and  temperature probe.  The probes were placed in the canisters to protect them.   The slots in the PVC were to allow flow through.  Photo taken by Al Neibur.