STREAM RECLASSIFICATION OF CAMPGROUND CREEK, FOND DU LAC COUNTY, WISCONSIN

Main Report

Part 4.  Habitat Site Specifics

Wisconsin DNR

Oshkosh Area Office

April 2010

By Michael Reif

TABLE OF CONTENTS

Part 1.  Introduction, Study Area Overview and General Overview Results

TABLE OF CONTENTS……………………………………………………………….2

TABLE OF TABLES…...................................................................................................4

TABLE OF FIGURES…………………………………………………………………..5

TABLE OF PHOTOS…………………………………………………………………...8

TABLE OF APPENDICES…………………………………………………………….10

ACKNOWLEDGEMENTS……………………………………………………………13

SUMMARY OF FINDINGS…………………………………………………………...14

INTRODUCTION AND STUDY AREA OVERVIEW…………………………..….21

INTRODUCTION……………………………………………………………...21

METHODS AND STUDY AREA OVERVIEW……………………………..21

Fish Community assessment………………………………………...…23

Habitat Assessment……………………………………………………..23

Macroinvertebrate Community Assessment………………………….24

Water Quality Assessment……………………………………………..25

GENERAL OVERVIEW RESULTS………………………………………….26

Part 2.  In Depth Analyses and Results, Origin and Main Headwater Wetland Complex, and Spring Tributary

IN DEPTH ANALYSES AND RESULTS FROM THE CAMPGROUND CREEK

SUBWATERSHED……………………………………………………………..13

CAMPGROUND CREEK ORIGIN SUBWATERSHED…................13

CAMPGROUND MAIN HEADWATER WETLAND COMPLEX……………………………………………………………...21

Part 3.  Historical Evaluation

HISTORICAL EVALUATION OF CAMPGROUND CREEK

ORIGIN SUBWATERSHED AND MAIN WETLAND

COMPLEX……………………………………………………..12

CAMPGROUND SPRING TRIBUTARY SUBWATERSHED

SPECIFICS……………………………………………………..17

Part 4.  Habitat Site Specifics

HABITAT SITE SPECIFICS…………………………………………12

Habitat Site C1c……………………………………….……..…12

Habitat Site C7………………………………………………….15

Habitat Site C8….........................................................................18

Habitat Site C12………………………………………………...19

Part 5.  Subwatershed Use Classifications and Literature Cited.

CAMPGROUND CREEK SUBWATERSHED USECLASSIFICATIONS……….13

ACT 310 GROUNDWATER PROTECTION AREA AND PROTECTION RECOMMENDATIONS FOR CAMPGROUND CR………………………………………………………………………………….….14

LITERATURE CITED………………………………………………………………...25

Part 6.  Appendices.

APPENDICES…………………………………………………………………………..13

TABLE OF TABLES

Part 1.  Introduction, Study Area Overview and General Overview Results

Table 1.  Current and proposed 2004 Use Guidance comparisons used in this report…15

Table 2.  Campground Cr. Subwatershed Use Classifications and 303d listings………15

Table 3.  Campground Creek site descriptions………………………………………….22

Table 4.  Campground Creek flows sampled on August 30, 2004…..………………….24

Table 5.  Campground Cr. Subwatershed areas (acres)………………………………….24

Part 2.  In Depth Analyses and Results, Origin and Main Headwater Wetland Complex, and Spring Tributary

No Tables in Part 2.

Part 3.  Historical Evaluation

No Tables in Part 3.

Part 4.  Habitat Site Specifics

Table 6.  Habitat, IBI and HBI scores for C1c…………………………………………..12

Table 7.  Campground Site C7 habitat data from 2003………………………………….17

Table 8.  Habitat data for Site C8 collected 2003………………………………………..18

Table 9.  Campground Cr. Site C12 habitat data from August 23, 2001………………...19

TABLE OF FIGURES

Part 1.  Introduction, Study Area Overview and General Overview Results

Figure 1.  Campground Subwatershed…………………………………………………..12

Figure 2.  Campground/Parsons Creek Watershed………………………………………17

Figure 3.  Campground Headwater Wetland…………………………………………….18

Figure 4.  Campground Cr. Lower Watershed…………………………………………..19

Figure 5.  Campground Cr. Subwatershed………………………………………………24

Part 2.  In Depth Analyses and Results, Origin and Main Headwater Wetland Complex, and Spring Tributary

Figure 6.  Campground Creek Origin……………………………………………………26

Figure 7.  Campground Cr. Origin spring locations……………………………………..27

Figure 8.  Campground Origin Site C1a (below pond) summer 2003 temp. summary…28

Figure 9.  Campground Origin Site C1b (Bible Camp) summer 2003 temp. summary…28

Figure 10.  Campground Origin Site C1c (habitat site) summer 2003 temp. summary…29

Figure 11.  Linear Regression of Site C1c Summer 2003 Temp. vs City of Ripon 2003

Air Temp……………………………………………………………………..29

Figure 12.  Campground Cr. Site C6 (below Mill Pond Rd.) summer 2001 temp. 
                   summary……………………………………………………………………..36

Figure 13.  Campground Cr. Site C10 (above the WWTF) summer 2001 temp.

summary……………………………………………………………………...36

Figure 14.  Campground Cr. 2001 daily avg. summary of all Sites comparison with Air

Temp. and Site C1c 2003 daily avg. temp…………………………………..42

Part 3.  Historical Evaluation

Figure 15.  1835 Platt Map of Campground Cr. Origin and Main Wetland Complex…..13

Table of Figures cont.

Figure 16.  Combination of the 1955 Topographical Map and 2000 Aerial Photo of the
                  Campground Origin and Main Wetland Complex…………………………..14

Figure 17.  Combination Map (1835 Platt, 1955 Topo and 2000 Aerial) of

Campground Origin Area……………………………………………………15

Figure 18.  Closeup 2000 Aerial of Campground Cr. diversion location into the Main

Wetland Complex……………………………………………………………16

Figure 19.  2000 Aerial of Main Wetland Complex showing diversion location and

Re-entry into main channel…………………………………………………..17

Figure 20.  Campground Spring Trib. Site CST2 (above River Rd.) summary of

2005 temp…………………………………………………………………….18

Figure 21.  Campground Spring Trib. Site CST2 (above River Rd.) 2003 temp.

summary……………………………………………………………………...19

Figure 22.  Campground Spring Trib. Subwatershed……………………………………20

Figure 23.  2005 Aerial Photo of the Biker Trib. Impoundment………………………...20

Part 4.  Habitat Site Specifics

Figure 24.  Campground Cr. Site C1c daily temp. summary for 2003-2004…………….14

Figure 25.  Campground Cr. Site C7 (below HWY D) summer 2001 temp. summary….17

Figure 26.  Campground Cr. Site C11 (below the WWTF) summer 2001 temp.

summary……………………………………………………………………...20

Part 5.  Subwatershed Use Classifications and Literature Cited.

Figure Cuse1.  Campground Origin Subwatershed……………………………………...59

Figure Cuse2.  Campground Origin Trib. Subwatershed………………………………..63

Figure Cuse3.  Campground Main Wetland Complex Subwatershed…………………...64

Figure Cuse4.  Spring Trib. Subwatershed……………………………………………....65

Figure Cuse5.  Biker Trib. Subwatershed……………………………………...………...66

Figure Cuse6  Middle-Stem Subwatershed…………………………………………..….67

Figure Cuse7.  Cemetery Subwatershed……………………………………………...….68

Figure Cuse8.  Village of Oakfield Subwatershed………………………………..……..69

Figure Cuse9.  Thill Rd. Subwatershed……………………………………………….....70

TABLE OF PHOTOS

Part 1.  Introduction, Study Area Overview and General Overview Results

Photo 1.  PVC canister and temperature probe…………………………………………21

Photo 2.  Campground Cr. as it flowed through the Deer Farm above HWY Y……….25

Photo 3.  Photo of one of the Campground Cr. Origin main springs coming from

the escarpment………………………………………………………………..27

Photo 4.  Closeup photo of Photo 3…………………………………………………….30

Photo 5.  Spring 2006 runoff in Trib. to Campground Origin………………………….31

Photo 6.  Bible Camp bridge across Campground Cr. Origin main stem………………32

Photo 7.  Metal bridge across Campground Cr. located before the Cr. entered the

Main Wetland…………………………………………………………………34

Photo 8.  Campground Creek below metal bridge at Site C2…………………………...34

Photo 9.  Photo of Escarpment on west side of Main Wetland Complex……………….35

Photo 10.  Large pond on Oakfield Conservation Club Land…………………………...35

Photo 11.  Outlet of large pond on Oakfield Conservation Club Land………………….36

Photo 12.  Campground Creek Site C5 above River Rd…………………………………37

Photo 13.  CST feeder spring located beween River Rd. and HWY F observed in

April 2004…………………………………………………………………….39

Photo 14.  Sample Site C12 above Thill Rd…………………………………………..…41

Part 4.  Habitat Site Specifics

Photo 15.  Campground Cr. Site C1c main riffle………………………………..…….…14

Photo 16.  Upstream end of C1c…………………………………………………..……..16

Photo 17.  Upstream end of Site C7…………………….…………………………….….17

Photo 18.  Eroded bank within Site C12…………………………………………….…...21

Photo 19.  Campground Cr. Site C11………………………………………………….....22

Photo 20. Village of Oakfield WWTF outfall…………………………………………....22

Photo 21.  Campground Cr. Site C12 looking upstream…………………………………23

TABLE OF APPENDICES

APPENDIX A.  CHEMICAL DATA…………………………………………………67

Table A1.  Campground Creek and Tributaries chemistry data from

the November 8, 2000 sampling…………………………………….68

Table A2.  Data from the chemical sampling of the Campground Creek

Origin area (06/05/2003)…………………………………………….69

APPENDIX B.  TEMERATURE AND D.O. GRAB DATA…………………………70

Table B1.  Campground Cr. Temp. and D.O. profile for July 6, 2001…………..71

Table B2.  Campground Cr. Temp. and D.O. profile for July 16, 2001…………71

Table B3.  Campground Cr. Temp. and D.O. profile for August 3, 2001……….71

Table B4.  Campground Cr. Temp. and D.O. profile for  August 8, 2001………72

Table B5.  Campground Cr. Temp. and D.O. profile for October 2, 2001

probe retrieval………………………………………………………..72

APPENDIX C.  TEMPERATURE PROBE DATA…………………………………..73

Table C1.  Campground Cr. Air Site (at WWTF) temperature summary

(summer 2001)……………………………………………………….74

Table C2.  Campground Cr. Site C5 (above River Rd.) temperature summary

for summer 2001……………………………………………………..75

Table C3.  Campground Cr. Site C6 (below Millbrook Rd.) temperature

summary for summer 2001…………………………………………..76

Table C4.  Campground Cr. Site C7 (below HWY D) temperature summary

for summer 2001……………………………………………………..77

Table C5.  Campground Cr. Site C10 (above WWTF) temperature summary

for summer 2001…………………………………………………….78

Table C6.  Campground Cr. Site C11 (below WWTF) temperature summary

for summer 2001…………………………………………………….79

Table C7.  Campground Origin Main Trib. (COMT) below HWY F temp.

summary for summer 2005…………………………………………..80

APPENDIX C cont.

Table C8.  Campground Cr. Origin (Site C1a) below private pond outfall

(2003)………………………………………………………………84

Table C9.  Campground Cr. Origin Site C1b summer 2003 temp. summary….85

Table C10.  Campground Cr. Origin Site C1c (habitat site) for summer 2003..86

Table C11.  Campground Cr. Origin Habitat Site C1c temp. summary

(11/06/03 to 01/26/04)……………………………………………87

APPENDIX D.  FISH DATA…………………………………………………………88

Table D1.  Data from the Campground Creek Site C7 fish sampling

(10/27/2000)………………………………………………………..89

Table D2.  Data from the Campground Cr. Site C10 fish sampling

(10/27/2000)………………………………………………………..89

Table D3.  Data from the Campground Creek Site C11 fish sampling

(10/27/2000)………………………………………………………...89

Table D4.  Data from the Campground Creek Site C8 (behind Cemetery)

fish sampling (August 17, 2001)……………………………………90

Table D5.  Data from the Campground Spring Trib. Site CST3 below River

Rd. (143 meter stretch below Green residence) backpack shocking

on October 4, 2005………………………………………………….90

APPENDIX E.  MACROINVERTEBRATE DATA…………………………………91

Table E1.  Campground Creek Site C1 (Habitat Site at Origin)

macroinvertebrate taxa list (collected 05/02/2003)………………….92

Table E2.  Campground Creek Site C1 (Habitat Site at Origin)

macroinvertebrate taxa list (collected 09/29/2004)………………….93

Table E3.  Campground Creek Site C7 (below HWY D) macroinvertebrate

taxa list (collected 10/19/2001)………………………………………94

Table E4.  Campground Creek Site C7 (below HWY D) macroinvertebrate

taxa list (collected 04/29/2002)………………………………………95

APPENDIX E cont.

Table E5.  Campground Creek Site C8 (behind Cemetery) macroinvertebrate

taxa list (collected 10/19/2001)………………………………………96

Table E6.  Campground Creek Site C10 (above WWTF) macroinvertebrate

Taxa list (collected 10/16/2001)……………………………………..97

Table E7.  Campground Creek Site C11(below WWTF) macroinvertebrate

taxa list (collected 10/16/2001)……………………………………….98

APPENDIX F.  SEDIMENT DATA………………………………………………….101

Table F1.  Sediment data from C1c collected June 16, 2003……

# HABITAT SITE SPECIFICS

# Habitat Site C1c

Habitat assessment was conducted in the Origin area at C1c.  The habitat data are in Table 4.  The riffles of the site were heavily dominated by Gammarus pseudolimnaeus and the small stonefly Nemoura trispinosa.  In the fall 2003 sample (Table M1) N. trispinosa numerically made up 25.9% of the mocroinvertebrate

community.  The high quality spring-fed riffle areas of Campground Cr. appear to be dominated by N. trispinosa.  In stream areas where N. trispinosa and G. pseudolimnaeus dominate the community is often made of Baetis tricaudata (Dimmick, 2004) which was the only mayfly found in May 2003.  The number of Glossosoma sp in the sample appeared lower than I visually observed.  I suspect this was due to the kick-net sampling technique.  Glossosoma sp was tightly attached to the rocks and the technique did not dislodge them nearly as easily as N. trispinosa so relative abundance was skewed away from Glossosoma.  Again, other methods such as light trapping would be highly useful to give a better picture of the aquatic macroinvertebrate communities.  G. pseudolimnaeus made up 54.5% of the fall 2003 sampled community.  Chironomids were third in abundance at 11.3% followed by the high quality caddisfly Parapsyche apicalus at 2.8%.  It would possibly be helpful to identify the Chironomidae further but the time needed to do preparations for head smashing was not available.  The are preserved and could still be further identified if needed.

Habitat Site C1c was a good reference for the main stem of the Campground Cr. Origin.  It was a function of a majority of the inputs to this section and provided a good definition of whether this part of Campground Cr. can sustain a trout population and/or population of cold water species such as sculpin.  The Habitat Score was 65 indicating good habitat (Table 6).  The three macroinvertebrate HBI values obtained from spring 2003, fall 2004 and spring 2005 samplings indicate a high quality cold water stream but also reflect the heavy sediment input from the upstream watershed during the heavy rains of spring/summer 2004.  The habitat work in Table 6 was conducted before these sediment runoff events.  However, visual observation during the habitat work and after the runoff events clearly describe conditions.  Prior to the runoff events the site was dominated by clean gravel bottom riffles and runs with little sediment accumulation.  After the runoff the bottom of even much of the swiftly flowing riffle areas were covered by several inches of fresh sediment.  Wading through the sediment was difficult.  I had to go to the shore to walk the site while in 2003 I was able to easily wade the entire site.  I would estimate the runoff covered 70% of the bottom of the site and had a major impact on the macroinvertebrate population and would have significantly cut down on trout habitat and food if a trout population had been established.

Table 6.  Habitat , IBI and HBI scores for Site C1c.

| Parameter | Calculated Value | Score | Rating |
| --- | --- | --- | --- |
| Riparian Buffer Width | >10.0 m | 15 | Excellent |
| Bank Erosion | 0.83 m of bare soil | 10 | Good |
| Pool Area | 7% | 0 | Poor |
| Width:Depth Ratio | 12.5 avg. thalweg | 10 | Good |
| Riffle:Riffle Ratio | 3.65 | 15 | Excellent |
| Fine Sediments | 49.6% | 5 | Fair |
| Cover For Fish | 10.4% | 10 | Good |
| Total |  | 65 | Good |
| HBI |  | 3.01 | Excellent |

*An IBI score was not determined due to insufficient sample (see write-up).

The water quality of Habitat Site C1c was excellent.  The temperature regime was very stable throughout all seasons with little if any ice forming during even the coldest winter periods (see Photo 15 and 16).  Peaks in the spring/summer of 2003 clearly indicate significant rainfall events (Table 7 and Table T1 in appendix).  Otherwise the temperature varied little during the day and from day to day clearly reflecting the heavy groundwater inputs in and above the site.

Figure 24.  Campground Cr. Site C1c daily temp. summary for 2003-04.

The macroinvertebrate population clearly reflects the site and imputs to the stream.  Gammarus pseudolimnaeus dominated the macroinvertebrate sample collected in May 2003 (Table EM1).  The small stonefly Nemoura trispinosa was second most dominant macroinvertebrate in the sample.  N. trispinosa has been documented as being typical in this type of spring feeder cold water habitat (Williams et al 1995) and is commonly dominant with  G. pseudolimnaeus and the mayfly Baetis tricaudata (Dimmick, 2004) as it was here.  This stonefly is also a good indicator of the cold water inputs and health of the spring feeders to Campground Cr.  A good population was also found in the spring area of CST and a small one in the Biker Trib. at BT1.

# Habitat Site C7

Site C7 (the second habitat site) was located below HWY D (see Figure 1).  This site was  important for two reasons:  1) it appeared to be the point where the oxygen levels of Campground Cr. clearly recovered from the depression caused by the main wetland complex and 2) it contained the only defined quality habitat for fantail darters found in Campground Cr.  The habitat of this site can also be characterized in 2 parts:  1) the upper reach where the gradient was fast (4 ft drop over 230 feet) and the lower reach where the gradient was noticeably less though still a mix of riffle/run (4ft drop over 324 feet).  The higher gradient area which contained a large bottom cover of rubble was the site where the fantails were localized.  Though only 3 were captured, I believe the difficulty in capturing them was due to the fact that they stayed on the bottom and under which rocks skewed the results to the low side (see Table D1).  The HBI was 5.0 for 10/29/2001 (Table E3) and 4.986 for 4/29/2002 (Table E4) both indicating good water quality (Hilsenhoff, 1987).  Both fish and macroinvertebrate populations reflected excellent diversity.

The habitat rating for this site (Table 7) indicated good habitat.  Bottom cover and attachment for macroinvertebrates was excellent.  Cover for game fish was very good.  The fact that Stenacron interpuntactum was the only Heptageneid found at this site indicated current use to be less than cold water (or at least that it has oxygen concerns at times likely due to problems from above the site).  Another indicator was that stoneflies were not found at this site.  A large number of the fish caught indicate cool water conditions (see Table D1).  A primary indicator of this would be the large number of pearl dace found.  Other indicator fish though indicated possible warm water conditions (such as the fantails).

Summer 2001 continuous daily average temperature data at C7 (Figure 21 and Table C4) were found to range from 17.3 Deg. C to 24.7 Deg. C.  Fifteen daily averages between July 20 and August 9 were found to be over the 20.0 Deg. C optimum required for Brook Trout and Brown Trout though lower than the lethal limit of 25.0 Deg. C (Becker 1983).  Discussions with local residents indicate that trout (rainbow and browns) were caught in the deepest central part of site C7 in the past though none were caught recently.   The local Oakfield Fishing Club has planted rainbow and browns in the past.  Present temperature conditions indicate only the ability for this site to contain a put and take fishery.  Koehnke (1999) indicated this site to have very good support for a put and take trout population.  A possibility exists for this to be enhanced but not without a significant reduction to the temperature warming in the summer by the large wetland complex as discussed above.

The flow at Site C7 was estimated to be 34.4% from the Origin Subwatershed,  2.5% from the Biker Trib. Subwatershed, 8.1% from the Campground Origin Trib. Subwatershed and 22.6% from the Spring Trib. Subwatershed (based on data listed in Table 4).  The remaining 32.4% can mostly be attributed to springs that feed the Main Wetland Complex Subwatershed though it is clear from the Topo Map that a spring comes into the Main Stem just below Site C6 at Millpond Rd.  This spring was not studied.  Therefore, it is clear that the condition of the Main Wetland Complex Subwatershed has a major effect on the temperature and oxygen content of the Main Stem and must be managed to where the flow is channelized into a natural meander and can receive spring input with minimized warming and oxygen demand.

Table 7.  Campground Site C7 habitat data from 2003.

| Parameter | Calculated Value | Score | Rating |
| --- | --- | --- | --- |
| Riparian Buffer Width | 6.63 | 5 | Fair |
| Bank Erosion | 0 | 15 | Excellent |
| Pool Area | 16.4% | 3 | Fair |
| Width:Depth Ratio | 13.6 avg. thalweg | 10 | Good |
| Riffle:Riffle Ratio | 6.14 | 5 | Fair |
| Fine Sediments | 32.5% | 15 | Excellent |
| Cover For Fish | 26.9% | 15 | Excellent |
| Total |  | 68 | Good |
| HBI |  | 5.000 | Good |
| CW IBI |  | 0 | Very Poor |
| WW IBI |  | 32 | Fair |

Figure 25.  Campground Cr. Site C7 (below HWY D) 2001 temp. summary.

Habitat Site C8

Habitat Site C8 was located in a non-dredged site in the Central Subwatershed that had both banks protected throughout the reach (Figure 1).  The habitat was similar to the lower half of Site C7 (Table 9).  Also similar were the fish and macroinvertebrate populations (Tables DF8 and M8).  Variations in the fish populations were that there were no fantails (there was no high gradient they like) and noticeably lower numbers of pearl dace possibly indicating warming conditions (the stream banks in the pasture located immediately above this site were all grazed though not eroded).  In the pasture above this site though indications are positive since much spring seepage around the extensive sedge hummocks was observed in the pasture.

Table 8.  Habitat data for Site C8 collected 2003.

| Parameter | Calculated Value | Score | Rating |
| --- | --- | --- | --- |
| Riparian Buffer Width | >10.0 m | 15 | Excellent |
| Bank Erosion | >1.0 | 0 | Poor |
| Pool Area | 0 | 0 | Poor |
| Width:Depth Ratio | 17.7 avg. thalweg | 5 | Good |
| Riffle:Riffle Ratio | 56.9 | 0 | Poor |
| Fine Sediments | 42.9% | 5 | Fair |
| Cover For Fish | 14.1% | 10 | Good |
| Total |  | 35 | Fair |
| HBI |  | 4.99 | Good |
| CW IBI |  | 10 | Poor |
| WW IBI |  | 37 | Fair |

Habitat Site C11

Habitat Site C11 was located from the mixed point below the Village of Oakfield WWTP downstream.  The length of the site was 385 feet (117.4 meters) with a stream with of 4.07 meters.  This Site was characteristic of most of Campground Cr. below HWY Y above and below the WWTP.  It was characterized by extensive ditching (that the stream has been reworking (and is continuing to rework) to re-generate its natural meandering.  This was noticeable side cutting in this process (see photo ?).  This side cutting appears to be adding important gravel to the stream from the adjacent subsoils.  As was apparent in Sites C7 and C8 the fish and macroinvertebrate populations appeared to be good as far as numbers and diversity.  An HBI was not conducted for this Site since a macroinvertebrate sample was not collected.  However, the macroinvertebrate population for Site C11, above the WWTP, can be used as a description of this site as well since the habitats were very similar.  The WW IBI for this site was 42.  A list of the fish species collected are in Table 3C in the Appendix.  The dominant species collected was the Common Shiner (Luxilus cornutus).  The habitat data collected are in Table 9 below.

Table 9.  Campground Cr. Site C11 habitat data from August 23, 2001.

| Parameter | Calculated Value | Score | Rating |
| --- | --- | --- | --- |
| Riparian Buffer Width | 7.1 m | 10 | Good |
| Bank Erosion | 2.61 | 0 | Poor |
| Pool Area | 0 | 0 | Poor |
| Width:Depth Ratio | 11.83 avg. thalweg | 10 | Good |
| Riffle:Riffle Ratio | 13.9 | 10 | Good |
| Fine Sediments | 42.6% | 5 | Fair |
| Cover For Fish | 33.1% | 15 | Excellent |
| Total |  | 50 | Good* |
| HBI |  | 4.99 | Good |
| CW IBI |  | 0 | Very Poor |
| WW IBI |  | 42 | Fair |

*It is notable that the Good habitat rating resulted partially from the high value of fish cover being derived almost entirely from overhanging canary grass.  This was a typical condition for this area of Campground Cr.

Temperature probe data collected for this site in the summer of 2001 are in Table ? of the Appendix and illustrated in the graph in Figure ? below.  It is notable to compare these temperatures to those of C7 (at the Jose Farm)and C11 (above the WWTP) for the summer of 2001.  The temperatures compare similarly to C11 indicating the WWTP had minimal effect on the stream temperature.  However, temperatures were noticeably higher than at C7 (the maximum for the summer being 5 Deg. C higher).  These higher temperatures can be at least in part due to the extensive exposure of the Creek to the sun between C7 and C11.

Figure  26.  Campground Cr. Site C11 (below the WWTF) summer 2001 temp. summary.

# Text boxes

Photo 15.  Campground Cr. Site C1c main riffle.  Looking upstream (December 2003).

Photo 16.  Upstream end of C1c.  Looking downstream from wooden bridge.  March 2003.

Photo 17.  Upstream end of  Site C7.   Looking downstream from HWY D.  Note the higher gradient.  This was the fantail site.  November 2000.

Photo 18.  Eroded bank within Site C11.  Note the high bank (from past extensive ditching).  There was noticeable side cutting in this site.  November 1, 2000.

Photo 19.  Campground Cr. Site C11.  Looking upstream from lower end (November 1, 2000).

Photo 20.  Village of Oakfield WWTF outfall.  Looking downstream (November 1, 2000).

Photo 21.  Campground Cr. Site C12 looking upstream.  Note the heavy bank canary grass cover that provided for an excellent fish cover rating (November 1, 2000).

Photo of Lower end of Campground Origin Subwatershed.