STREAM RECLASSIFICATION OF CAMPGROUND CREEK, FOND DU LAC COUNTY, WISCONSIN

Main Report

Part 5.  Subwatershed Use Classifications and Literature Cited.

Wisconsin DNR

Oshkosh Area Office

April 2010

By Michael Reif

TABLE OF CONTENTS

Part 1.  Introduction, Study Area Overview and General Overview Results

TABLE OF CONTENTS……………………………………………………………….2

TABLE OF TABLES…...................................................................................................3

TABLE OF FIGURES…………………………………………………………………..4

TABLE OF PHOTOS…………………………………………………………………...5

TABLE OF APPENDICES……………………………………………………………..6

ACKNOWLEDGEMENTS……………………………………………………………..7

SUMMARY OF FINDINGS……………………………………………………………8

INTRODUCTION AND STUDY AREA OVERVIEW…………………………..….18

INTRODUCTION……………………………………………………………...18

METHODS AND STUDY AREA OVERVIEW……………………………..19

Fish Community assessment………………………………………...…20

Habitat Assessment……………………………………………………..20

Macroinvertebrate Community Assessment………………………….21

Water Quality Assessment……………………………………………..22

GENERAL OVERVIEW RESULTS………………………………………….23

Part 2.  In Depth Analyses and Results, Origin and Main Headwater Wetland Complex, and Spring Tributary

IN DEPTH ANALYSES AND RESULTS FROM THE CAMPGROUND CREEK

SUBWATERSHED……………………………………………………………..26

CAMPGROUND CREEK ORIGIN SUBWATERSHED…................26

CAMPGROUND MAIN HEADWATER WETLAND COMPLEX……………………………………………………………...30

Part 3.  Historical Evaluation

HISTORICAL EVALUATION OF CAMPGROUND CREEK

ORIGIN SUBWATERSHED AND MAIN WETLAND

COMPLEX……………………………………………………..12

CAMPGROUND SPRING TRIBUTARY SUBWATERSHED

SPECIFICS……………………………………………………..17

Part 4.  Habitat Site Specifics

HABITAT SITE SPECIFICS…………………………………………12

Habitat Site C1c……………………………………….……..…12

Habitat Site C7………………………………………………….15

Habitat Site C8….........................................................................18

Habitat Site C12………………………………………………...19

Part 5.  Subwatershed Use Classifications and Literature Cited.

CAMPGROUND CREEK SUBWATERSHED USECLASSIFICATIONS……….13

ACT 310 GROUNDWATER PROTECTION AREA AND PROTECTION RECOMMENDATIONS FOR CAMPGROUND CR………………………………………………………………………………….….14

LITERATURE CITED………………………………………………………………...25

Part 6.  Appendices.

APPENDICES…………………………………………………………………………..13

TABLE OF TABLES

Part 1.  Introduction, Study Area Overview and General Overview Results

Table 1.  Current and proposed 2004 Use Guidance comparisons used in this report…15

Table 2.  Campground Cr. Subwatershed Use Classifications and 303d listings………15

Table 3.  Campground Creek site descriptions………………………………………….22

Table 4.  Campground Creek flows sampled on August 30, 2004…..………………….24

Table 5.  Campground Cr. Subwatershed areas (acres)………………………………….24

Part 2.  In Depth Analyses and Results, Origin and Main Headwater Wetland Complex, and Spring Tributary

No Tables in Part 2.

Part 3.  Historical Evaluation

No Tables in Part 3.

Part 4.  Habitat Site Specifics

Table 6.  Habitat, IBI and HBI scores for C1c…………………………………………..12

Table 7.  Campground Site C7 habitat data from 2003………………………………….17

Table 8.  Habitat data for Site C8 collected 2003………………………………………..18

Table 9.  Campground Cr. Site C12 habitat data from August 23, 2001………………...19

TABLE OF FIGURES

Part 1.  Introduction, Study Area Overview and General Overview Results

Figure 1.  Campground Subwatershed…………………………………………………..12

Figure 2.  Campground/Parsons Creek Watershed………………………………………17

Figure 3.  Campground Headwater Wetland…………………………………………….18

Figure 4.  Campground Cr. Lower Watershed…………………………………………..19

Figure 5.  Campground Cr. Subwatershed………………………………………………24

Part 2.  In Depth Analyses and Results, Origin and Main Headwater Wetland Complex, and Spring Tributary

Figure 6.  Campground Creek Origin……………………………………………………26

Figure 7.  Campground Cr. Origin spring locations……………………………………..27

Figure 8.  Campground Origin Site C1a (below pond) summer 2003 temp. summary…28

Figure 9.  Campground Origin Site C1b (Bible Camp) summer 2003 temp. summary…28

Figure 10.  Campground Origin Site C1c (habitat site) summer 2003 temp. summary…29

Figure 11.  Linear Regression of Site C1c Summer 2003 Temp. vs City of Ripon 2003

Air Temp……………………………………………………………………..29

Figure 12.  Campground Cr. Site C6 (below Mill Pond Rd.) summer 2001 temp. 
                   summary……………………………………………………………………..36

Figure 13.  Campground Cr. Site C10 (above the WWTF) summer 2001 temp.

summary……………………………………………………………………...36

Figure 14.  Campground Cr. 2001 daily avg. summary of all Sites comparison with Air

Temp. and Site C1c 2003 daily avg. temp…………………………………..42

Part 3.  Historical Evaluation

Figure 15.  1835 Platt Map of Campground Cr. Origin and Main Wetland Complex…..13

Table of Figures cont.

Figure 16.  Combination of the 1955 Topographical Map and 2000 Aerial Photo of the
                  Campground Origin and Main Wetland Complex…………………………..14

Figure 17.  Combination Map (1835 Platt, 1955 Topo and 2000 Aerial) of

Campground Origin Area……………………………………………………15

Figure 18.  Closeup 2000 Aerial of Campground Cr. diversion location into the Main

Wetland Complex……………………………………………………………16

Figure 19.  2000 Aerial of Main Wetland Complex showing diversion location and

Re-entry into main channel…………………………………………………..17

Figure 20.  Campground Spring Trib. Site CST2 (above River Rd.) summary of

2005 temp…………………………………………………………………….18

Figure 21.  Campground Spring Trib. Site CST2 (above River Rd.) 2003 temp.

summary……………………………………………………………………...19

Figure 22.  Campground Spring Trib. Subwatershed……………………………………20

Figure 23.  2005 Aerial Photo of the Biker Trib. Impoundment………………………...20

Part 4.  Habitat Site Specifics

Figure 24.  Campground Cr. Site C1c daily temp. summary for 2003-2004…………….14

Figure 25.  Campground Cr. Site C7 (below HWY D) summer 2001 temp. summary….17

Figure 26.  Campground Cr. Site C11 (below the WWTF) summer 2001 temp.

summary……………………………………………………………………...20

Part 5.  Subwatershed Use Classifications and Literature Cited.

Figure 27.  Campground Cr. Groundwater Protection Area……………………………15

Figure Cuse1.  Campground Origin Subwatershed……………………………………...16

Figure Cuse2.  Campground Origin Trib. Subwatershed………………………………..17

Figure Cuse3.  Campground Main Wetland Complex Subwatershed…………………...18

Figure Cuse4.  Spring Trib. Subwatershed……………………………………………....19

Figure Cuse5.  Biker Trib. Subwatershed……………………………………...………...20

Figure Cuse6  Middle-Stem Subwatershed…………………………………………..….21

Figure Cuse7.  Cemetery Subwatershed……………………………………………...….22

Figure Cuse8.  Village of Oakfield Subwatershed………………………………..……..23

Figure Cuse9.  Thill Rd. Subwatershed……………………………………………….....24

TABLE OF PHOTOS

Part 1.  Introduction, Study Area Overview and General Overview Results

Photo 1.  PVC canister and temperature probe…………………………………………21

Photo 2.  Campground Cr. as it flowed through the Deer Farm above HWY Y……….25

Photo 3.  Photo of one of the Campground Cr. Origin main springs coming from

the escarpment………………………………………………………………..27

Photo 4.  Closeup photo of Photo 3…………………………………………………….30

Photo 5.  Spring 2006 runoff in Trib. to Campground Origin………………………….31

Photo 6.  Bible Camp bridge across Campground Cr. Origin main stem………………32

Photo 7.  Metal bridge across Campground Cr. located before the Cr. entered the

Main Wetland…………………………………………………………………34

Photo 8.  Campground Creek below metal bridge at Site C2…………………………...34

Photo 9.  Photo of Escarpment on west side of Main Wetland Complex……………….35

Photo 10.  Large pond on Oakfield Conservation Club Land…………………………...35

Photo 11.  Outlet of large pond on Oakfield Conservation Club Land………………….36

Photo 12.  Campground Creek Site C5 above River Rd…………………………………37

Photo 13.  CST feeder spring located beween River Rd. and HWY F observed in

April 2004…………………………………………………………………….39

Photo 14.  Sample Site C12 above Thill Rd…………………………………………..…41

Part 4.  Habitat Site Specifics

Photo 15.  Campground Cr. Site C1c main riffle………………………………..…….…14

Photo 16.  Upstream end of C1c…………………………………………………..……..16

Photo 17.  Upstream end of Site C7…………………….…………………………….….17

Photo 18.  Eroded bank within Site C12…………………………………………….…...21

Photo 19.  Campground Cr. Site C11………………………………………………….....22

Photo 20. Village of Oakfield WWTF outfall…………………………………………....22

Photo 21.  Campground Cr. Site C12 looking upstream…………………………………23

TABLE OF APPENDICES

APPENDIX A.  CHEMICAL DATA…………………………………………………13

Table A1.  Campground Creek and Tributaries chemistry data from

the November 8, 2000 sampling…………………………………….14

Table A2.  Data from the chemical sampling of the Campground Creek

Origin area (06/05/2003)…………………………………………….15

APPENDIX B.  TEMERATURE AND D.O. GRAB DATA…………………………16

Table B1.  Campground Cr. Temp. and D.O. profile for July 6, 2001…………..17

Table B2.  Campground Cr. Temp. and D.O. profile for July 16, 2001…………17

Table B3.  Campground Cr. Temp. and D.O. profile for August 3, 2001……….17

Table B4.  Campground Cr. Temp. and D.O. profile for  August 8, 2001………18

Table B5.  Campground Cr. Temp. and D.O. profile for October 2, 2001

probe retrieval………………………………………………………..18

APPENDIX C.  TEMPERATURE PROBE DATA…………………………………..19

Table C1.  Campground Cr. Air Site (at WWTF) temperature summary

(summer 2001)……………………………………………………….20

Table C2.  Campground Cr. Site C5 (above River Rd.) temperature summary

for summer 2001……………………………………………………..21

Table C3.  Campground Cr. Site C6 (below Millbrook Rd.) temperature

summary for summer 2001…………………………………………..22

Table C4.  Campground Cr. Site C7 (below HWY D) temperature summary

for summer 2001……………………………………………………..23

Table C5.  Campground Cr. Site C10 (above WWTF) temperature summary

for summer 2001…………………………………………………….24

Table C6.  Campground Cr. Site C11 (below WWTF) temperature summary

for summer 2001…………………………………………………….25

Table C7.  Campground Origin Main Trib. (COMT) below HWY F temp.

summary for summer 2005…………………………………………..26

APPENDIX C cont.

Table C8.  Campground Cr. Origin (Site C1a) below private pond outfall

(2003)………………………………………………………………27

Table C9.  Campground Cr. Origin Site C1b summer 2003 temp. summary….28

Table C10.  Campground Cr. Origin Site C1c (habitat site) for summer 2003..29

Table C11.  Campground Cr. Origin Habitat Site C1c temp. summary

(11/06/03 to 01/26/04)……………………………………………30

APPENDIX D.  FISH DATA…………………………………………………………32

Table D1.  Data from the Campground Creek Site C7 fish sampling

(10/27/2000)………………………………………………………..33

Table D2.  Data from the Campground Cr. Site C10 fish sampling

(10/27/2000)………………………………………………………..33

Table D3.  Data from the Campground Creek Site C11 fish sampling

(10/27/2000)………………………………………………………...33

Table D4.  Data from the Campground Creek Site C8 (behind Cemetery)

fish sampling (August 17, 2001)……………………………………34

Table D5.  Data from the Campground Spring Trib. Site CST3 below River

Rd. (143 meter stretch below Green residence) backpack shocking

on October 4, 2005………………………………………………….34

APPENDIX E.  MACROINVERTEBRATE DATA…………………………………35

Table E1.  Campground Creek Site C1 (Habitat Site at Origin)

macroinvertebrate taxa list (collected 05/02/2003)………………….36

Table E2.  Campground Creek Site C1 (Habitat Site at Origin)

macroinvertebrate taxa list (collected 09/29/2004)………………….37

Table E3.  Campground Creek Site C7 (below HWY D) macroinvertebrate

taxa list (collected 10/19/2001)………………………………………38

Table E4.  Campground Creek Site C7 (below HWY D) macroinvertebrate

taxa list (collected 04/29/2002)………………………………………39

APPENDIX E cont.

Table E5.  Campground Creek Site C8 (behind Cemetery) macroinvertebrate

taxa list (collected 10/19/2001)………………………………………40

Table E6.  Campground Creek Site C10 (above WWTF) macroinvertebrate

Taxa list (collected 10/16/2001)……………………………………..41

Table E7.  Campground Creek Site C11(below WWTF) macroinvertebrate

taxa list (collected 10/16/2001)……………………………………….42

APPENDIX F.  SEDIMENT DATA…………………………………………………..43

Table F1.  Sediment data from C1c collected June 16, 2003…… …………………………………..44

Campground Creek Summary of Results and Subwatershed Use Classifications

As was described above Campground Creek can be subdivided into 9 separate subwatersheds that can be described according to how they function within their own self contained subwatershed.  The Use Classifications of  Campground Cr. and Campground Cr. Tributaries can also be described within these subwatersheds.  These Use Classifications are listed in Table 1 in the SUMMARY OF FINDINGS  section at the start of this report.  They are also illustrated in the following 9 maps which split out each subwatershed into a larger map for greater description.

As mentioned earlier in the CAMPGROUND CREEK ORIGIN SUBWATERSHED section, Campground Cr. originates in several springs that come off an escarpment just north of HWY F.  These springs keep the winter and summer water temperatures very stable and maintain a good baseflow around 1 to 1.5 cfs (depending on precipitation conditions of any particular year).  These conditions, along with some quality riffles and pools, appear to provide habitat for at least a small reproducing brook trout population.  However, the current Use must be classified as CWA-Cold due to the fact that no salmonids or cold water fish species were found during shocking or other visual observations.  As was also discussed earlier in the Habitat section for C1c, the amount of sediment runoff that was documented in the summer of 2004 due to May-June heavy rainfall runoff indicate runoff and sedimentation to be too great to count on a brook trout population (and high quality macroinvertebrates for that matter) to be completely healthy year around.

As was discussed in the CAMPGROUND CREEK MAIN HEADWATER WETLAND COMPLEX SUBWATERSHED, the water quality as it moves from the Origin Subwatershed to the Main Wetland Subwatershed was of high quality (stable cold water temperatures, 100% D.O. saturation and clear water).  As it left the Main Wetland Complex Subwatershed it had poor quality (low D.O. (seasonally near 0 mg/l with fish kills) and had high water temperatures (as much as 14.5 Deg. C increase from when it went into the Wetland)).  It was also heavily stained as it left the Main Wetland Subwatershed due to DOC.  This staining was maintained all the way to the confluence with the E. Br. of the Fond du Lac R.

The confluence of the Campground Origin Trib. and Main Stem of  Campground Cr. marked the downstream end of both Subwatersheds.  The Campground Origin Trib. within the Campground Origin Trib. Subwatershed was found to have continuous flow throughout the Study (even during the dry summers of 2003 and 2005).  However, winter observations indicate complete ice cover at the point of confluence during the coldest part of the winter.  This indicated spring flow input to be closer to the upper part of the Trib.  This Trib. was observed to have cold water conditions near its origin above HWY F as well as a high quality cold water macroinvertebrate population.  Therefore, its Current Use classification was determined to be DFAL-MC.  Potential Use depending on what occurs with the Origin Trib. Subwatershed is DFAL-MC with seasonal use by trout (CWA).

The CAMPGROUND CREEK MIDDLESTEM SUBWATERSHED was defined by the low quality water entering it from the Main Wetland Complex Subwatershed.  The closest Current Use classification that fits this Subwatershed is DFAL-NG though it cannot meet this Use in some of the Subwatershed due to the minimum D.O. not being able to meet the DFAL 5 mg/l limit.  This was caused by the water temperatures coming into the Middlestem Subwatershed were found to be as high as 30 Deg. C during warm periods of the summer with very low D.O. (near 0 mg/l at times).  For this Study this Subwatershed can be defined by data collected at Site C6 where it crossed Millpond Rd.  The Creek was found to be very deep (as much as 3 feet) below Millpond Rd.  This could provide good salmonid habitat if this Subwatershed could meet the Potential Use of CWB-Class IIx (mainly from trout that could migrate (and seasonal reside) from upstream CWA Potential Use areas.  There was a Trib. that came into the Creek from the west (see Byron Topographic Map) that was not studied.  It came into the Creek in the deepest areas downstream from Site C6.  It is unknown what effect (if any) it had on the Creek.  The Campground Spring Trib. entered Campground Cr. in the upper part of this Subwatershed and likely had positive effects on the Middlestem in relation to temperature and D.O.  With Watershed work it could also aid in the Middlestem meeting Potential Use.

The Spring Trib. in the Campground Spring Trib. Subwatershed entered Campground Cr. in the upper end of the Middlestem Subwatershed.  It was defined by Site CST2 above River Rd. and backpack shocking done in the fall of 2005 as well as visual observations of the Subwateshed.  Its  Current Use was determined to be DFAL-Coolwater particularly due to the large numbers of Brassy Minnows that we captured during the all of 2005 backpack shocking.  Water temperatures were never found above 18 Deg. C during the warm months indicating cold water Use Potential.  As mentioned above, past trout stocking (including brook trout) found that there could be year-to-year survival of some stocked trout though no evidence of reproduction was found.  Winter temperatures were not found to be as stable as with the Origin Subwatershed but localized areas were found with good spring flow which could allow for some reproduction of brook trout and cold water species of fish.  Therefore, the Potential Use was determined to be CW-A-Class IIn.  Groundwater inflows, through found to be good, were not found to be sufficient to warrant a CW-A Class I classifications since suitable areas for brook trout reproduction appear to be localized.  In order to meet the Use Potential much Subwatershed work would have to be done to stabilize hydraulics, sediment runoff and concerns with impounded springs in the origin area south of HWY F.

The Cemetery Subwatershed  covered the area of HWY D down to just below HWY Y.  This subwatersed was defined by Sites C7 (a habitat site discussed in the Habitat Section above) as well as site C8 behind the Village of Oakfield Cemetery.  Other visual observations aided in the Current Use classification of DFAL-NG.  The low D.O. caused by conditions in the Main Wetland Subwatershed was found to have recovered by the point where this Subwatershed started (Site C7).  The high water temperatures were found to have recovered before that point.  The Potential Use of  CW-B-Class IIx cannot be attained without the improvements mentioned above for other Subwatersheds above this one.  Other conditions within the Subwatershed would have to be improved such as deepening the Creek, maintaining shade and solving some extensive erosion sediment runoff problems.  Macroinvertebrate and forage fish populations were found to be very good in terms of numbers and diversity.  Notable in the upper half of Site C7 (as discussed in the Habitat Section above) was the large localized population of Fantail Darters.  Riffle areas are extensive as are meanders (this Subwatershed did not appear to have been influenced but past ditching as was done with other Subwatersheds).  As with other Subwatersheds it was found to have numerous small feeders and seepage areas which, with protection, could aid in the Subwatershed meeting Potential Use.

The Village of Oakfield Subwateshed originated below just below HWY Y and extended downstream about ½ mile.  It contained two somewhat significant spring feeders that can be found on the Watershed maps in this report (Figures 1 and Cuse8).  Both spring feeders were noticeably modified by urbanization and agricultural runoff.  During most of this Study the lower feeder took effluent from the can cooling water discharge of Chiquita Foods during the summer which noticeably warmed the feeder.  At the time of this writing that was no longer the case.  The Village of Oakfield WWTF discharged near the middle of this Subwatershed.  It was found to have some seasonal though apparently localized effect on the macroinvertebrate population.  As discussed in other sections above (Habitat Site C11) the Creek in this Subwatershed was characterized by extensive past ditching and was found to be beginning the process of recovery (side cutting and meandering).

Act 310 Groundwater Protection Area and Protection Recommendations for Campground Cr.

Figure 25 below includes the Groundwater Protection Area for Campground Creek and adjacent springs and tributaries that require protection  to maintain and attain a coldwater resource and fishery for Campground Cr.  The Parsons Cr. Groundwater Protection Area is included for comparison.  2003 Assembly Bill 926 (2003 Wisconsin Act 310) requires in 281.34 Growndwater withdrawals.  (8). Groundwater Protection Areas. (b) The Department shall create accurate images of groundwater protection areas.  A map defining the 1200 foot Groundwater Protection Area around Parsons Creek and the East Branch to Parsons Creek is in Figure 25.  This Groundwater Protection Area is established around the entire Creek since it is established as a Class I and II trout water (DNR, 1980).  This is also intended to protect the spring areas and Cold Water Tributaries to Campground Cr. and includes many permanent working springs (many are described in this report) that support the flow and temperature of Campground Creek maintaining conditions for a sustaining brook trout population.  According to Act 310 this Groundwater Protection Area provide for the requirement of an Environmental Impact Statement for any construction of any high capacity well within the Area.

The springs that need particular protection are:  1) those just north of the Bible Camp that come from the base of an open part of the Escarpment there; 2) those that come from the Escarpment along the NW side of the Main Wetland in the Main Wetland Subwatershed; and 3) those that are along the entire stretch of the Campground Spring Trib. between CTY F and River Rd.

It is also important to note that it is necessary that an  Environmental Review Document be developed under Wis. Administrative Code NR 150 specifically related to groundwater impacts for any WPDES Permitted entity related to groundwater impacts.  It is also recommended that a Groundwater Conservation Plan be developed for the entire Campground Creek Subwatershed regarding groundwater quantity, quality and temperature issues.

Figure 27.  Campground Cr. Groundwater Protection Area.

LITERATURE CITED

Becker, G. C.  1983.  Fishes of Wisconsin.  Univ. of Wis. Press.  1052 p.

Betten, C.  1950.  The genus Pycnopsyche (Tricoptera).  Annals of the Entomological Society of America 43(4): 508-22.

Congdon, J.  1982.  Management Recommendations-Fond du  Lac County Trout Streams.  DNR internal memo.

Dimmick, J.  2003.   Memo on Nemoura trispinosa.  UW-SP. 1p.

Hacker, V.  1956.  1955 Stream Shocker Survey of Byron Creek, Fond du Lac County.  DNR internal memo.

Hasse, Bob.  2007.  Personal Communication regarding Creek flow restriction and temperature warming.

Koehnke, S. E.  1999.  Comprehensive Cold Water Stream Survey of Upper Fox River Watershed, Fond du Lac County, WI  WDNR.

Lyons, J.  1992.  Using the Index of Biotic Integrity (IBI) to Measure Environmental Quality in Warmwater Streams of Wisconsin.  U.S. Dept. of Agriculture.  General Technical Report NC-149.  51 p.

WDNR, 2000.  Guidelines for Evaluating Habitat of Wadable Streams.  Bureau of Fisheries and Habitat Protection.

Hilsenhoff, W. L.  1987.  An Improved Biotic Index of Organic Stream Pollution.  Vo. 20(1): 31-39.

WDNR, 2004.  Guidelines for Designating Fish & Aquatic Life Uses for Wisconsin Surface Waters.  Pub-WT-807-04.  60 pp.

WDNR, 2007.  Sediment & Nutrient TMDL for Parsons Creek & its East Tributary, Fond du Lac County, WI.  Wis. Dept. Nat. Res.  Bureau of Watershed Management.  58 pp.

Reif, 2006.  April 24, 2006 Evaluation of Parsons and Campground Cr. with Trout Unlimited.  WDNR File Memo.  7 pp.

Reif, 2009a.  Parsons Creek Stream Classification, Fond du Lac County, Wisconsin.  In progress.

Reif, 2009b.  Silver Creek Stream Classification, Fond du Lac County, Wisconsin.  In progress.

Simonson, T. D., J. Lyons, and P. D. Kanehl.  2000.  Guidelines for Evaluating Fish Habitat in Wisconsin Streams.  US Dept. Ag.  Gen. Tech. Report NC-164.  36 pp.

Stoerzer, L.  1999.  Waterway History:  T14N R17E, S. 20, Fond du Lac County.  DNR Memo.  11 pp.

WDNR, 2002.  Wisconsin Trout Streams.  99 pp.

Weisensel, D. and Mazenet, 1975.  Village of Oakfield WWTP Stream Classification.  WDNR.

Williams, D. D., N. E. Williams, and I. D. Hogg.  1995.  Life History of Nemoura trispinosa (Plecoptera:  Nemouridae) Along a Permanent-Temporary Water Habitat Gradient.  34: 155-163.

# Text boxes

Photo of Lower end of Campground Origin Subwatershed.