Doty Creek Stream Classification, Fond du Lac County, Wisconsin

By Michael D. Reif

WDNR Oshkosh, WI

December 2010

INTRODUCTION

I collected information from Doty Creek (a classified trout stream (WDNR, 1980)) between 2007 and 2009 to begin a Study to understand that Subwatershed to compare to Campground Cr. and Parsons Cr. (two other classified trout streams in Fond du Lac County (WDNR, 1980).  Doty Creek is a local name.  It is also known as Dotyville Creek.  The actual mapped name is the Sheboygan River.  It is an origin area of the Sheboygan River.  I prefer the name Doty Creek since it separates an origin cold and coolwater part of the Sheboygan River from the rest of the warm water parts of the River.  Data available from this introductory study are sufficient to gain a general understanding of the use classification of Doty Creek.  There are currently no point source discharges within the Doty Creek Subwatershed as defined by this study.

DOTY CREEK STUDY AREA AND METHODS USED

Three sample sites were used to describe Doty Creek and the Doty Creek Subwatershed (Table 1 and Figure 1).  Temperature monitors were set at Site DT1 and D2.  These monitors were enclosed in PVC canisters with slots to allow stream water to constantly flow through the inside of the canister and across the monitor sensor (see Photos 1 and 2).

Table 1.  Doty Cr. Site descriptions.

| Site | Miles From Mouth | Swims ID | Site Description |
| --- | --- | --- | --- |
| D2 | 3.9 | 203096 | Doty Cr. 200 ft. below CTY T |
| D1 | 6.9 | 10021316 | Doty Cr. 200 ft. above Northview Rd. |
| D0 | 9.8 | - | Origin of Doty Creek |
| DT1 | 0.97 | 10010463 | Trib. To Doty Cr. 100 ft. below 7 Hills Rd. |

The Subwatershed deliniation map in Figure 1 was done in Terrain Navigator Pro which also gives the Subwatershed area.  The Site and  distances for Table 1 were also determined with the distance tool in Navigator Pro.  The distances in Figure 5 for the Doty Creek gradient were done with a hand map measurer on a Topo Map.  The Navigator Pro measuring appeared noticeably more accurate since one can more closely follow the Creek on the map.

P

Figure 3.  Doty Creek Site D2 daily temperatures for summer 2009.

Figure 4.  Doty Cr. Trib. Site DT1 daily temperatures for summer 2009.

Figure 5.  Doty Creek Gradient of Mainstem from Origin to Mouth.

Macroinvertebrate Community Assessment

Macroinvertebrates were collected in the Spring of 2007 from Sites D1 and D2.  Samples were preserved in 95% isopropyl alcohol and  delivered to the University of Wisconsin-Stevens Point  Entomology Lab for identification and enumeration.  A Hilsenhoff Biotic Index (HBI) was calculated for each sample (Hilsenhoff, 1987).

WaterQuality Assessment

Onset (tidbit) temperature loggers were placed at Sites DT1 and D2 for spring-summer-fall of 2009.  Loggers were attached inside PVC Canisters (see Photos 1 and 2) that had slits cut in 2 sides to allow water to freely pass through and create a continuous flow past the probe.  Canisters were allowed to lie on the stream bottom in areas where the bottom was hard and siltation was reduced.  Loggers were only placed in riffles to make sure they always had good water flow through.   Instantaneous temperature and D.O. measurements were taken throughout the Study with an YSI 85.

RESULTS AND DISCUSSION OF PRESENT AND HISTORICAL DATA

As I alluded to earlier, this Study was an abbreviated Study due to money and time.  As a result, only macroinvertebrate and temperature data were collected along with visual overservations.  This is sufficient data to make some general conclusions about the current use and use potential of the Subwatershed.

A Fish Survey was conducted in July 1955 by Vern Hacker (see Oshkosh Fishery File on Dottyville Cr., Hacker, 1955 and 1967).  It mentions stocking of a total of 500 brook trout in April, May and June of 1955.  Shocking found 12 brook trout in 1955 (8 fingerlings, 1 adult and 3 marked (stocked)) at their Site 1 (about ½ mile above my Site D1).  Other species noted were abundant Pearl Dace, occasional Western Mudminnow, Brook Stickleback and Western Blacknose Dace.  Southern Redbelly Dace and Central Johnny Darters were found to be rare.  One Yellow Perch (2.4”) was also found.  No trout were found in that Survey at their Site 2 (my Site D1).  Similar other species were found along with white suckers and common Southern Redbelly Dace.  These data indicate coolwater conditions with possible coldwater transition.  No trout were found downstream at two sites to 0.75 miles above Dotyville.  My Site D2 was below Dotyville.  In a May 31, 1956 memo from Vern Hacker to Thomas Wirth evaluating these 1955 data Hacker indicated the fingerling brook trout found indicated natural reproduction.

In a March 17, 1982 memo from James Congdon to Gordon Priegel (Congdon, 1982) a Study was referenced where 6 creeks in Fond du Lac Co. were stocked and surveyed to evaluate the Department’s brook trout stocking program at the time.  The six creeks were Dottyville, Campground, Ladoga, Feldners, Parsons and Lake Fifteen Creeks.  I have Stream Classifications Studies done on Campground (Reif, 2010) and Parsons (Reif, 2009).  He references Surveys they conducted in 1981 on Dotyville Cr. from their Site 1 through Site 3.  They found no trout.  He recommended Dotyville Cr. and Silver Cr. be taken out of the Trout Stream Bulletin.  Data I collected on Silver Cr. indicates otherwise (Reif, 2009b and 2010).  Silver Cr. appeared to have salmonid migration upstream from Green Lake.

A Study at least as extensive as the one we did on Parson’s is necessary to evaluate Doty Cr. sufficiently to make final conclusions.  However, analyses of data above with my data indicate Cold Water B – IIn from the Origin down to below my Site D1 (the SWIMS indicated trout water area (see Figure 2) and DFAL Coolwater from there down to the confluence with the rest of the Sheboygan River (end of the Doty Cr. Subwatershed). The high numbers of Pearl Dace and Southern Redbelly Dace found indicate that along with the temp. data at Site D2.   Temperature monitor sites need to be extended to the historical sites 1 and 2 as well as below this Study’s Site D2.  Observations during this Study indicate sediment and habitat degradation concerns.

Table 2.  Doty Creek Site DY1 macroinvertebrate data from April 24, 2007 sample.

| Taxa | Number of Individuals | HBI Number |
| --- | --- | --- |
| Amphipoda |  |  |
| Gammaridae |  |  |
| Gammarus pseudolimnaeus | 102 | 4 |
| Coleoptera |  |  |
| Elmidae |  |  |
| Dubiraphia sp | 1 | 6 |
| Diptera |  |  |
| Ceratopogonidae |  |  |
| Bezzia/Palpomyia sp | 1 | 6 |
| Mallochohelea sp | 1 | - |
| Chironomidae |  |  |
| Chironomini |  |  |
| Microtendipes pedellus group | 1 | 6 |
| Paratendipes sp | 1 | 8 |
| Orthocladiinae |  |  |
| Corynoneura sp | 2 | 7 |
| Heterotrissocldius pupa | 1 | - |
| Parakiefferiella sp | 1 | - |
| Parametriocnemus sp | 1 | 5 |
| Tvetenia paucunca | 1 | 4 |
| Tanytarsini |  |  |
| Rheotanytarsus exiguous group | 1 | 6 |
| Stempellinella sp | 7 | 4 |
| Simuliidae |  |  |
| Simulium sp | 1 | - |
| Eucopepoda |  |  |
| Cyclopidae | 1 | - |
| Isopoda |  |  |
| Asellidae |  |  |
| Caecidotea intermedia | 11 | 8 |
| Megaloptera |  |  |
| Sialidae |  |  |
| Sialis sp | 1 | 4 |
| Perciformes |  |  |
| Percidae | 1 | - |
| Trichoptera |  |  |
| Limnephilidae |  |  |
| Anabolia sp | 4 | 5 |
| Total | 141 |  |
| HBI = |  | 4.500 |

Table 3.  Doty Creek (main site) macroinvertebrate data from April 24, 2007 sample.

| Taxa | Number of Individuals | HBI Number |
| --- | --- | --- |
| Amphipoda |  |  |
| Gammaridae |  |  |
| Gammarus pseudolimnaeus | 4 | 4 |
| Coleoptera |  |  |
| Elmidae |  |  |
| Optioservus sp | 3 | 4 |
| Optioservus fastiditus | 12 | 4 |
| Stenelmis sp | 15 | 5 |
| Stenelmis crenata | 6 | 5 |
| Diptera |  |  |
| Chironomidae larvae | 2 | - |
| Chironomini |  |  |
| Microtendipes pedellus group | 1 | 6 |
| P. (Uresipedilum) flavum | 1 | 5 |
| Diamesinae |  |  |
| Diamesa sp | 10 | 5 |
| Diamesa pupa | 1 | - |
| Orthocladiinae |  |  |
| C. (Cricotopus) sp | 1 | 7 |
| Cricotopus luciae | 1 | 7 |
| Cricotopus trifascia | 1 | 7 |
| Eukiefferiella brehmi group | 2 | 8 |
| Eukiefferiella claripennis group | 1 | 8 |
| Orthocladius pupa | 1 | - |
| O. (Orthocladius) sp | 24 | 6 |
| Parakiefferiella pupa | 1 | - |
| Parametriocnemus sp | 1 | 5 |
| Tanytarsini |  |  |
| Paratanytarsus sp | 1 | 6 |
| Tanytarsus sp | 1 | 6 |
| Tanypodinae |  |  |
| Chonchapelopia sp | 4 | 6 |
| Empididae |  |  |
| Hemerodromia sp | 1 | 6 |
| Simuliidae |  |  |
| Prosimulium mysticum | 4 | 2 |
| Tipulidae |  |  |
| Antocha sp | 2 | 3 |
| Ephemeroptera |  |  |
| Caenidae |  |  |
| Caenis sp | 3 | 7 |
| Heptageniidae |  |  |
| Stenacron interpunctatum | 5 | 7 |
| Maccarrertium mediopunctatum | 1 | 3 |
| Isopoda |  |  |
| Asellidae |  |  |
| Caecidotea intermedia | 13 | 8 |
| Plecoptera |  |  |
| Perlodidae |  |  |
| Isoperla nana | 6 | 5 |
| Trichoptera |  |  |
| Hydropsychidae |  |  |
| Ceratopsyche slossonae | 4 | 4 |
| Cheumatopsyche sp | 15 | 5 |
| Hydopsyche betteni | 4 | 6 |
| Hydropsyche cuanis | 2 | 6 |
| Limnephilidae |  |  |
| Pychnopsyche sp | 2 | 4 |
| Philopotamidae |  |  |
| Chimarrra aterrima | 1 | 4 |
| Uenoidae |  |  |
| Neophylax concinnus | 1 | 3 |
| Total | 162 |  |
| HBI = |  | 5.405 |

LITERATURE CITED

Congdon, J.  1982.  Memo to Gordon Priegel regarding WDNR trout management of six Fond du Lac. Co. trout streams.  WDNR Oshkosh Fisheries File.

Dimmick, J.  2006.  Personal Communication.  UW-SP.

Dott, R. H. and Attig, J. W.  2004.  Roadside Geology of Wisconsin.  Mountain Press Pub. Co.  346 p.

Hacker, V.  1956.  Memo regarding 1955 Dotyville Cr. brook trout surveys.  WDNR Oshkosh Fishery File.

Hilsenhoff, W. L.  1987.  An Improved Biotic Index of Organic Stream Pollution.  The Great Lakes Entomologist.  Vo. 20(1): 31-39.

Reif, M. D.  2009a.  Stream Classification of Parsons Creek, Fond du Lac Co., Wisconsin.  May 2009.  WDNR.  88 p.

Reif, M. D.  2009b.  Stream Classification of Campground Creek, Fond du Lac Co., Wisconsin.  May 2009.  WDNR.  85 p.

Reif, M. D.  2010.  Stream Classification of Silver Creek, Fond du Lac Co., Wisconsin.  Dec. 2010.  WDNR.  57 p.

WDNR, 1980.  Wisconsin Trout Streams.   Publication 6-3600(80).  65 p.

WDNR, 2002.  Wisconsin Trout Streams.  99 pp

# Text boxes

Doty Creek Map (from Fond du Lac Co. GIS) showing the numerous Drumlins from the last glacier that populate the Subwatershed.

Photo 1.  PVC Canister with old style Onset Temp. Sensor.  Note the slots in the canister to allow water to flow through.

Photo 2.  PVC Canister with Onset TidBit Temp. Sensor.  The canister is the same as with the old style Onset Senor shown in Photo 1.