DE NEVUE CREEK STREAM RECLASSIFICATION, FOND DU LAC COUNTY, WISCONSIN

DNR OSHKOSH

December 2010

BY MICHAEL REIF

TABLE OF CONTENTS

TABLE OF CONTENTS……………………………………………………………………………...……2

TABLE OF TABLES……………………………………………………………………………………….3

TABLE OF FIGURES……………………………………………………………………………………...4

TABLE OF PHOTOS……………………………………………………………………………………….5

TABLE OF APPENDICES…………………………………………………………………………………6

ACKNOWLEDGEMENTS……………………………………………………………………………...…7

SUMMARY OF FINDINGS………………………………………………………………………………..8

INTRODUCTION AND STUDY AREA OVERVIEW…………………………………………………10

DENEVUE CREEK STUDY AREA AND METHODS USED……………………………….10

Fish Community Assessment…………………………………………………………..17

Habitat Assessment……………………………………………………………………..17

Macroinvertebrate Community Assessment………………………………………….17

Water Quality Assessment……………………………………………………………..17

ANALYSES AND DISCUSSION…………………………………………………………………………18

LITERATURE CITED……………………………………………………………………………………39

APPENDICES……………………………………………………………………………………………..40

TABLE OF TABLES

Table 1.  East Branch of Ne Nevue Creek Segment Classifications……………………………………8

Table 2.  West Branch of Ne Nevue Creek Segment Classifications……………………………………8

Table 3.  De Nevue Creek Main Stem Segment Classification………………………………………….9

Table 4.  De Nevue Cr. Stream Class Study Site Descriptions………………………………………….11

Table 5.  De Nevue Cr. and Branch Segment Lenghts………………………………………………….12

Table 6.  Table of Subwatershed acreages……………………………………………………………….13

Table 7.  Habitat data collected from Site ED2 (mixed point below the Eden WWTF)……………...23

Table 8.  Fish data from the E. Br. of De Nevue Cr. Site ED2 (below Eden WWTF)…………………23

Table 9.  Fish data from E. Br. of De Nevue Site ED3 (below Lime Rd.)……………………………...27

Table 10.  E. Br. of De Nevue Cr. Site ED4 habitat data ………………………...……………………..28

Table 11.  E. Br. of De Nevue Cr. Site ED4 (above Mill Rd.) fish data………………………………...29

Table 12.  Total Phosphorus monthly NON LTT sampling data from Site D1 (2007-2008)………….34

Table 13.  De Nevue Cr. T-P (mg/l) data from June 17, 2003 sampling (a non-event sampling)……..37

TABLE OF FIGURES

Figure 1a.  E. Br. of De Nevue Cr. Subwatershed……………………………………………………….11

Figure 1b.  W. Br. of De Nevue Cr. Subwatershed………………………………………………………12

Figure 1c.  De Nevue Cr. Main Stem Subwatershed…………………………………………………….13

Figure 2.  Aerial Photo of E. Br. of De Nevue Cr. from Origin at Twin Lake to Site ED4..…………..14

Figure 3.  Aerial Photo of E. Br. of De Nevue Cr. Origin at Twin Lake……………………………….15

Figure 4.  Aerial Photo of Impoundment and Dam of E. Br. of De Nevue Cr. above Site ED3……...16

Figure 5.  E. Br. of De Nevue Cr. Site ED1 (above Eden WWTF) summer 2005 temp. data…………19

Figure 6.  Summer 2004 daily Air Temp. data collected at Eden WWTF……………………………..21

Figure 7.  Summer 2008 daily Air Temp. data collected at the Eden WWTF…………………………21

Figure 8.  De Nevue Cr. gradient including East Branch……………………………………………….24

Figure 9.  E. Br. of De Nevue Cr. Site ED4 (above Mille Rd.) summer 2008 daily temp. data……….28

Figure 10.  E. Br. De Nevue Cr. Site ED5 (above Rhinehardt Rd.) summer 2004 daily temp. data…30

Figure 11.  W. Br. De Nevue Cr. Site WD3 (above Rhinehardt Rd.) 2008 summer daily temp. data..31

Figure 12.  Aerial Photo of Sites ED5 and WD3 and confl. of E. and W. Branches of De Nevue Cr...32

Figure 13.  West Branch of De Nevue Cr. and De Nevue Cr. Main Stem gradient……………………33

Figure 14.  East Branch of De Nevue Cr. and De Nevue Ct. Main Stem gradient…………………….34

Figure 15.  Aerial Photo of Site D1……………………………………………………………………….35

Figure 16.  Regression chart for data in Table 12……………………………………………………….36

Figure 17.  Tidbit temp. data for Lake De Nevue Trib. immediately below CTH K …………………36

Figure 18.  Aerial photo of Lake De Nevue and its outlet……………………………………………….37

TABLE OF PHOTOS

Photo 1.  PVC canister and temperature probe…………………………………………………………18

Photo 2.  E. Br. of De Nevue Cr. looking upstr. toward the wooden bridge near Lakeside lagoons...20

Photo 3.  Eden WWTF outfall…………………………………………………………………………….20

Photo 4.  E. Br. to De Nevue Cr. looking downstream from near the Eden WWTF…………………..22

Photo 5.  Measuring flow at Sit e ED2 below the Eden WWTF………………………………………...24

Photo 6.  E. Br. of De Nevue Cr. above Lime Rd. looking upstream past dam………………………..26

Photo 7.  E. Br. of De Nevue Cr. above Lime R. below dam looking upstream………………………..26

Photo 8.  Fish sampling Site ED3 on the E. Br. of De Nevue Cr. below Lime Rd……………………..27

Photo 9.  E. Br. of De Nevue Cr. Site ED5 looking upstream above Rhinehardt Rd………………….30

TABLE OF APPENDICES

APPENDIX A.  2003 De Nevue Creek Chemistry Data……………………………………………….40

APPENDIX B.  Macroinvertebrate Data……………………………………………………………….43

APPENDIX C.  De Nevue Site D1 2008 Monthly Chemistry Data and Eden WWTF TP…………..52

APPENDIX D.  2009 Chemistry and Flow Data……………………………………………………….60

ACKNOWLEDGEMENTS

The WDNR employees that contributed to field work on this study were in alphabetical order:

Chad Cook, Wastewater Specialist

Shannon Davis, Fisheries Technician

Jeff Haack, Water Quality Limits Coordinator

Michelle Lehner, Wastewater Specialist

Keith Otis, Fisheries Research Specialist

Randall Piette, Fisheries Research

Michael Reif, Wastewater Specialist

Mark Stanek, Wastewater Engineer

Explanations of what each individual did during the study are in the METHODS AND STUDY AREA part of this report.

SUMMARY OF FINDINGS

The De Nevue Creek Subwatershed including East and West Branches was studied from 2002 through 2008 to determine the Use Designations of each Segment.  The classifications determined are listed in Tables 1, 2 and 3.

Table 1.  East Branch of De Nevue Creek Segment Classifications.

| Segment | Miles | Segment Description | Current Classification | Attainable Use Classification | Comments |
| --- | --- | --- | --- | --- | --- |
| I | 0 | Origin atTwin Lakes | WWSF/ DFAL-GF | WWSF/ DFAL-GF | The E. Br. Originated in Twin Lakes south of Eden |
| II | 1.22 | Twin Lakes Outlet to the Village of Eden WWTF Outfall | LFF/TFAL | LFF/TFAL | This Segment had low flows in summer though still perennial |
| III | 5.19 | Village of Eden WWTF Outfall downstream to mouth of E. Br. Of De Nevue Cr. at confluence with the W. Br. Of De Nevue Cr. | WWFF/ DFAL-NG | WWFF/ DFAL-NG Seasonal DFAL-GF | This Segment was significantly degraded by the WWTF effluent, dam above Lime Rd. and numerous farm ponds intersecting springs |

Table 2.  West Branch of De Nevue Creek Segment Classification.

| Segment | Miles | Segment Description | Current Classification | Attainable Use Classification | Comments |
| --- | --- | --- | --- | --- | --- |
| I | 5.93 | Origin downstream to confluence with E. Br. Of De Nevue Cr. | WWFF/ DFAL-NG | WWFF/ DFAL-NG | This Segment had only 1/5 the base flow of the E. Br. |

Table 3.  De Nevue Creek Main Stem Segment Classification.

| Segment | Miles | Segment Description | Current Classification | Attainable Use Classification | Comments |
| --- | --- | --- | --- | --- | --- |
| I | 4.44 | De Nevue Cr. from confluence with E. and W. Br. Of De Nevue Cr. downstream to the mouth at Lake Winnebago | WWFF/ DFAL-NG | WWFF/ DFAL-NG Seasonal DFAL-GF |  |

The origin of the E. Br. Of De Nevue Cr. was at Twin Lakes located south of the Village of Eden.  I did not evaluate this lake but locals informed me that it is fished for panfish and bass.  That would warrant a Warm Water Sport Fish classification.  I did not observe the Lake’s two outlets south of CTY B but I did observe the west outlet above the Lakeside Foods cooling water outfall and found it to always have some flow.  The flow from there down to above the Village of Eden WWTF outfall was found to be sufficient to sustain a small community of tolerant fish such as fathead minnows and creek chubs.  It was also able to sustain a macroinvertebrate community with some higher quality species such as mayflies and caddisflies but was highly dominated by sow bugs.  As a result I was only able to classify the Segment (Segment II) from Twin Lakes down to the WWTF outfall as Limited Forage Fishery (LFF).

Near the WWTF outfall the Creek began to pick up more springs increasing baseflow.  The flow from the WWTF aids this.  We were able to find an improved, though still tolerant, fish community at the mixed point below the WWTF outfall.  The fish community was dominated by fish tolerant to habitat alterations such as White Suckers and Creek Chubs.  This was true at all sites where the fish community was evaluated.  From this point downstream I have classified the E. Br. of De Nevue Cr. WWFF or DFAL-NG under the 2004 guidance.  Flow and temperature were sufficient to sustain a WWFF even though the what was found indicated significant problems.  These problems likely resulted throughout the E. Br. Subwatershed from sources including the Eden WWTF, agricultural runoff, wetland drainage, and discharge from farm ponds where were prevalent throughout the Subwatershed.  The farm ponds appeared to intercept many of the spring inputs to the E. Br. of De Nevue Cr.

The dam located above Lime Rd. appeared to have a significant negative effect on the E. Br. of De Nevue Cr.  Improvement of the E. Br. of De Nevue to meet present and Attainable Use Designations will require the removal of this dam and re-establishment of the natural stream channel.

The E. Branch Segments II and III continuous summer temperatures recorded indicated coolwater conditions.  However, coolwater fish species such as Pearl Dace and Brassy Minnows were not found.  Since flow and temperature were sufficient to sustain these species there were likely non-natural Subwatershed problems that need to be corrected to sustain these fish.  I have already touched on several of those.

INTRODUCTION AND STUDY AREA OVERVIEW

INTRODUCTION

De Nevue Cr. was studied to update its Use Designation since that hadn’t been done since the original one was done in 1975 by Weisensel and Mazanet (1975) and in 1982 by Keith Hutchison (1982).  Since this original classification was done so long ago and was narrow in scope and new criteria and methodology had changed significantly a new reclassification study was started in 2002.  A map of the Study Area is in Figure 1.  At the time of this writing, De Nevue Cr. was delineated as an Unnamed Tributary to De Nevue Cr. (WBIC 139100) which originated in Twin Lake south of the Village of Eden and flowed north to below Rhinehardt Rd. where it met with what was listed as the main stem of De Nevue Cr.  For the purposes of this report I will be calling the Trib. To De Nevue Cr. down to below Rhinehardt Rd. the East Branch and the other Trib. that comes from the west and combines with the East Branch below Rhinehardt Rd. the West Branch of De Nevue Cr.   From the confluence  point of these two Branches I will be calling the Creek De Nevue Creek (WBIC 138700).    In Hutchison’s Stream Classification he also called the Branch by the WWTF the East Branch to DeNevue Cr.  At that time the discharge point was in the same place it was during this survey.  At that time, as  now,  the discharge was to an approximately 50 yard long channel before entering the Creek.  He classified this channel as marginal surface water with the reasoning that there would be no flow when the WWTF was not discharging.  He also classified the E. Br. to De Nevue Cr. as continuous intermediate aquatic life (as did Weisensel and Mazanet (1975)) which corresponds to limited forage fishery (LFF) in the current Wis. Adm. Code NR 104 classification system.  I will be maintaining that as the current classification above the WWTF but will be allowing for an upgrade to warm water forage fishery (WWFF) below the WWTF.  I will also be allowing for seasonal  Warm Water Sport Fish (WWSF) based on potential changes in the watershed as discussed later in this report.  WWFF and WWSF are full fish and aquatic life use categories according to Wis. Adm. Code NR 102.   I am classifying the channel the WWTF discharges to also as LFF since the WWTF discharges continuously and there were springs at the base of the discharge which appeared to work most of the time.  These conditions would allow for the forage fishery of the E. Br. of De Nevue to freely move in and out of this channel.

The East Branch of De Nevue Cr. actually originated in Twin Lakes located about ½ mile southeast of the Village of Eden.  I don’t have first hand knowledge of Twin Lakes but locals have told me that it is fished for large mouth bass and pan fish.  Twin Lakes actually had two outlets (one going though Eden which is commented on in Weisensel (1975) and one that goes around the eastern boundary of the Village of Eden where it flows through at least 3 fairly large ponds created by damning the Lake outlet stream).  This last mentioned outlet entered the East Branch of De Nevue about ¼ mile below the WWTF outfall.  As also mentioned in the Weisensel report, springs enter De Nevue above and below the WWTF and downstream.  It appears they work well due to the steep topography along the Creek.  This was the case at least to the east all the way to at least Lake De Nevue due to to the steep Niagara Escarpment there from which originated many springs.  Groundwater pressure to create springs is also evidenced by at least one of the ponds located just to the south of Lime Rd. about ½ mile below the WWTF.  By my few observations this pond had a good outflow to the East Branch due to go groundwater inflow.  This was confirmed by the discussion I had with the owner who told me the same.

DENEVUE CREEK STUDY AREA AND METHODS USED

As stated above, De Nevue Cr. has been separated into 3 sub-watersheds:  1) the East Branch of De Nevue Cr (Figure 1a).; 2) the West Branch of De Nevue Cr. (Figure 1b); and 3) the Main Stem of De Nevue Cr. (Figure 1c).   A table of the Study Area stream sites is in Table 1.  As stated above, the East Branch of De Nevue Cr. started in Twin Lakes south of the Village of Eden and picked up springs as it flowed north of Eden.  The Village of Eden WWTF discharged to the E. Br. just downstream from the Village.

Table 4.  De Nevue Cr. Stream Class Study Site Descriptions.

| Site | Distance From L. Winn. Mouth (miles) | Distance From Branch Mouth (miles) | SWIMS Station ID | Type of Sampling | Location |
| --- | --- | --- | --- | --- | --- |
| ED1 | 9.57 | 5.13 | 10022707 | C,F,M,T,V | E. Br. to DeNevue Cr. 200 feet above Eden WWTF outfall |
| Eden WWTF | 9.54 | 5.10 | 10022708 | TFD,V | Village of Eden WWTF Outfall |
| ED2 | 9.52 | 5.08 | 10022709 | C,F, T,V | E. Br. to DeNevue Cr. Mixed Pt. below Eden WWTF |
| ED3 | 8.96 | 4.52 | 10016483 | C,F,M,T,V | E. Br. to DeNevue Cr. at Lime Rd. |
| ED4 | 6.63 | 2.19 | 10010866 | C,F,M,T,V | E. Br. to DeNevue Ct. above Mill Rd. |
| ED5 | 4.63 | 0.19 | 10015850 | C,T,V | E. Br. to DeNevue Cr. above Rhinehardt Rd. |
| LD1 | - | 0.44 |  | T,V | L. DeNevue Outlet Trib. at CTH K |
| WD1 | 7.81 | 3.37 |  | V | W. Br. to DeNevue Cr. at Rademann Quarry influent point at Kelly Rd. crossing |
| WD2a | 6.18 | 1.74 |  | C,V | W. Br. to DeNevue Cr. above Boyke property |
| WD2b | 5.92 | 1.48 |  | C,V | W. Br. to DeNevue Cr. below Boyke property |
| WD3 | 4.81 | 0.37 | 10007742 | C,M,T,V | W. Br. to DeNevue Cr. above Rhinehardt Rd. |
| D1 | 1.93 | - | 1007739 | C,F,H,M,V | DeNeveu Cr.-200 feet above 4th St. Bridge |
| D1c | 4.44 | - | - | V | DeNevue Cr. at confluence with E. and W. Branches |

C=Chemistry; F=Fish; M=Macroinvertebrates; T=Temperature (Tidbit); TFD=Treatment Facility Data; V=Visual

Table 5.  De Nevue Cr. and Branch Segment Lengths.

| Segment | Length in Miles |
| --- | --- |
| East Branch of De Nevue Cr. | 6.41 |
| West Branch of De Nevue Cr. | 5.93 |
| De Nevue Cr. Main Stem (from L. Winn. To Confl.) | 4.44 |
| L. De Nevue Outlet (from L. De Nevue to E. Br.) | 0.70 |

Table 6.  Table of Subwatershed acreages.

| Subwatershed | Total Acres |
| --- | --- |
| East Branch of De Nevue Creek Subwatershed | 7281 |
| West Branch of De Nevue Creek Subwatershed | 3064 |
| De Nevue Creek Main Stem Subwatershed | 4183 |
| Total | 14522 |

Fish Community Assessment

Fish Surveys were conducted as described in Guidelines for Assessing Fish Communities of Wadable Streams in Wisconsin (WDNR, 2000).  Fish surveys were conducted by Michael Reif, Mark Stanek and Jeff Haack.   Fish field identifications were done on all Sites by Michael Reif.  A few fish that could not be identified in the field were preserved in formalin and finally identified at the Oshkosh DNR office lab.

Habitat Assessment

Habitat assessment at nearly all the fish assessment sites and many of the macroinvertebrate sites was conducted as described in Guidelines for Evaluating Habitat of Wadable Streams (WDNR, 2000).  Habitat

Surveys at ED1 and ED4 were conducted by Michael Reif and  Shannon Davis-Foust. Habitat Surveys done at ED2 was by Michael Reif and Michelle Lehner.  Instantaneous flows were taken at each habitat site with a Swoffer Instruments, Inc. Model 2100 Series current meter.  This meter was also used for all other flow measurements taken during this Study.  Data was evaluated according to Fish Habitat Rating-Streams (FHR-Streams) as described in Guideline for Evaluating Fish Habitat in Wisconsin Streams (Simmons, Lyons and Kanel, 1994).

Macroinvertebrate Community Assessment

Macroinvertebrates were collected in the spring of  2004 from Sites ED2, ED3, and ED5.  Macroinvertebrates were also sampled from those Sites in the spring of 2008 as well as WD3 and D1.  Samples were delivered to the University of Wisconsin-Stevens Point Aquatic Entomology Lab for identification.  Data and analyses can be found in the SWIMS database as well as in this report.

Water Quality Assessment

Onset temperature loggers were placed at Sites ED1, ED3, ED4, and D1 in the spring, summer and fall of 2004.  Probes were installed at Sites ED3,ED4 and WD3 in 2008. Loggers were attached inside PVC canisters (see Photo 1) that had slits cut in 2 sides to allow water to freely pass through and create a continuous flow past the probe.  The canisters were attached to rebar pounded into the stream bottom.  The canisters were either allowed to lay on the hard gravel bottom in riffles to keep them in the flow and from sedimenting over.  Figures of the graphs from the temp. logger data are distributed in the main part of this report while the raw avg., min, and max.’s for each site are tables in Appendix A.  Instantaneous temperature and D.O. measurements were taken through the study with a YSI 55 or YSI 85 meter.  Chemistry samples were collected in June of 2003 from sites ED1, ED3, ED4 and ED5.  These data are in Appendix A.  Summer monthly chemistry samples for T-P, O-P, Temp., D.O., Cond., and Chlorides were taken from Site D1 as part of the 2007 Non-LTT Monthly Stream Monitoring.  These data are in Appendix C along with the Eden WWTF T-P for 2007.  Chemistry samples and flows were collected from Sites ED5 and WD3 in the spring of 2009 (see Appendix D).

ANALYSES AND DISCUSSION

Site ED1 on the E. Br. of De Nevue Cr. was located above the Village of Eden WWTF outfall.  It was located as a background to the Village of Eden WWTF outfall discharge.  It was downstream from the cooling water outfall of  Lakeside Foods Inc. of Eden at the RR tressel.  The Lakeside cooling water normally discharged between June and November.  Data could have been influenced by it during that period.  A temperature meter was installed in the Creek about 200 feet above the WWTF outfall confluence in  the summer of 2005.  One was installed in the same location in the summer of 2004 but it was lost in the floods of may and June.  The data from 2005 are illustrated in Figure 5 and Tabled in Appendix A1.   The daily averages appear to be in a reasonable range.  The maximums varied  a lot and reached fairly high levels (26 to 28 Deg. C).  As I already stated, data may have been modified by the cooling water from Lakeside.

It is notable that Site ED1 had exposed bedrock from bank to bank just below the RR Tressel.  This point could be significant in evaluating where and how to construct any additions or modifications of the Village of Eden WWTF.

Figure 5.  E. Br. De Nevue Cr. Site ED1 (above the Village of Eden WWTF) summer 2005 temp. data.

A macroinvertebrate sample was collected on October 9, 2002 from Site ED1 from riffles along side the Lakeside lagoons (above and below the RR tressel).  The HBI derived from this sample was 7.375 indicating poor water quality.  There were very large numbers of Asellus sp (HBI value of 8) in this site (72.4% of the total 490 picked) which had a large influence on the final HBI value.  There were 3 species of Baetis there likely because there was a good growth of aquatic plants these mayflies like to inhabit.  The second most abundant species was Hydropsyche betteni.  Along with the other caddisflies and the mayflies indicates the E. Br. of DeNevue at ED1 to be a permanent (perennial) stream though the normal summer base flow appeared to be in the range of  0.1 cfs or less.  Only 4 individuals of Gammarus were found in the 490 picked from the ED1 macroinvertebrate sample.  This is another indicator of low flows with little spring inflow though all observations I had of this site were that the Creek was perennial there even in low flow years.

Figure 6.  Summer 2004 daily Air Temp. data collected at the Eden WWTF.

Figure 7.  Summer 2008 daily Air Temp. data collected at the Eden WWTF.

Table 7.  Habitat data collected from Site ED2 (mixed point below the Eden WWTF) Aug. 31, 2005.

| Parameter | Calculated Value | Score | Rating |
| --- | --- | --- | --- |
| Riparian Buffer Width | 0m | 0 | Poor |
| Bank Erosion | 0.08m | 15 | Excellent |
| Pool Area | 10.7% | 3 | Fair |
| Width:Depth Ratio | 10.3 avg. thalweg | 10 | Good |
| Riffle:Riffle Ratio | 18.0 | 5 | Fair |
| Fine Sediments | 38.3% | 5 | Fair |
| Cover For Fish | 0 | 0 | Poor |
| Total |  | 38 | Fair |
| Flow | 0.587 cfs |  |  |
| WWBI |  | 0 | Very Poor |
| CWB1 |  | 0 | Very Poor |

Habitat data was collected from Site ED2 from the mixed point below the Village of Eden WWTF downstream (Table 2).  The habitat was found to be fair.  This site was completely open to the sun since it was in a pasture.  The fishery was sampled at ED2 on Aug. 12, 2004.  As with other sites on this Creek, the fishery was dominated by Creek Chubs which had a large effect on the Very Poor WWIBI  rating of 0.

Table 8.  Fish data from the E. Br. of De Nevue Cr. Site ED2 (below Eden WWTF ) August 12, 2004.

| Scientific Name | Common Name | Number Collected | Tolerance |
| --- | --- | --- | --- |
| Catostomus commersoni (Lacepede) | White Sucker | 39 | Habitat |
| Culaea inconstans (Kirtland) | Brook Stickleback | 3 | D.O. |
| Luxilus cornutus (Mitchill) | Common Shiner | 9 | - |
| Nocomis biguttatus (Kirtland) | Hornyhead Chub | 4 | - |
| Semotilus atromaculatus (Mitchill) | Creek Chub | 41 | Habitat |
| Umbra limi (kirtland) | Central Mudminnow | 4 | D.O. |
| Total |  | 100 |  |
| WWIBI |  | 0 | Very Poor |

Figure 8.  De Nevue Cr. gradient including East Branch.

Figure7.  E. Br. De Nevue Cr. Site ED3 (below Lime Rd.) summer 2004 daily temp. data.

Figure 8.  E. Br. De Nevue Cr. Site ED3 (below Lime Rd.) summer 2008 daily temp. data.

Site ED3 was located on the E. Br. of DeNevue Cr. above and below Lime Rd.  Macroinvertebrates were collected from a riffle above Lime Rd. in the fall of 2002.  Data from that sample are listed in Appendix Table B2.  The HBI was determined to be 5.471 indicating good water quality (i.e. some organic pollution, Hilsenhoff, 1987).  While collecting the sample I observed very large numbers of Hydropsychidae (Hydropsyche betteni and a species of Cheumatopsyche sp were sub-sampled during laboratory picking in equal numbers).  Due to proximity, this site was likely influenced by the Dam above Lime Rd. (see Photo 6 and Figure 4) and discharge from the ponds (spring fed connected enlargements) above Lime Rd. (See Figure 3).

Macroinvertebrates were also sampled in the spring of 2008.  The resultant HBI was 5.050.  That sample did not have the dominant number of Hyrdropsyche betteni and Cheumatopsyche sp as in 2002.  I also observed that it overall numbers of insects in my net were less than in 2002.  Even though the HBI was higher in 2008 there appeared to have been something that caused a reduction in macroinvertebrate densities.

A temperature monitor was located in a riffle/run below Lime Rd. in the summer of 2004 and summer of 2008.  Somehow they stayed stable in the high flows of spring 2004 and 2008 when other probes at Sites ED1, ED4 and D1 were washed away.  Initial rainfall in early June 2008 was high as well as left over flows from the heavier than normal 2007-08 snow falls.  The rest of the summer was normal for rainfall.  I mention this since it may be related to the higher general deviation of the min. and max. from the avg. in 2008 than in 2004.  This greater deviation from the mean may have a negative impact on the aquatic life.

Table10.  Fish data from E. Br. of De Nevue Site ED3 (below Lime Rd.) Aug. 12, 2004 sampling.

| Scientific Name | Common Name | Number Collected | Tolerance |
| --- | --- | --- | --- |
| Catostomus commersoni (Lacepede) | White Sucker | 16 | Habitat |
| Etheostoma nigrum Rafinesque | Johnny Darter | 10 | - |
| Lepomis macrochirus Rafinesque | Bluegill | 11 | - |
| Luxilus cornutus (Mitchill) | Common Shiner | 8 | - |
| Micropterus salmloides (Lacepede) | Largemouth Bass | 3 | - |
| Nocomis biguttatus (Kirtland) | Hornyhead Chub | 3 | - |
| Pimephales promelas (Rafinesque) | Fathead Minnow | 2 | - |
| Rhinichthys atratulus (Hermann) | Blacknose Dace | 3 | Habitat |
| Semotilus atromaculatus (Mitchill) | Creek Chub | 94 | Habitat |
| Umbra limi (kirtland) | Central Mudminnow | 1 | D.O. |
| Total |  | 151 |  |
| WWBI |  | 2 | Very Poor |
| CWIBI |  | 0 | Very Poor |

A fish species list for Site ED3 is in Table 4.  As will all other sites on the Creek sampled for fishery this site was dominated by Creek Chubs which had a major impact on the Very Poor  WWIBI rating of 2.  Some small young of the year largemouth bass and blugill were found but these were likely from local spring fed farm ponds rather than indigenous to the Creek itself.

A list of habitat data for Site ED4 below Mill Rd. is in Table 5.  Habitat analyses determined a Fair habitat.  This site was mostly shaded with a good mix of riffles and pools and good gravel/rubble substrate.  The poor riffle:riffle analysis and poor ocver for fish had a significant effect on the result.  A fish species list for Site ED4 below Mill Rd. is in Table 6.  As with the other sites on this Creek the base fishery was dominated by Creek Chubs with other general tolerant fish making up most of the rest of the numbers.  As with other sites this resulted in a Very Poor WWIBI of 0.

Figure 9.  E. Br. De Nevue Cr. Site ED4 (above Mill Rd.) summer 2008 daily temp. data.

Table 5.  E. Br. of DeNevue Cr. Site ED4 habitat data collected Aug. 27, 2003.

| Parameter | Calculated Value | Score | Rating |
| --- | --- | --- | --- |
| Riparian Buffer Width | 8.5m | 10 | Good |
| Bank Erosion | 0.45m | 10 | Good |
| Pool Area | 27.5% | 3 | Fair |
| Width:Depth Ratio | 13.0 | 10 | Good |
| Riffle:Riffle Ratio | 27.8 | 0 | Poor |
| Fine Sediments | 26.0% | 5 | Fair |
| Cover For Fish | 3% | 0 | Poor |
| Total |  | 38 | Fair |
| Flow | 1.039 cfs |  |  |
| HBI 2002 |  | 4.555 | Good |
| HBI 2008 |  | 5.467 | Good |
| WWBI |  | 0 | Very Poor |
| CWB1 |  | 0 | Very Poor |

Table 6.  E. Br. of DeNevue Cr. Site ED4 (above Mill Rd.) fish data collected Aug. 27, 2003.

| Scientific Name | Common Name | Number Collected | Tolerance |
| --- | --- | --- | --- |
| Catostomus commersoni (Lacepede) | White Sucker | 7 | Habitat |
| Etheostoma nigrum Rafinesque | Johnny Darter | 5 | - |
| Nocomis biguttatus (Kirtland) | Hornyhead Chub | 5 | - |
| Rhinichthys atratulus (Hermann) | Blacknose Dace | 9 | Habitat |
| Semotilus atromaculatus (Mitchill) | Creek Chub | 74 | Habitat |
| Lepomis cyanellus Rafinesque | Green Sunfish | 1 | D.O. |
| Total |  | 101 |  |
| WWIBI |  | 0 | Very Poor |

A photo of the downstream end of Site ED4 above Mill Rd. is on the cover page of this report.  Macroinvertebrates were collected from Site ED4 in Oct. 9, 2002 during that fall sampling.  The Site had quality habitat indicated by numerous riffles and riffle/gravel habitat.  The HBI determined from this sample was 4.555 indicating good water quality.  Of the fall 2002 sites sampled for macroinvertebrates on the E. Br. of DeNevue Cr. Site ED4 had the best HBI value.  It should also be noted that the HBI was near the Very Good HBI level of 4.50.  Along with the quality of habitat as well as stable low flows (high flows were extensive at times such as the floods of May-June 2004 and spring of 2008) the temperature regime indicated by the graph of the min., max. and avg. in Figure 9 for the summer of 2008 normally stayed in the range between 15 Deg. C and 20 Deg. C while the min. and max. values deviated from the mean very little through the summer.  This lack of deviation from the mean (tightness of data) indicates stability in temperature and could be important in establishing a trout population in the future.  The observations I made at this site in the winter indicated significant ice cover during the cold parts of winter.  For sites like this, I did not leave a continuous temp. meter in the winter due to high potential of loss from ice movement.  This ice cover also indicates to me a high likelihood that salmonid eggs and fry would not be able to make it through the winter.

Macroinvertebrates were also sampled in the spring of 2008 along with Sites ED3 and D1.  As indicated in the writing of those 2 sites the macroinvertebrate populations appeared sparce and not of the quality I would have expected from this site in the spring.  I did not observe any Limnephilidae such as Pycnopsyche sp and Limnephilus sp as I observed in other years at Site ED5.  The habitat of Site ED4 was such that I would have expected large numbers of these Tricopterans there.  I conclude from this a water quality problem occurred in the E. Br. of DeNevue Cr. during at least the last year since these species have a 1 year life cycle hatching and laying eggs mainly in the fall during leaf fall since that is the main food source.  I also did not find large number of Hydropsychidae as I would have expected from this site.

I talked with the neighbor of Site ED4 on several occasions while conducting this study.  He owned 20 acres on both sides of the Creek upstream from Mill Rd.  He showed us where at least before the 1930’s a mill was located south of Mill Road with a large pond (impoundment formed by damning the East Branch ) upstream from Mill Rd. on what was during this study his property.  He said the pond was at least 2-3 acres in size.  When the mill was there a channel ran from the impoundment down to and under Mill Rd. to the Mill to operate the water wheel at the Mill.  He showed me photos of the family that owned the Mill from the 1930’s boating and swimming on pond in the summer and skating on the pond in the winter.  This impoundment was gone during this study through remnants of it are still there.  In the 1920’s there were few trees on the land.  During this study his 20 acres was mostly forested including where the pond was.  I believe historical information on this old Mill can be found in Fond du Lac along with the original water wheel.

A model done by John Lyons in 2007 indicated the potential of DeNevue Cr. to be a trout stream.  Site ED4 give some indication through temperature data that this may be a real possibility.  However, as mentioned in other parts of this report, that potential can only be realized if all farm ponds intersecting springs be eliminated or at least modified so the springs can function in a positive way on the temperature of De Nevue Cr.  The Dam upstream from Lime Rd. will clearly also have to be removed.

Figure 10.  E. Br. DeNevue Cr. Site ED5 (above Rhinehardt Rd.) summer 2004 daily temp. data.

Site ED5 on the E. Br. of DeNevue Cr. above Rhinehardt Rd., as with Site ED4, had high quality habitat mixing riffles with runs and pools and having good amounts of quality gravel/rubble substrate.  Also, as with ED4 it had a good base flow but was subject to very high flows during runoff times such as the spring of 2008 when I lost the temperature probe that I placed in this Site.  This was also evidenced by some of the large willow trees on the banks falling over the Creek at ED5 in spring 2008.

Figure 11.  W. Br. of DeNevue Cr. Site WD3 (above Rhinehardt Rd.) 2008 summer daily temp.  data.

The W. Br. of DeNevue Cr. Site WD3 located above Rhinehardt Rd. was analyzed in 2008 using a daily temp. recorder (see Figure 11 for the illustration of these data).  These daily temperatures indicated a good temperature regime though not quite as good as at Sites ED4 and ED5 on the E. Br.  Sites ED5 and WD3 are good sites to make comparisons between the two branches of DeNevue Cr.  The base flow of WD3 was also clearly less than the E. Br. at ED5.  Chemistry data and flows were collected from Sites ED5 and WD3 on June 1, 2009.  These data are in Appendix D.  These samples were also non-event samples so I could evaluate the normal flow conditions of each branch.  The flow of ED5 was measured to be 2.190 cfs while the flow of WD3 was found to be 0.458 cfs.  This was a near 5X greater flow at ED5 compared to WD3.  The visual characteristics of these two branches clearly illustrates this as well.  Actual habitat measurements were not obtained at either site.

Figure 12.  Aerial Photo of Sites ED5 and WD3 and confluence of E. and W. Branches of  De Nevue Cr..

Site D1 was used to describe the DeNevue Cr. Main Stem Subwatershed (see Figure 13).  That site was located adjacent to the Fond du lac City Park at the SW corner of 4th St. and National Ave.  It was chosen for its location and a point where it would likely describe the DeNevue Cr. Main Stem segment well.  Site D1 was used for the Oct. 2007 to Sept. 2008 NON-LTT sampling.  These data are in the Tables in Appendix C.  I summarized the T-P and SS data from these monthly samplings and Tabled them in Table 7.  The T-P correlates fairly well with SS (see Figure 12) with an R2 of 0.8228.  SS was fairly high at this site during the May through September months despite most samplings being during non-event conditions.  As a result, the SS can be said to generally not be related to runoff.  I can only speculate the source of the SS.  One possibility is algae from the impoundment above Lime Rd. and the ponds on the Lake DeNevue Outlet.  This Outlet Trib. entered the E. Br. of DeNevue Cr. above Site ED5 above Rhinehardt Rd. (see Figure 16).  A similar T-P to SS situation was found during the June 2009 sampling of Sites ED5 and WD3 (see Tables D1 and D2 in Appendix D).  The T-P and SS were higher at ED5 than WD3 despite there being no runoff conditions.  So, from the data that I have I conclude that the source of the SS is from the E. Br. more so than the W. Br. under non-event flow conditions.  The opposite may be true under runoff conditions since the West Branch is very agricultural.

In addition to the E. W. and Main Stem of DeNevue Cr. I also collected some temperature and general visual data from the outlet of Lake DeNevue.  In the summer of 2004 I had a tidbit recorder in the Trib. just below CTH K.  The graph of these data is in Figure 15.  Note how tight the data are about the mean throughout the summer.  This situation is complex.  Normally the effluent from a lake is warm in the summer since the discharge primarily drains the top layer of the lake (assuming a broad litoral zone to the point of discharge).

Figure 13.   West Branch of De Nevue Cr. and De Nevue Cr. Main Stem gradient.

The gradient of the West Branch of De Nevue Creek combined with the main stem of De Nevue Creek is in Figure 13.  As with the East Brach the gradient throughout the West Branch of fairly uniform though it did reduce some in the last mile of the reach between WD2a and the confluence with the E. Br.  Though the gradients were similar the base flow of the West Branch was about 1/5 that of the E. Branch.  It did not have the spring flow advantage of being closer to the steep escarpment that ran along the east side of most of the reach of the E. Branch.  The West Branch Subwatershed was even more agricultural (percentage of the Subwatershed) than the E. Branch and had a lot of steep slopes of fields running to the Creek (as with the E. Branch) allowing for high potential for runoff.

Figure 14.  East Branch of De Nevue Cr. and De Nevue Ct. Main Stem gradient.

Figure 15.  Aerial Photo of Site D1 (1 inch = 180 feet).

| Table 12. Total Phosphorus monthly NON LTT sampling data from Site D1 (2007-2008). |
| --- |
| Date | T-P mg/l | SS mg/l |  |  |  |  |  |
| 24-Oct-07 | 0.179 | 17 |  |  |  |  |  |
| 19-Nov-07 | 0.046 | 3 |  |  |  |  |  |
| 12-Dec-07 | 0.055 | ND |  |  |  |  |  |
| 10-Jan-08 | 0.358 | 69 |  |  |  |  |  |
| 7-Feb-08 | 0.085 | 3 |  |  |  |  |  |
| 30-Apr-08 | 0.047 | 3 |  |  |  |  |  |
| 21-May-08 | 0.091 | 6 |  |  |  |  |  |
| 26-Jun-08 | 0.195 | 37 |  |  |  |  |  |
| 15-Jul-08 | 0.188 | 26 |  |  |  |  |  |
| 20-Aug-08 | 0.177 | 25 |  |  |  |  |  |
| 17-Sep-08 | 0.185 | 18 |  |  |  |  |  |

Figure 16.  Regression chart for data in Table 11.

Figure 17.  Tidbit temp. data for Lake De Nevue Trib. immediately below CTH K (summer 2004).

Figure 18.  Aerial photo of Lake De Nevue and its outlet.

Table 13.  De Nevue Creek T-P (mg/l) data from June 17, 2003 sampling (a non-event sampling).

| Site | Result (mg/l) |
| --- | --- |
| ED1 | 0.158 |
| ED3 | 0.381 |
| ED4 | 0.268 |
| ED5 | 0.336 |
| D1 | 0.313 |

Total Photosphorus Evaluation of De Nevue Cr.

Data collected during this study indicate the E. Br. of De Nevue Cr. and the main stem of De Nevue Cr. do not meet the proposed T-P standard of 0.075.  This proposed standard can be found in the 2010 WisCALM Guidance (WDNR, 2009).  The T-P data collected from several sites on these branches on June 17, 2003 are in Table 8.  The T-P data collected during the 2007-08 NON-LTT sampling at Site D1 are in Table 7.  All samples collected during the 2003 sampling exceed the 0.075 mg/l T-P proposed standard as well as the 0.100 mg/l T-P standard listed in proposed rule NR 102.03(3).  It is notable that the highest T-P concentration in 2003 was from Site ED3 below Lime Rd.  Reasons for this were likely: 1) that ED3 was below the Village of Eden WWTF which discharged T-P on the June 17 sampling date of 0.686 mg/l (24-hour composite) and a T-P range of 0.618 and 1.411 mg/l in the month of June 2003 (see Appendix A Table A6); and 2) that ED3 was below the impoundment located above Lime Rd.  It was likely that algae growth was high in this impoundment which resulted in T-P being concentrated in algal cells and carried downstream.  I observed this concentrating of T-P in algae during the 1985-1987 Fox River Chlorophyll a study (Reif, 1987).  It is also notable that the T-P data exceeded the 0.075 mg/l proposed value in the 2007-08 NON-LTT sampling at Site D1 for the months of Oct. 2007, Feb. 2008 and May through Sept. 2008 with the highest concentration of  0.195 mg/l in June.  It is also notable that in the same data the proposed 0.100 mg/l T-P standard was exceeded in the months of Oct. 2007 and June-Sept. 2008.  T-P concentrations were significantly higher in the summer than winter.  One reason for this was possibly that planktonic algal populations were higher in the summer and thus able to concentrate more T-P.  I did not sample for chlorophyll a during this study but the NON-LTT samples were analyzed for SS which correlated well with the T-P (see Figure 12.  The Village of Eden WWTF T-P data for the 2007-08 NON-LTT sampling are listed in Table C12 of Appendix C.  Since the NON-LTT samples were collected during non-event conditions it is likely that most of the T-P sampled was from the Eden WWTF.

LITERATURE CITED

Hilsenhoff, W. L.  1987.  An Improved Biotic Index of Organic Stream Pollution.  The Great Lakes Entomologist.  Vo. 20(1): 31-39.

Hutchinson, K. F.  1983.  Stream Classification of the E. Br. of DeNevue Creek at Eden.  WDNR.  1 p.

Weisensel, D. C. and J. L Mazanet.  1975.  Eden, Fond du Lac County, Wastewater Receiving Stream Classification.  WDNR.  4p.

Reif, M. D.   Fox River-Oshkosh Chlorophyll a Water Quality Relationships, 1985-1987.  WDNR, 100 p.

Reif, M. D.  2009.  Stream Classification of Parsons Creek, Fond du Lac Co., Wisconsin.  May 2009.  87 p.

Reif, M. D.  2010.  Stream Classification of Campground Creek, Fond du Lac Co., Wisconsin.  May 2009.  112 p.

WDNR, 2004.  Guidelines for Designating Fish & Aquatic Life Uses for Wisconsin Surface Waters.  Pub-WT-807-04.  60 pp.

APPENDIX A

2003 De Nevue Creek Chemistry Data

APPENDIX B

Macroinvertebrate Data

Table B1.  E. Br. of DeNevue Cr. Site ED1 (above Eden WWTF outfall along side the Lakeside Foods lagoons) macroinvertebrate data collected October 9, 2002.

Table B2.  East Branch of DeNevue Cr. Site ED3 (above Lime Rd.) macroinvertebrate data from sample collected October 9, 2002.

Table B3.  E. Br. of DeNevue Cr. Site ED3 (above and below Lime Rd.) macroinvertebrate data from sample collected May 5, 2008.

| Taxa | # Counted | HBI Value |
| --- | --- | --- |
| Coleoptera |  |  |
| Elmidae |  |  |
| Dubiraphia sp | 1 | 6 |
| Optioservus sp | 7 | 4 |
| Stenelmis sp | 60 | 5 |
| Stenelmis crenata | 7 | 5 |
| Diptera |  |  |
| Chironomidae |  |  |
| Chironomini |  |  |
| Polypedilum (Uresipedilum) flavum | 1 | 5 |
| Orthocladiinae |  | - |
| Cricotopus (Cricotopus) pupae | 1 | - |
| Annulator complex | 4 | 7 |
| Hydrobaenus sp | 3 | 8 |
| Orthocladius pupae | 1 | - |
| Orthocladius (Orthocldius) sp | 9 | 6 |
| Tanytarsini |  |  |
| Cladotanytarsus sp | 1 | 7 |
| Psychodidae |  |  |
| Psychoda sp | 1 | 10 |
| Simuliidae |  |  |
| Simulium pupae | 1 | - |
| Ephemeroptera |  |  |
| Heptageniidae |  |  |
| Stenacron interpunctatum | 1 | 7 |
| Trichoptera |  |  |
| Hydropsychidae |  | - |
| Cheumatopsyche sp | 1 | 5 |
| Hydropsyche betteni | 1 | 6 |
| Amphipoda |  |  |
| Gammaridae |  |  |
| Gammarus pseudolimnaeus | 35 | 4 |
| Isopoda |  |  |
| Asellidae |  |  |
| Caecidotea intermedia | 4 | 8 |
| Hyroida |  |  |
| Hydridae | 1 | - |
| Nematoda | 1 | - |
| Oligochaeta | 6 | - |
| Naididae | 677 | - |
| Tubificidae | 72 | - |
| Tricladida | 5 | - |
| Total |  |  |
| Biotic Index |  | 5.050 |

Table B4.  E. Br. of DeNevue Cr. Site ED4 (above Mill Rd.) macroinvertebrate data from sample collected October 9, 2002.

Table B5.   . Br. of DeNevue Cr. Site ED4 (above Mill Rd.) macroinvertebrate data from sample collected May 5, 2008.

| Taxa | # Counted | HBI Value |
| --- | --- | --- |
| Coleoptera |  |  |
| Elmidae |  |  |
| Optioservus sp | 24 | 4 |
| Optioservus fastiditus | 4 | 4 |
| Stenelmis sp | 4 | 5 |
| Stenelmis crenata | 3 | 5 |
| Diptera |  |  |
| Chironomidae larvae | 2 | - |
| Chironomini pupae | 1 | - |
| Cryptochironomus sp | 4 | 8 |
| Paratendipes sp | 45 | 8 |
| Paratendipes (Pentapedilum) sp A Epler | 1 | 4 |
| Paratendipes (Tripodura) scalaenum group | 1 | 7 |
| Paratendipes (Uresipedilum) aviceps | 3 | 5 |
| Diamesinae |  |  |
| Diamesa sp | 9 | 5 |
| Orthocladiinae |  | - |
| Brillia flavifrons group | 1 | 5 |
| Corynoneura sp | 2 | 7 |
| Corynoneura pupae | 1 | - |
| Cricotopus (Cricotopus) pupae | 1 | - |
| Cricotopus annulator complex | 2 | 7 |
| Cricotopus infuscatus/triannula | 1 | 7 |
| Parkiefferiella sp | 1 | - |
| Parametriocnemus sp | 10 | 5 |
| Orthocladius (Orthocladius) sp | 17 | 6 |
| Cicotopus/Orthocladius sp | 1 | 5 |
| Tanytarsini |  |  |
| Rheotanytarsus pupae | 1 | - |
| Rheotanytarsus exiguus group | 1 | 6 |
| Tanypodinae |  |  |
| Conchapelopia sp | 1 | 6 |
| Empididae |  |  |
| Chelifera sp | 1 | 6 |
| Simuliidae |  |  |
| Simulium sp | 4 | - |
| Simulium verecundum “complex” | 6 | 6 |
| Simulium fibrinflatum | 3 | 6 |
| Ephemeroptera |  |  |
| Baetidae |  |  |
| Baetis sp | 12 | - |
| Baetis brunneicolor | 3 | 4 |
| Baetis flavistriga | 7 | 4 |
| Plecoptera |  |  |
| Capniidae |  |  |
| Allocapnia sp | 3 | 3 |
| Tricoptera |  |  |
| Hydropsychidae |  |  |
| Cheumatopsyche sp | 2 | 5 |
| Hydropsyche betteni | 2 | 6 |
| Ceratopsyche slossonae | 1 | 4 |
| Amphipoda |  |  |
| Gammaridae |  |  |
| Gammarus pseudolimnaeus | 46 | 4 |
| Isopoda |  |  |
| Asellidae |  |  |
| Caecidotea sp | 1 | - |
| Nematoda | 2 | - |
| Oligochaeta |  |  |
| Naididae | 137 | - |
| Tubificidae | 6 | - |
| Total | 380 |  |
| HBI |  | 5.467 |

Table B6.  E. Br. of DeNevue Cr. Site ED5 (above Rhinehardt Rd.) macroinvertebrate data from sample collected October 9, 2008.

Table B7.  W. Br. of DeNevue Cr. Site WD3 (above Rhinehardt Rd.) macroinvertebrate data from sample collected May 5, 2008.

| Taxa | # Counted | HBI Value |
| --- | --- | --- |
| Coleoptera |  |  |
| Elmidae |  |  |
| Dubiraphia sp | 6 | 6 |
| Optioservus sp | 8 | 4 |
| Optioservus fastiditus |  | 4 |
| Diptera |  |  |
| Ceratopogonidae |  |  |
| Mallochohelea sp | 1 | - |
| Chironomidae larvae |  | - |
| Chironomini |  | - |
| Glyptotendipes sp | 1 | 10 |
| Polypedilum (Polypdelum) illioense group | 1 | 6 |
| Polypedilum (Tripodura) halterale group | 1 | 3 |
| Orthocladiinae pupae | 1 | - |
| Cricoptopus (Cricotopus) pupae | 1 | - |
| Eukiefferiella sp | 1 | 8 |
| Eukiefferiella (Claripennis) group | 17 | 8 |
| Eukiefferiella (Claripennis) group pupae | 4 | - |
| Hydrobaenus sp | 5 | 8 |
| Hydrobaenus pupae | 4 | - |
| Orthocladius (Orthocladius) sp | 26 | 6 |
| Orthocldiius pupae | 1 | - |
| Parametriocnemus sp | 1 | 5 |
| Tanypodinae |  |  |
| Conchapelopia sp | 3 | 6 |
| Simuliidae |  |  |
| Cnephia ornithophila | 5 | - |
| Fibrinflatum sp | 1 | 6 |
| Prosimulium multidentatum | 1 | - |
| Simulium verecundum “complex” | 21 | 6 |
| Tabanidae |  |  |
| Chrysops sp | 1 | 6 |
| Heteroptera |  |  |
| Corixidae |  |  |
| Sigara grossolineata | 2 | - |
| Plecoptera |  |  |
| Perlodidae |  |  |
| Isoperla nana | 2 | 5 |
| Amphipoda |  |  |
| Gammaridae |  |  |
| Gammarus pseudolimnaeus | 16 | 4 |
| Gastropoda |  |  |
| Physidae |  |  |
| Sphaerium sp | 2 | - |
| Isopoda |  |  |
| Asellidae |  |  |
| Caecidotea intermedia | 6 | 8 |
| Oligochaeta |  |  |
| Tubificidae | 5 | - |
| Pelecypoda |  |  |
| Sphaeriidae |  |  |
| Sphaerium sp | 2 | - |
| Total | 155 |  |
| Biotic Index |  | 5.992 |

Table B8.  DeNevue Cr. Site D1 (above 4th St.) macroinvertebrate data from sample collected May 5, 2008.

| Taxa | # Counted | HBI Value |
| --- | --- | --- |
| Coleoptera |  |  |
| Elmidae |  |  |
| Optioservus sp | 8 | 4 |
| Optioservus fastiditus | 2 | 4 |
| Stenelmis sp | 10 | 5 |
| Diptera |  |  |
| Chironomidae |  |  |
| Chironomini |  |  |
| Paratendipes sp | 11 | 8 |
| Polypedilum (Polypdelum) illioense group | 1 | 6 |
| Polypedilum (Uresipedilum) aviceps | 3 | 5 |
| Daimesinae |  |  |
| Diamesa sp | 1 | 5 |
| Orthocladiinae |  |  |
| Brillia flavifrons group | 1 | 5 |
| Cricotopus (Cricotopus) pupae | 5 | - |
| Cricotopus (Cricotopus) bicinctus | 2 | 6 |
| Eukiefferiella (Claripennis) group | 1 | 8 |
| Hydrobaenus sp | 1 | 8 |
| Nanocladius (Nanocladius) spiniplenus | 1 | 3 |
| Orthocladiius pupae | 2 | - |
| Orthocladius (Orthocladius) sp | 44 | 6 |
| Parametriocnemus sp | 4 | 5 |
| Tanypodinae |  |  |
| Nilotanypus fimbriatus | 1 | 6 |
| Simuliidae |  |  |
| Simulium sp | 1 | - |
| Simulium verecundum “complex” | 4 | 6 |
| Simulium fibrinflatum | 13 | 6 |
| Ephemeroptera |  |  |
| Baetidae |  |  |
| Baetis brunneicolor | 1 | 4 |
| Plecoptera |  |  |
| Capniidae |  |  |
| Allocapnia sp | 1 | 3 |
| Tricoptera |  |  |
| Hydropsychidae |  |  |
| Cheumatopsyche sp | 2 | 5 |
| Polycentropodidae |  |  |
| Polycentropus sp | 1 | 6 |
| Amphipoda |  |  |
| Gammaridae |  |  |
| Gammarus pseudolimnaeus | 5 | 4 |
| Oligochaeta |  |  |
| Naididae | 5 | - |
| Tubificidae | 5 | - |
| Total | 142 |  |
| Biotic Index |  | 5.720 |

APPENDIX C

DENEVUE SITE D1 2008 MONTHLY CHEMISTRY DATA and EDEN WWTF TP

APPENDIX D

2009 CHEMISTRY AND FLOW SAMPLES

# Text boxes

East Branch of De Nevue Cr. (Site ED4 looking downstream toward the Mill Rd. Bridge.

Photo 1.  PVC canister and  temperature probe.  The probes were placed in the canisters to protect them.   The slots in the PVC were to allow flow through.  Photo taken by Al Neibur.

Photo 2.  E. Br. of De Nevue Cr. looking upstream toward the wooden bridge between Lakeside Foods lagoons and Eden WWTF.  (Oct. 9, 2002)

Photo 4.  E. Br. to De Nevue Cr. looking downstream from near the Eden WWTF.  The WWTF effluent entered the Cr. to the right center of the photo.  Oct. 9, 2002.

Photo 3.  Eden WWTF outfall with TF in background.  Note the watercress at base of concrete outfall indicating spring inputs.  May 2004.

Photo 6.  E. Br. of DeNevue Cr. above Lime Rd. looking upstream past dam and impoundment.  Photo Oct. 9, 2002.

Photo 7.  E. Br. of DeNevue Cr. above Lime Rd. below dam looking upstream.  The fox farm spring fed pond entered from the left of the lower part of the photo.  Oct. 9, 2002.

Photo 10.  E. Br. to DeNevue Cr. Site ED5 looking upstream above Rhinehardt Rd.  Oct. 9, 2002.

Photo 8.  Fish sampling Site ED3 on the E. Br. of DeNevue Cr. below Lime Rd. Aug. 12, 2004..

Photo 5.  Measuring flow at Site ED2 on the E. Br. of De Nevue Cr. below the Eden WWTF.  Aug. 12, 2004.

Figure 1d

De Nevue Cr.

Lake Winnebago