INVESTIGATION OF AN AREA OF CONTAMINATED SEDIMENT

IN RIB LAKE, TAYLOR COUNTY

December  2008

Craig Roesler – WI DNR

Background

Lake sediment core collection in 2006 found a buried layer of black sediment near the mouth of “Tannery Creek”, an unnamed stream on the north side of Rib Lake.  The black sediment layer contained animal hair and had a strong oil-like odor.  Rib Lake is a shallow 324 acre lake.  Past sediment surveys of the lake found soft sediment depths of up to 40 feet.  The lake received waste materials from a tannery and a sawmill The tannery operated from 1892 – 1923.  The sawmill operated from 1881 – 1948.    Waste materials such as hair, bark fragments, charcoal, and logs are present in the lake sediment.  Other than sunken logs, these waste materials are generally present in only the top 3 feet of sediment, indicating most sediment in the lake has been naturally deposited.

Past Rib Lake sediment analyses found high levels of mercury in surficial sediment (1.5 mg/kg in top 0-4”).  Arsenic, copper, and zinc concentrations are also somewhat high.  The source of these elevated metal concentrations has been undetermined.  Past information suggested the old tannery was using a bark tanning process only and was unlikely to be the source.

Methods

Sediment cores were collected from 28 sites (figure 1) near the mouth of Tannery Creek to document the extent of the buried layer of black sediment.  Cores were collected through the ice on March 19th and 21st 2008.  A 2”(?) diameter acrylic tube with a sliding piston was used.  Each core was extruded from the sampling tube and the thickness and characteristics of the sediment layers were recorded.  Sediment layers being tested were homogenized in a stainless steel bowl and transferred to zip-lock polyethylene bags and glass jars with Teflon-lined lids provided by the Wisconsin State Lab of Hygiene.  The samples were placed in coolers on ice, and were later refrigerated prior to being shipped in iced coolers to the State lab for testing.

The darkened layer from site 12 was partitioned into 2 layers (1.0-2.1, 2.1-3.4 ft) for separate analyses.  Composite samples from 3 sites each were used to test the black layer from locations where it was 1 ft thick and 0.5 ft thick.

GPS coordinates of core sites were measured in the field, and later plotted on maps.  The boundary of the contaminated area, and a 1 ft thick black layer isobar were plotted by interpolation and extrapolation from measured sites.

Results

The measured thickness of the black layer at the core sites is shown in figure 2.  The maximum thickness found was 2.4 ft.  The boundary of the contaminated area and the 1 ft thick isobar is shown in figure 3.  The total contaminated area is 2.3 acres.  The contaminated area with a black layer thickness >1 ft is 0.48 acres.  The total volume of contaminated sediment is 2,320 yd3.

Figure 4 shows the thickness of the overlying “clean” sediment at the core sites.  The thickness of the clean layer ranges from 1.0 to 2.6 ft, and averages 1.45 ft.  The volume of overlying clean sediment is 5,447 yd3.  The total volume of both the clean sediment and the black layer is 7,767 yd3.

The overlying clean sediment is a medium brown color, and composed of very fine to coarse particulates.  Wood chips are often present (table 3).

The contaminated layer is black and consistently contains animal hair.  It has an oil-like odor and a faint bluish sheen can be seen on the surfaces of extracted samples.

Test results for the contaminated layer samples are shown in tables 1 and 2.  Results from previous Rib Lake sediment samples and Consensus Based Sediment Quality Guidelines (CBSQG’s) are also shown for comparison.  CBSQ’s are based on toxicity to sediment dwelling organisms.  While these organisms are typically restricted to the upper 4-6 inches of sediment, applying these guidelines to deeper sediment still provides some perspective of the significance of the contaminant concentrations.

Inorganic test results (table 1) show mercury concentrations are very high, ranging from 2.8 to 10.7 mg/kg.  These are far in excess of CBSQG probable effects concentration (1.1 mg/kg).  Concentrations of arsenic (33-80 mg/kg) and copper (202-234 mg/kg) also exceed CBSQ probable effects concentrations.  Zinc concentrations (159-205 mg/kg) are moderately high, but only exceed the CBSQ threshold effects concentration.

The concentrations of all 4 metals in the contaminated layer samples are substantially higher than in the 1998 open lake sediment samples.  This fact in combination with the consistent presence of animal hair in the contaminated layer samples indicates past tannery discharges are the primary source of the elevated metals concentrations in the lake sediment.

Organic test results (table 2) show the petroleum product present in the contaminated layer is motor oil.  Oil is used in finishing leather.  Tannery leather is reported to have a 16-19% oil content.  The consistent presence of animal hair with the oil also indicates the tannery was the source.

PCB’s were not detected.  They were not in use at the time of tannery operation.  Total organic carbon ranged from 18.9-26.6%.  Several PAH compounds were present in the samples.  None of them exceeded CBSQ’s threshold effects concentrations (at 1% total organic carbon).  PAH concentrations in the 1998 open lake sediment samples at some sites were higher than those found in the contaminated layer samples.  The PAH compounds found also vary somewhat between the two sets of samples.  This suggests additional PAH sources have affected the open lake sediment.

Considerations for the Future

If undisturbed, there is probably little movement of mercury, arsenic, copper and zinc out of the contaminated layer.  It is currently capped with 1 ft or more of cleaner sediment.  Overlying water depth is about 3-6 ft.  Some disturbance by outboard motors and boat anchors may occur.  An extreme windstorm could conceivably cause resuspension of the contaminants.  If the lake level became lower, (the outlet dam has a 1 ft head) the potential for wind-induced resuspension would probably increase.  Any sediment disturbing activities in the area should be avoided.

The most desirable solution would be the removal of the contaminated material.  However, the cost of removal may be prohibitive.  A total of about 7,767 yd3 of material would need to be removed.  There is some woody debris buried in the sediment, especially closest to the creek mouth, which might complicate sediment removal.

Potential funding sources for dredging are limited.  DNR has an Environmental Damage Compensation Fund that might be a potential funding source for sediment removal.  The amount of money in this fund varies from year to year.  The DNR Upper Chippewa Basin Water Leader, Tom Aartila could be contacted to inquire about this funding source.

The ATC Environmental Impact Fund is a potential funding source that Taylor County has.  Arlen Albrecht with the Taylor Co. UW-Extension program can be contacted to inquire about this funding source.

Dredging costs can be highly variable and will depend on the contaminant concentrations of the mixed dredge spoils, the distance to a disposal site, and the method of dredging.  Further evaluation of these variables would be needed to obtain a cost estimate.

| TABLE 1. RIB LAKE SEDIMENT SAMPLE INORGANIC RESULTS |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- |
| MARCH 21, 2008 SAMPLES FROM NEAR MOUTH OF "TANNERY" CREEK |  |  |  |  |
| (RESULTS IN MG/KG DRY WT) |  |  |  |  |  |  |  |  |
|  |  |  |  |  |  | 1998 |  |  |  |  |
|  |  |  |  |  |  | RIB LAKE |  |  |  |  |
|  | SITE 12 | SITE 12 | COMPOSITE* | COMPOSITE* |  | 4 SITE |  |  |  |  |
|  | 1.0-2.1 FT | 2.1-3.4 FT | 0.5 FT THICK | 1.0 FT THICK |  | 0-42 INCH |  |  | CBSQG** |  |
| PARAMETER | LAYER | LAYER | LAYER | LAYER |  | LAYER |  | TEC'S | MEC'S | PEC'S |
| Mercury | 5.4 | 10.7 | 5.2 | 2.8 |  | 0.06 - 0.36 |  | 0.18 | 0.64 | 1.1 |
| Arsenic | 37 | 80 | 63 | 33 |  | 14 - 30 |  | 9.8 | 21.4 | 33 |
| Copper | 211 | 202 | 234 | 226 |  | 25 - 41 |  | 32 | 91 | 150 |
| Zinc | 191 | 159 | 205 | 189 |  | 94 - 136 |  | 120 | 290 | 460 |
|  | *3 site composites of black layer underlying >1 ft. of "clean" brown sediment |  |  |
|  | **Consensus based sediment quality guidelines probable effects concentrations |  |  |
|  | TEC = threshold effects concentration, MEC = midpoint effects concentration, |  |  |
|  | PEC = probable effects concentration |  |  |  |  |  |  |

| TABLE 2. RIB LAKE SEDIMENT SAMPLE ORGANIC RESULTS |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| MARCH 21, 2008 SAMPLES FROM NEAR MOUTH OF "TANNERY" CREEK |  |  |  |  |  |  |
| (RESULTS IN NG/G DRY WT, EXCEPT TOC AND SOLIDS IN %) |  |  |  |  |  |  |
|  |  |  |  |  |  | 1998 |  |  |  |  |
|  |  |  |  |  |  | RIB LAKE |  |  |  |  |
|  | SITE 12 | SITE 12 | COMPOSITE* | COMPOSITE* |  | 4 SITE |  |  |  |  |
|  | 1.0-2.1 FT | 2.1-3.4 FT | 0.5 FT THICK | 1.0 FT THICK |  | 0-42 INCH |  |  |  |  |
| PARAMETER | LAYER | LAYER | LAYER | LAYER |  | LAYER |  |  |  |  |
| PCB | no detect | not tested | not tested | not tested |  | no detect |  |  |  |  |
| total organic carbon | 21.8% | 18.9% | 21.4% | 26.6% |  | 22 - 25% |  |  |  |  |
| solids | 17.0% | 13.0% | 11.0% | 13.0% |  | 5 - 6.4% |  |  |  |  |
|  |  |  |  |  |  |  |  |  | CBSQG** |  |
| PAH compound |  |  |  |  |  |  |  | TEC'S | MEC'S | PEC'S |
| 2-methylnapthalene | 72 | 59 | 100 | 82 |  | not tested |  | 20.2 | 111 | 201 |
| acenapthene | no detect | no detect | no detect | no detect |  | n.d. - 560 |  | 6.7 | 48 | 89 |
| acenapthylene | no detect | no detect | 180 | no detect |  | n.d. - 1500 |  | 5.9 | 67 | 128 |
| anthracene | 180 | 95 | 130 | 110 |  | n.d. - 450 |  | 57.2 | 451 | 845 |
| benzo (a) anthracene | 690 | 700 | 170 | no detect |  | no detect |  | 108 | 579 | 1050 |
| benzo (a) pyrene | 990 | no detect | no detect | 430 |  | no detect |  | 150 | 800 | 1450 |
| benzo (b) fluoranthene | 220 | no detect | no detect | no detect |  | no detect |  | 240 | 6820 | 13400 |
| chrysene | 1600 | no detect | 550 | no detect |  | no detect |  | 166 | 728 | 1290 |
| fluoranthene | no detect | no detect | no detect | no detect |  | 310 - 1800 |  | 423 | 1327 | 2230 |
| fluorene | no detect | no detect | no detect | no detect |  | n.d. - 390 |  | 77.4 | 307 | 536 |
| napthalene | 140 | 180 | 770 | 240 |  | no detect |  | 176 | 369 | 561 |
| phenanthrene | 860 | 560 | 720 | 670 |  | 500 - 3200 |  | 204 | 687 | 1170 |
| pyrene | 1800 | 870 | 930 | 1100 |  | n.d. - 2600 |  | 195 | 858 | 1520 |
| perylene | not tested | not tested | not tested | not tested |  | n.d. - 880 |  | none | none | none |
| petroleum product | motor oil | not tested | not tested | not tested |  | not tested |  |  |  |  |
|  | *3 site composites of black layer underlying > 1 ft. of "clean" brown sediment |  |  |
|  | ** Consensus based sediment quality guidelines at 1% total organic carbon |  |  |
|  | TEC = threshold effects concentration, MEC = midpoint effects concentration, |  |  |
|  | PEC = probable effects concentration |  |  |  |  |  |  |  |

| TABLE 3. RIB LAKE SEDIMENT CORE SITE DATA, MARCH 19th AND 21st 2008 |
| --- |
|  |  |  |  | BLACK | BLACK |  |  |
|  |  |  | WATER | LAYER | LAYER |  |  |
|  |  |  | DEPTH | THICKNESS | DEPTH |  |  |
| NO. | LAT | LONG | (feet) | (feet) | (feet) | COMMENTS | OTHER LAYERS |
| 0 | 45.31877 | 90.19977 | 2.1 | 0 | 0 | no oil top 2', woody, hard to core | 0-2.0 brown (core end) |
| 1 | 45.31862 | 90.19975 | 2.8 | 0 | 0 | no oil top 1.5', woody, hard to core | 0-1.5 brown (core end) |
| 2 | 45.31852 | 90.19975 | 3.2 | 1.5 plus | 1 | woody, core stopped at 2.5' | 0-1 brown, coarse particulates |
|  |  |  |  |  |  |  | 1-2.5 black, oil odor, hair (core end) |
| 3 | 45.31822 | 90.19967 | 4.8 | 0.7 | 1.7 |  | 0-0.7 brown, coarse organics |
|  |  |  |  |  |  |  | 0.7-1.7 brown, fine |
|  |  |  |  |  |  |  | 1.7-2.4 black, oil odor, hair |
|  |  |  |  |  |  |  | 2.4-3.7 brown, smooth |
| 4 | 45.31812 | 90.19971 | 5.7 | 0.2 | 1.5 |  | 0-1.5 brown, med. particulates |
|  |  |  |  |  |  |  | 1.5-1.7 black, oil odor, hair |
|  |  |  |  |  |  |  | 1.7-3.8 brown, smooth |
| 5 | 45.3182 | 90.19994 | 4 | 1.4 | 1.7 |  | 0-1.7 brown, med. particulates |
|  |  |  |  |  |  |  | 1.7-3.1 black, oil odor, hair |
|  |  |  |  |  |  |  | 3.1-5.0 brown, smooth |
| 6 | 45.31835 | 90.20027 | 3.9 | 0.4 | 2 |  | 2-2.4 black, oil odor hair |
| 7 | 45.31822 | 90.20035 | 3.9 | 0 | 0 | no oil top 2', abundant wood chips | 0-2.0 brown, abundant wood chips (core end) |
| 8 | 45.31834 | 90.19926 | 5.2 | 0 | 0 | 3' core was clean | 0-3.0 brown |
| 9 | 45.31856 | 90.1995 | 3.3 | 0.6 plus? | 2 | dense hair prevented deeper core | 0-2.0 brown |
|  |  |  |  |  |  |  | 2-2.6 black, oil odor, hair (core end) |
| 10 | 45.31858 | 90.19904 | 5.8 | 0.1 | 1 | some hair, not black | 0-1.0 brown |
|  |  |  |  |  |  |  | 1.0-1.1 dark brown, some hair |
|  |  |  |  |  |  |  | 1.1-3.0 brown, smooth |
| 11 | 45.31886 | 90.19901 | 5.2 | 0.5 | 1 | part of 0.5' composite | 0-1.0 brown, fine particulates |
|  |  |  |  |  |  |  | 1.0-1.5 black, oil odor, hair |
|  |  |  |  |  |  |  | 1.5-4.0 brown, smooth |
| 12 | 45.31844 | 90.19978 | 3.9 | 2.4 | 1 | layers sampled, 1-2.1, 2.1-3.4 | 0-1.0 brown, coarse particulates |
|  |  |  |  |  |  |  | 1.0-2.1 black, oil odor, hair |
|  |  |  |  |  |  |  | 2.1-3.4 very dk brown, some hair, some oil odor |
|  |  |  |  |  |  |  | 3.4-4.5 med to dk brown, smooth |
| 13 | 45.31828 | 90.19986 | 4.6 | 1.1 | 1 | part of 1' composite | 0-1.0 brown, med particulates |
|  |  |  |  |  |  |  | 1.0-2.1 black, oil odor, hair |
|  |  |  |  |  |  |  | 2.1-3.8 brown, smooth |
| 14 | 45.31838 | 90.19965 | 4.8 | 0.9 | 1 | part of 1' composite | 0-1.0 brown, med particulates |
|  |  |  |  |  |  |  | 1.0-1.9 black, oil odor, hair |
|  |  |  |  |  |  |  | 1.9-3.9 brown, smooth |
| 15 | 45.31868 | 90.19932 | 4.1 | 1.6 | 1.5 |  | 0-0.7 brown with wood chips |
|  |  |  |  |  |  |  | 0.7-1.5 brown, smooth |
|  |  |  |  |  |  |  | 1.5-3.1 black, oil odor, hair |
|  |  |  |  |  |  |  | 3.1-3.8 dk brown, smooth |
| 16 | 45.31878 | 90.1991 | 5.1 | 1 | 1 | part of 1' composite | 0-1.0 brown |
|  |  |  |  |  |  |  | 1.0-2.0 black, oil odor, hair |
|  |  |  |  |  |  |  | 2.0-3.7 brown, smooth |
| 17 | 45.31818 | 90.19967 | 5.5 | 0.6 | 1.8 | part of 0.5' composite | 0-1.8 brown, some wood chips |
|  |  |  |  |  |  |  | 1.8-2.4 black, oil odor, hair |
|  |  |  |  |  |  |  | 2.4-3.7 brown, smooth |
| 18 | 45.31834 | 90.20016 | 4.1 | 0.6 | 1.7 | part of 0.5' composite | 0-1.7 brown with wood chips |
|  |  |  |  |  |  |  | 1.7-2.3 black, oil odor, hair |
|  |  |  |  |  |  |  | 2.3-4.1 dk to med brown, smooth |
| 19 | 45.31821 | 90.20006 | 4.7 | 0.4 | 1.9 |  | 0-1.9 brown with wood chips |
|  |  |  |  |  |  |  | 1.9-2.3 black, oil odor, hair |
|  |  |  |  |  |  |  | 2.3-4.3 dk to med brown, smooth |
| 20 | 45.3181 | 90.20007 | 4.5 | 0.1 | 2.6 |  | 0-2.6 brown with wood chips |
|  |  |  |  |  |  |  | 2.6-2.7 trace of black, oil odor, hair |
|  |  |  |  |  |  |  | 2.7-4.3 brown, smooth |
| 21 | 45.31841 | 90.19934 | 4.1 | 0.3 | 1.8 |  | 0-1.8 brown, some wood chips |
|  |  |  |  |  |  |  | 1.8-2.1 black, oil odor, hair |
|  |  |  |  |  |  |  | 2.1-4.3 brown, smooth |
| 22 | 45.3185 | 90.19938 | 4.5 | 1.3 | 1.3 |  | 0-1.3 brown with coarse particulates |
|  |  |  |  |  |  |  | 1.3-2.6 black, oil odor, hair |
|  |  |  |  |  |  |  | 2.6- 4.5 dk to med brown, smooth |
| 23 | 45.31894 | 90.19884 | 5.9 | 0.3 | 1.4 |  | 0-1.4 brown, smooth |
|  |  |  |  |  |  |  | 1.4-1.7 black, oil odor, hair |
|  |  |  |  |  |  |  | 1.7-3.9 brown, smooth |
| 24 | 45.31897 | 90.19868 | 5.9 | 0.4 | 1.1 |  | 0-1.1 brown, smooth |
|  |  |  |  |  |  |  | 1.1-1.5 black, oil odor, hair |
|  |  |  |  |  |  |  | 1.5-3.5 brown, smooth |
| 25 | 45.3192 | 90.19827 | 5.8 | 0.1 | 1.4 |  | 0-1.4 brown, smooth |
|  |  |  |  |  |  |  | 1.4-1.5 black, oil odor, hair |
|  |  |  |  |  |  |  | 1.5-4.3 brown, smooth |
| 26 | 45.31877 | 90.19859 | 6 | 0 | 0 |  | 0-3.4 brown, smooth |
| 27 | 45.31884 | 90.19926 | 3.7 | 0? | 0? |  | 0-1.0 brown, abund. wood chips, hair at bottom |
|  |  |  |  |  |  |  | no oil observed (core end) |
| 28 | 45.31899 | 90.19991 | 3.1 | 0 | 0 | creek channel 75' below bridge | 0-3.0 brown with plant fragments |

# Text boxes

FIG. 1  RIB LAKE SEDIMENT CORE LOCATIONS

For scale, site 7 to 25 is 648 feet

FIG. 2  THICKNESS (FT) OF CONTAMINATED LAYER (IN RED)

For scale, site 7 to 25 is 648 feet