| 2010 Impaired Waters Documentation Sheet |
| --- |
| Author: Jean Unmuth | Date Prepared: October 2, 2009 |
| Waterbody Name: Little Bear Creek | Watershed Code and Name: LW14 Bear Creek |
| WADRS ID: 18505 | WBIC: 1234700 | If you don’t know the ID numbers, go to i-SWDV (CRTL + Click) to find them. |
| Choose from the following to indicate what you are recommending: |
| __X___ Proposed new listing |
| _____ Proposed changes for water already on 303(d) list (check type of change below) ( TMDL ID Number: _______ |
|  | _____ Proposed change to existing list (new pollutants, impairments, mileages, etc.) |
|  | _____ Proposed for de-listing ( a report may be needed depending on the reasons) |
|  | _____ General 303d documentation for water already on list |
| Description of waterbody segment |
| Start Mile: ____0________ End Mile: 6.66 (Approximated) Total miles: _____6.66_______ Lake Acres: ____________ | Detail (describe segment using road crossings, convergence with other waterbodies, etc.): From the mouth of Little Bear Creek upstream to the junction of an unnamed tributary WBIC: 5033157, located East of Little Bear Road. See attached map for start and end locations. |
| Use Designation Categories | List use designation & data source for each category. |
| Current (Existing) Fish & Aquatic Life Use: (Aquatic Community) | FAL |
| Attainable (Potential) Fish & Aquatic Life Use: (Aquatic Community) | Cold |
| Designated (Codified) Fish & Aquatic Life Use: | Default |
| Is it supporting its Attainable Use? _____ Fully supporting ___X__ Partially supporting _____ Not supporting Does a Specific Fish Advisory Exist? (This is different from the statewide mercury advisory.) ___ Yes __X__ No ___ Don’t know If so, what is the specific advisory: |
| Pollutants & Impairments Pollutants (Place an X next to all pollutants that you are recommending for listing, de-listing or monitoring needs. If you are recommending adding a new pollutant to a waterbody that is already on the list, write ADD.) |
| ___X__ Phosphorus | _X____ Sediment | _____ Bacteria | _____ PAHs | _____ PCBs |
| _____ NH3 (Ammonia) | ___X__ Thermal (elevated temp.) | _____ Hg | _____ Creosote | _____ Metals |
| Other Pollutants: |
| Impairments (Place an X next to all impairments that you are recommending for listing, delisting, or monitoring needs. If you are recommending adding a new pollutant to a waterbody that is already on the list, write ADD. ) |
| __X___ Degraded Habitat | __X___ Eutrophication | ___X__ Temperature |
| _____ Contaminated Fish Tissue | _____ Chronic Toxicity | _____ Aquatic Toxicity |
| _____ Low Dissolved Oxygen | _____ Aquatic Invasives |  |
| Other Impairments: |
| Source of impairment (Place an X next to the source category.) if you need an explanation of source categories., see http://dnr.wi.gov/org/water/wm/wqs/303d/categories.html . |
| __X___ NPS Dominated | _____ NPS/Pt. Source Blend | _____ Point Source |
| _____ Contaminated Sediment | _____ Atmospheric Deposition | __X__ Physical Habitat |
| _____ Unknown | Other: _____________________________ |
| Specific causes of impairment (Describe to the best of your ability what you think is contributing to the impairment.) Stream was historically ditched and moved out of the original bed (channelized), starting approximately 2 miles downstream from the headwaters, for approximately ½ of it’s stream length or about 4 miles total channelized. Agricultural use, mainly crops in upper ½ along the stream is heavy, with very little to no vegetative buffers. Grazing may not contribute greatly to impairment, but large concentrated animal feeding operations exist close to the stream, and one specifically has been problematic due to an overflow of manure storage tank to a wetland area bordering the stream. |
| Information is based on: Monitoring data (specific data) less than 5 years old (Circle One) YES NO |
| Map When possible, please create a map of your waterbody and submit it with this form. It is easy to create a 8.5 x 11 map of the area you are describing. Go to the go to the Intranet Surface Water Viewer i-SWDV (CRTL + Click). Choose “Find Location” to find the waterbody, then “Layers” to choose “Standards, Monitoring and Assessment”. If it is already on the 303(d) list, then click “Impaired Waters 303d". If you want to show the monitoring stations, also click on "SWIMS Station Points". Then choose “Print” (this will create a pdf map), add a title under "Map Title" and your name and date under “Map Notes", click "OK" and then "Open Map" at the next screen. Save the file and attach it when you send in this sheet. For additional help on how to make a map, check out page 12-14 on the website http://www.dnr.state.wi.us/org/water/SWDV/help/documents/SWDV_Basic_User_Guide_%209_07.pdf |
| Monitoring & Listing Data 1. Monitoring Study, Date, Results. List water quality exceedences indicating magnitude, duration and frequency. Stations: 10021319 Parameters: Unmuth monitoring: 2007 and 2008 Fish IBI both poor, 2007 MIBI poor /HIBI good (some organic pollution), 2008 Transparency poor. USGS 2008 Total Phosphorus samples where 5 of 6 samples taken over a 6 month period exceeded 0.075 mg/l. Database where data is stored (Fish Database, SWIMS, FishSED, Personal PC): Fish Database, SWIMS, Personal PC |
| 2. Monitoring Study, Date, Results. List water quality exceedences indicating magnitude, duration and frequency. Stations: 10021057 Parameters: 2007 Temperature 11% of 17 mean daily samples taken in June and August exceeded 73 F(22.7 C). 2007 & 2008 Fish IBI’s Very Poor and Poor. 2008 Habitat rank Fair (40). Database where data is stored (Fish Database, SWIMS, FishSED, Personal PC): Fish Database, SWIMS, Personal PC |
| 3. Monitoring Study, Date, Results. List water quality exceedences indicating magnitude, duration and frequency. Stations: Parameters: Database where data is stored (Fish Database, SWIMS, FishSED, Personal PC): |
| Narrative on why you are proposing this waterbody to be listed or delisted? The stream has good permanent flow from large springs in the upper watershed. There are deep enough runs in some segments to support cold water game fishes. Stream ditching, channelization, and moving the stream out of the original banks has likely increased sediment problems in areas of flat topography where silt settles out. Much of the riparian corridor is either cropped or pastured, with large dairy operations close to the stream, and grazing in wetland areas all along the stream corridor. Lack of fish holding habitat, lack of instream habitat, and lack of riffle/pool/runs from stream channelization. Also, some wetlands drained through ditching, also contributing sediment, and phosphorus from agricultural lands. |
| List and Attach any additional reports, updated watershed tables, analyses etc. including use designation survey. 1. 2. 3. 4. 5. |