| 2010 Impaired Waters Documentation Sheet |
| --- |
| Author: Craig Roesler, Tom Aartila, Kristi Minahan | Date Prepared: 10-28-2009 |
| Waterbody Name: Lac Courte Oreilles (including Musky Bay) | Watershed Code and Name: UC20 Couderay River |
| WADRS ID: 15368 | WBIC: 2390800 | If you don’t know the ID numbers, go to i-SWDV (CRTL + Click) to find them. |
| Choose from the following to indicate what you are recommending: |
| _____ Proposed new listing |
| __X__ Reviewed but not proposed for listing |
| _____ Proposed changes for water already on 303(d) list (check type of change below) ( TMDL ID Number: _______ |
|  | _____ Proposed change to existing list (new pollutants, impairments, mileages, etc.) |
|  | _____ Proposed for de-listing ( a report may be needed depending on the reasons) |
|  | _____ General 303d documentation for water already on list |
| Description of waterbody segment |
| Start Mile: ____________ End Mile: ____________ Total miles: ____________ Lake Acres: ___5039_________ | Detail (describe segment using road crossings, convergence with other waterbodies, etc.): Lac Courte Oreille is a large, deep, mesotrophic (near oligotrophic) lake. Musky Bay is a somewhat isolated bay at the southwest end of Lac Courte Oreille. |
| Use Designation Categories | List use designation & data source for each category. |
| Current (Existing) Fish & Aquatic Life Use: (Aquatic Community) | Deep Lowland |
| Attainable (Potential) Fish & Aquatic Life Use: (Aquatic Community) | Deep Lowland |
| Designated (Codified) Fish & Aquatic Life Use: | Default |
| Is it supporting its Attainable Use? ___X*__ Fully supporting _____ Supporting _____ Not supporting (*Lac Courte Oreille is ‘Fully Supporting’ FAL uses; Musky Bay is probably ‘Supporting’ FAL uses) Does a Specific Fish Advisory Exist? (This is different from the statewide mercury advisory.) ___ Yes __X__ No ___ Don’t know If so, what is the specific advisory: |
| Pollutants & Impairments Pollutants (Place an X next to all pollutants that you are recommending for listing, de-listing or monitoring needs. If you are recommending adding a new pollutant to a waterbody that is already on the list, write ADD.) |
| _____ Phosphorus | _____ Sediment | _____ Bacteria | _____ PAHs | _____ PCBs |
| _____ NH3 (Ammonia) | _____ Thermal (elevated temp.) | _____ Hg | _____ Creosote | _____ Metals |
| Other Pollutants: |
| Impairments (Place an X next to all impairments that you are recommending for listing, delisting, or monitoring needs. If you are recommending adding a new pollutant to a waterbody that is already on the list, write ADD. ) |
| _____ Degraded Habitat | _____ Eutrophication | _____ Temperature |
| _____ Contaminated Fish Tissue | _____ Chronic Toxicity | _____ Aquatic Toxicity |
| _____ Low Dissolved Oxygen | _____ Aquatic Invasives |  |
| Other Impairments: |
| Source of impairment (Place an X next to the source category.) if you need an explanation of source categories., see http://dnr.wi.gov/org/water/wm/wqs/303d/categories.html . |
| _____ NPS Dominated | _____ NPS/Pt. Source Blend | _____ Point Source |
| _____ Contaminated Sediment | _____ Atmospheric Deposition | _____ Physical Habitat |
| _____ Unknown | Other: _____________________________ |
| Specific causes of impairment (Describe to the best of your ability what you think is contributing to the impairment.) |
| Information is based on: Monitoring data (specific data) less than 5 years old (Circle One) YES NO |
| Map When possible, please create a map of your waterbody and submit it with this form. It is easy to create a 8.5 x 11 map of the area you are describing. Go to the go to the Intranet Surface Water Viewer i-SWDV (CRTL + Click). Choose “Find Location” to find the waterbody, then “Layers” to choose “Standards, Monitoring and Assessment”. If it is already on the 303(d) list, then click “Impaired Waters 303d". If you want to show the monitoring stations, also click on "SWIMS Station Points". Then choose “Print” (this will create a pdf map), add a title under "Map Title" and your name and date under “Map Notes", click "OK" and then "Open Map" at the next screen. Save the file and attach it when you send in this sheet. For additional help on how to make a map, check out page 12-14 on the website http://www.dnr.state.wi.us/org/water/SWDV/help/documents/SWDV_Basic_User_Guide_%209_07.pdf |
| Monitoring & Listing Data 1. Monitoring Study, Date, Results. List water quality exceedences indicating magnitude, duration and frequency. Stations: 583046 (Deep Hole) Parameters: Average TSI based on chlorophyll a is 41, which places Lac Courte Oreilles in the Excellent category for Deep Lowland Lakes. Average Total Phosphorus from 2004-2008 is .013 mg/l, which does not exceed the impairment threshold of .03 for Deep Lowland Lakes. Database where data is stored (Fish Database, SWIMS, FishSED, Personal PC): SWIMS |
| 2. Monitoring Study, Date, Results. List water quality exceedences indicating magnitude, duration and frequency. Data provided by the Courte Oreilles Lakes Association, Alf Sivertson, President Stations: Musky Bay MB-1 (deep spot in bay) Parameters: Total Phosphorus data were reviewed from Musky Bay from 2000-2005; the annual mean TP values calculated using DNR methodology are attached. Because these data are from the Bay only, we are comparing them to the Shallow Lowland Lake category thresholds. The May-Oct average annual TP mean (29 ug/l) for 2000-2005 does not exceed the threshold for Shallow Lowland lakes of 40 ug/l. Sampling was also done from 2006-2008, but individual TP test results for these years were not submitted to the DNR. Alf Sivertson submitted mean summer values (July 15-Sept. 15) from 2006-2008; the three-year mean is 35 ug/l. The May-October means for 2006-2008 are likely to be lower than the summer means, as seen in previous years. Database where data is stored (Fish Database, SWIMS, FishSED, Personal PC): Craig Roesler’s personal files (paper copies) |
| 3. Monitoring Study, Date, Results. List water quality exceedences indicating magnitude, duration and frequency. Stations: Musky Bay Parameters: A plant survey was done in Aug. 2007 (Macrophyte Survey, Musky Bay—Lac Courte Oreille) by Harmony Environmental which indicated that the Floristic Quality Index (FQI) of 35. According to the report, the mean for lakes in the Northern Lakes & Forests ecoregion is 24.3 (higher FQI values indicate better quality). Database where data is stored (Fish Database, SWIMS, FishSED, Personal PC): Craig Roesler’s personal files (paper copy) |
| Narrative on why you are proposing this waterbody to be listed or delisted? DNR does not recommend Lac Courte Oreille or Musky Bay be listed on the Impaired Waters List. For Lac Courte Oreilles, average TSI based on chlorophyll a is 41, which places Lac Courte Oreilles in the Excellent category for Deep Lowland Lakes. Average Total Phosphorus from 2004-2008 is .013 mg/l, which does not exceed the impairment threshold of .03 for Deep Lowland Lakes. For Musky Bay, the May-Oct average annual TP mean (29 ug/l) for 2000-2005 does not exceed the threshold for Shallow Lowland lakes of 40 ug/l. |
| List and Attach any additional reports, updated watershed tables, analyses etc. including use designation survey. 1. 2. |

| Lac Courte Oreille WBIC 2390800 |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- |
| Fieldwork Start | Station ID | Station Name | WBIC | Description | Result | Units | Header/Labslip Depth | Lab Comments |
| 04/26/2004 15:00 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | 0.014 | MG/L | 1 Meters |  |
| 08/31/2004 12:00 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | 0.014 | MG/L | 0 to 2 Meters |
|  |  |  |  | Annual Average | NA (need 3 data points) |  |
| 04/19/2005 10:00 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | ND | MG/L | .5 Meters |  |
| 08/02/2005 12:00 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | 0.013 | MG/L | 1 Meters |  |
| 08/23/2005 11:00 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | 0.009 | MG/L | 1 Meters |  |
| 09/08/2005 9:30 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | 0.013 | MG/L | 1 Meters |  |
| 09/08/2005 9:30 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | 0.013 | MG/L | 1 Meters |  |
| 09/08/2005 9:30 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | 0.013 | MG/L | 1 Meters |  |
|  |  |  |  | Annual Average | 0.0122 |  |  |  |
| 04/18/2006 10:00 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | 0.01 | MG/L |  |  |
| 08/25/2006 12:00 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | 0.015 | MG/L | 1 Meters |  |
| 09/07/2006 8:30 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | *0.014 | MG/L | 1 Meters | SAMPLE RECEIVED WITH ICE MELTED |
| 09/14/2006 9:00 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | 0.014 | MG/L | 1 Meters |  |
|  |  |  |  | Annual Average | 0.013 |  |  |  |
| 05/18/2007 11:00 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | 0.02 | MG/L | 1 Meters |  |
| 07/30/2007 10:30 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | 0.01 | MG/L | 1 Meters |  |
| 08/22/2007 10:00 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | *0.015 | MG/L | 1 Meters | SAMPLE RECEIVED WITH ICE MELTED |
| 09/04/2007 9:30 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | 0.011 | MG/L | 1 Meters |  |
|  |  |  |  | Annual Average | 0.013667 |  |  |  |
| 05/12/2008 13:00 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | 0.014 | MG/L | 0 to 2 Meters |
| 07/29/2008 9:25 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | 0.014 | MG/L | 0 to 2 Meters |
| 08/25/2008 11:15 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | 0.01 | MG/L | 0 to 2 Meters |
| 09/12/2008 10:00 | 583046 | Lac Courte Oreilles - Deep Hole | 2390800 | PHOSPHORUS TOTAL | 0.011 | MG/L | 0 to 2 Meters |
|  |  |  |  | Annual Average | 0.01225 |  |  |  |
|  |  |  |  | Multi-Year Average | 0.012779 | MG/L |  |  |
| Impairment threshold for Deep Lowland Lakes is .03 mg/l. |  |  |  |  |  |
| Lac Courte Oreille does not exceed the impairment threshold. |  |  |  |  |  |

TP Calculations for Musky Bay Deep Hole done by DNR staff using DNR methodology,

based on individual data points received from Courte Oreilles Lakes Association, Alf Sivertson, President

| MUSKY BAY TOTAL P DATA FOR DEEP SITE (MB-1), 2000-2005 |
| --- |
|  | MAY-OCT |  | JULY 15- SEPT 15 |  |
| YEAR | MEAN TP (ug/l) |  | MEAN TP (ug/l) |  |
| 2000 | 24 |  | 24 |  |
| 2001 | 19 |  | 21 |  |
| 2002 | 32 |  | 51* |  |
| 2003 | 27 |  | 49 |  |
| 2004 | 25 |  | 30 |  |
| 2005 | 45 |  | 57** |  |
| MEAN = | 29 |  | 39 |  |
|  |  |  | *Based on only 2 August samples |
|  |  |  | **Based on 3 July samples |